## Slide 1: Program Design and Analysis Chapter 5
COE 306: Introduction to Embedded Systems
Dr. Aiman El-Maleh
Computer Engineering Department
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Next . . .
Embedded Software Components
  State Machines
  Circular Buffers
  Queues
Models of Programs
The Compilation Process

## Slide 3: Embedded Software Components
Embedded code must
  run at a required rate to meet system deadlines,
  fit into the allowed amount of memory,
  meet power consumption requirements
Some of the most common software components in embedded systems are:
  1. State machines: well suited to reactive systems such as user interfaces
  2. Circular buffers: useful in digital signal processing
  3. Queues: useful in digital signal processing

## Slide 4: Software State Machine
State machine keeps internal state as a variable, changes state based on inputs
Uses: control-dominated code; reactive systems
Example: Seat Belt Controller
  Turn on buzzer if a person sits in a seat and does not fasten the seat belt within a fixed amount of time
  Inputs:
    Seat sensor: to know when a person has sat down
    Seat belt sensor: to know when the belt is fastened
    Timer: to know when the fixed interval has elapsed
  Output: the buzzer
  States: Idle, seated, buzzer, belted

## Slide 5: State Machine Example: Seat Belt Controller

## Slide 6: Seat Belt Controller: C Code
#define IDLE 0 #define BELTED 2 #define SEATED 1 #define BUZZER 3
buzzer_on = OFF; timer_on = OFF;
switch(state) {
case IDLE:
if (seat) { state = SEATED; timer_on = TRUE; } break;
case SEATED:
if (belt) state = BELTED;
else if (timer) {state = BUZZER; buzzer_on = TRUE; } break;
case BELTED:
if (!seat) state = IDLE;
else if (!belt) { state = SEATED; timer_on = TRUE; } break;
case BUZZER:
if (belt) {state = BELTED; buzzer_on = OFF;}
else if (!seat) { state = IDLE; buzzer_on = OFF; }
}

## Slide 7: Circular Buffer
A data structure that allows efficient stream processing
Commonly used in signal processing:
  new data constantly arrives;
  each datum has a limited lifetime.
Use a circular buffer to hold the data stream
x1
x2
x3
x4
x5
x6
t1
t2
t3
x1
x2
x3
x4
Circular buffer
x5
x6
x7
Data stream

## Slide 8: Circular Buffer: C Implementation
Data structure
  put()
  init()
  get()
#define SIZE 3
int buffer[SIZE];
int pos;
void put(int value) {
pos = (pos + 1) % SIZE;
buffer[pos] = value;
}
void init() {
for (int i = 0; i < SIZE; i++)
buffer[i] = 0;
pos = SIZE - 1;
}
/* get the ith value from the circular buffer; zero being the newest value */
int get(int i) {
int index = (pos - i) % SIZE;
return buffer[index];
}

## Slide 9: Using Circular Buffers: FIR Filter
One output:
for (i = 0; i < SIZE; i++)
y += x[i] * b[i];
Processing as a stream using
a circular buffer:
int fir(int value) {
int i, y;
put(value);
for (i = 0, y = 0; i < SIZE; i++)
y += b[i] * get(i);
return y;
}

## Slide 10: Queues
Used when data arrival and departure or amount is unpredictable
A queue is also referred to as an elastic buffer
Circular buffer has a fixed number of data elements while a queue may have varying number of elements
Queues can be implemented based on linked lists or arrays
A linked list allows arbitrary sizes but requires dynamic memory allocation

## Slide 11: An Array-Based Queue
#define SIZE 5
int q[SIZE];
int head, tail;
void queue_init() {
head = 0;
tail = 0;
}
void enqueue(int value) {
if ((tail+1) % SIZE == head)
error("The queue is full");
q[tail] = value;
tail = (tail+1) % SIZE;
}
int dequeue() {
int value;
if (head == tail)
error("The queue is empty");
value = q[head];
head = (head+1) % SIZE;
return value;
}

## Slide 12: Producer/Consumer Systems
Queues allow varying input and output rates
Queues modify the flow of control in the system as well as store data

## Slide 13: Models of Programs
Source code is not a good representation for programs:
  clumsy
  language-dependent
Compilers derive intermediate representations to manipulate and optimize the program.
Abstraction allows easier analysis
One general model describes all language-specific models

## Slide 14: Data Flow Graph (DFG)
A data flow graph is a model of a program with no conditionals
Describes the minimal ordering requirements on operations
Single-Assignment Form: A variable appears only once on the left-hand side
x = a + b;
y = c - d;
z = x * y;
y = b + d;
original basic block
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
single assignment form

## Slide 15: Data Flow Graph (DFG)
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
single assignment form
The data flow graph determines feasible reorderings of
operations, which may help reduce pipeline or cache conflicts

## Slide 16: Control-Data Flow Graph (CDFG)
CDFG: represents control and data.
Uses data flow graphs as components.
A CDFG has two types of nodes:
  Data flow nodes: encapsulates a complete data flow graph
    Write operations in basic block form for simplicity
  Decision nodes: describe all types of control (branch)

## Slide 17: CDFG Example
if (cond1) bb1();
else bb2();
bb3();
switch (test1) {
case c1: bb4(); break;
case c2: bb5(); break;
case c3: bb6(); break;
}

## Slide 18: CDFG: For Loop
For Loop:
for (i=0; i<N; i++)
loop_body();
Equivalent While Loop:
i=0;
while (i<N) {
loop_body(); i++; }

## Slide 19: Compilation and Execution
an image of the program’s bits in memory

## Slide 20: From Assembly Code to Execution
Assembly Code
  Human-readable
  Abstracts out instruction format
  Abstracts out exact addresses
The Assembler
  Translates assembly code to binary representation (object code) according to instruction formats
  Partially translates labels into addresses
The Linker
  Determines all addresses across multiple program files
  Generates the executable binary file

## Slide 21: The Assembler
Labels are the most important abstraction provided by the assembler
Label processing requires two passes:
  1. Determine label addresses
    By advancing a Program Location Counter (PLC)
    PLC is incremented by instruction size (4 bytes in ARM)
  2. Assemble instructions using computed label values
The ORG pseudo-op specifies the origin, i.e. first address, of the program
  Relocatable code requires alternative mechanisms both in assembly code and generated object code

## Slide 22: The Symbol Table
Label addresses, resulting from the first pass, are recorded in a symbol table
A pseudo-op allows adding symbols to the table without occupying space in program memory: EQU—does not advance PLC
Example:

## Slide 23: Object File
Header
  location of main entry point (if any)
  size and position of pieces of file
Text Segment: instructions
Data Segment
  static data (local/global vars, strings, constants)
Relocation Information
  Instructions and data that depend on actual addresses
  Linker patches these bits after relocating segments
Symbol Table
  External (exported) references
  Unresolved (imported) references

## Slide 24: Object File Formats
Unix
  a.out
  COFF: Common Object File Format
  ELF: Executable and Linking Format
  …
Windows
  PE: Portable Executable
All support both executable and object files

## Slide 25: Linking
Combines several object modules into a single executable module
Allows programs to be divided into multiple files
Allows using pre-assembled libraries
Puts modules in order
Modifies object code to make the necessary links between files
Relocate each object’s text and data segments
Resolve as-yet-unresolved symbols
Record top-level entry point in executable file

## Slide 26: The Linker
The linker proceeds in two phases:
  1. Determine the first address in each object file, based on:
    The order in which the files are to be loaded
    The size of each object file
  2. Merge symbol tables, and update relative addresses in object files
The assembler must identify label references in object files
Both absolute and relative addressing are important in embedded systems:
Interrupts and I/O registers require absolute addressing

## Slide 27: Example

## Slide 28: Example

## Slide 29: Example: Objdump Disassembly

## Slide 30: Example: Objdump Symbols

## Slide 31
main.o
...
0C000000
21035000
1b80050C
8C040000
21047002
0C000000
...
00 T main
00 D uname
*UND* printf
*UND* pi
40, JL, printf
4C, LW/gp, pi
50, JL, square
math.o
...
21032040
0C000000
1b301402
3C040000
34040000
...
20 T square
00 D pi
*UND* printf
*UND* uname
28, JL, printf
30, LUI, uname
34, LA, uname
printf.o
...
3C T printf
...
21032040
0C40023C
1b301402
3C041000
34040004
...
0C40023C
21035000
1b80050c
8C048004
21047002
0C400020
...
10201000
21040330
22500102
...
Entry:0040 0100
text:0040 0000
data:1000 0000
calc.exe
00000003
0077616B
2
1
B
A
3
1
2
3
0040 0000
0040 0100
0040 0200
1000 0000
1000 0004
LUI 1000
ORI 0004
uname
pi
math
main
printf
.text
Symbol tbl
Relocation info
LW $4,-32764($gp)
$4 = pi
JAL square
JAL printf
LA uname

## Slide 32: Linking Example