COE 405, Term 181

Design & Modeling of Digital Systems

Assignment# 1

Due date: Thursday, Sep. 27

# It is required to design an iterative combinational circuit that computes the equation Z=2*X-1, where X is an n-bit unsigned number.

## Determine the number of inputs and outputs needed for your 1-bit cell. Explain the meaning of values in the interface signals.

## Derive the truth table of your 1-bit cell.

## Derive minimized equations for your 1-bit using K-Map method.

## Write a Verilog model for modeling your 1-bit cell by using an assign statement for each output.

## Write a Verilog model for modeling a 4-bit circuit based on the 1-bit model you have.

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=1}, {X=-1}, {X=3} and {X=-3}.

## This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a PDF file that contains the following items:

## i.      Your name and ID

## ii.     Assignment number

## iii.    Problem statement

## iv.    Your solution

## v. Include snapshots of simulation output to illustrate the correctness of your models.