COE 405, Term 162

Design & Modeling of Digital Systems

Assignment# 1 Solution

Due date: Saturday, March 4

# Consider the two functions f=(a ( b) + (a ( c) and g=a b + a' c + b' c'.

## Implement the function f using only 2x1 MUXs and inverters minimizing the number of MUXs used.

f = a' (b + c) + a (b' + c')

= a' ( b' (c) + b (1) ) + a ( b' (1) + b (c') )

## Compute the function f(g based on orthonormal basis expansion.

f  = a' b' (c) + a' b (1)  + a b' (1) + a b (c')

g = a' (b' + c) + a (b + c')

= a' ( b' (1) + b (c) ) + a ( b' (c') + b (1) )

= a' b' (1) + a' b (c) + a b' (c') + a b (1)

f(g = a' b' (c(1) + a' b (1(c) + a b' (1(c') +  a b (c'(1)

= a' b' (c') + a' b (c') + a b' (c) + a b (c)

= a' c' + a c

# It is required to design an iterative combinational circuit that computes the equation Z=3*X-3, where X is an n-bit unsigned number.

## Determine the number of inputs and outputs needed for your 1-bit cell. Explain the meaning of values in the interface signals.

This circuit can be designed by assuming that we have a borrow of 3 feeding the first cell or by representing -3 as -1+-1+-1 where -1 is represented in 2's complement as 11…111 and thus adding 3 to each cell. I will follow the second approach. We need to represent carry-out values in the range 0 to 5. Thus, we need three signals to represent Carry out values propagation across cells.

## Derive the truth table of your 1-bit cell.

| C1i-2 | C1i-1 | C0i-1 | Xi | C2i | C1i | C0i | Zi |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 |
| 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 |
| 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 | X | X | X | X |
| 1 | 1 | 0 | 1 | X | X | X | X |
| 1 | 1 | 1 | 0 | X | X | X | X |
| 1 | 1 | 1 | 1 | X | X | X | X |

## Derive minimized equations for your 1-bit using K-Map method.

Zi = C0i-1' Xi' + C0i-1 Xi = (C0i-1 ( Xi)'

C0i = C1i-1' C0i-1' + C1i-1' Xi + C1i-1 C0i-1 Xi'

= C1i-1' (C0i-1' + Xi) + C1i-1 C0i-1 Xi'

= C1i-1 ( (C0i-1' + Xi)

C1i = C1i-1 Xi' + C2i-1' C1i-1' Xi + C2i-1' C0i-1 Xi' + C2i-1 C0i-1' Xi'

= C1i-1 Xi' + C2i-1' C1i-1' Xi + Xi' (C2i-1 ( C0i-1)

C2i = C1i-1 Xi + C2i-1 Xi + C2i-1 C0i-1

## Write a Verilog model for modeling your 1-bit cell by using an assign statement for each output.

module OneCell (output C2i, C1i, C0i, Zi, input C2i_1, C1i_1, C0i_1, Xi);

assign Zi = C0i_1 ~^  Xi;

assign C0i = C1i_1 ^ (~C0i_1 |  Xi);

assign C1i = C1i_1 & ~Xi | ~C2i_1 &  ~C1i_1 & Xi | ~Xi &  (C2i_1 ^ C0i_1);

assign C2i = C1i_1 & Xi | C2i_1 & Xi | C2i_1 & C0i_1;

endmodule

## Write a Verilog model for modeling a 4-bit circuit based on the 1-bit model you have.

module D3XM3 (output C2, C1, C0, output [3:0] Z, input [3:0] X);

OneCell M1 (C2_0, C1_0, C0_0, Z[0],0, 0, 0, X[0]);

OneCell M2 (C2_1, C1_1, C0_1, Z[1],C2_0, C1_0, C0_0, X[1]);

OneCell M3 (C2_2, C1_2, C0_2, Z[2],C2_1, C1_1, C0_1, X[2]);

OneCell M4 (C2, C1, C0, Z[3],C2_2, C1_2, C0_2, X[3]);

endmodule

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=1}, {X=3}, {X=5} and {X=4}.

module D3XM3_Test();

reg [3:0] X;

wire C2, C1, C0;

wire [3:0] Z;

D3XM3 M1 (C2, C1, C0, Z, X);

initial begin

X=4'b0001;

#100 X=4'b0011;

#100 X=4'b0101;

#100 X=4'b0100;

end

endmodule

The generated simulation waveform verifies the correct functionality of the designed circuit:

# Text boxes

Xi

Zi

C2i-1

C1i-1

C0i-1

C2i

C1i

C0i