COE 405, Term 181

Design & Modeling of Digital Systems

Assignment# 2

Due date: Saturday, Oct. 13

# Consider the given FSM that has 7 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State | Output (Z) |
| --- | --- | --- |
|  | X=0 | X=1 | X=0 | X=1 |
| S0 | S3 | S1 | 0 | 1 |
| S1 | S3 | S2 | 1 | 0 |
| S2 | S6 | S5 | 0 | 1 |
| S3 | S0 | S4 | 0 | 1 |
| S4 | S0 | S5 | 1 | 0 |
| S5 | S1 | S2 | 0 | 1 |
| S6 | S0 | S2 | 1 | 0 |

## Determine the equivalent states.

## Reduce the state table into minimum number of states and show the reduced state table.

# Consider the given FSM that has 5 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S1, 1 | S2, 1 |
| S1 | S2, 0 | S3, 0 |
| S2 | S2, 1 | S3, 1 |
| S3 | S3, 0 | S4, 0 |
| S4 | S3, 1 | S4, 1 |

## Implement the FSM using the following state assignment: S0=000, S1=001, S2=100, S3=010 and S4=101.

## Implement the FSM using the following state assignment: S0=010, S1=101, S2=111, S3=001 and S4=011.

## Compare the area of the two resulting circuits.

# It is required to design a sequential circuit using Mealy model that computes the equation Z=3*X-4, where X is an unsigned number that will be fed serially.  Assume that the circuit has an asynchronous Reset input that resets the machine to the reset state.

## Draw the state diagram for your sequential circuit. Make sure that your state machine is minimal and that it does not have any redundant state.

## Derive minimized equations for the output Z and next state variables.

## Write a structural Verilog model for modeling your sequential circuit.

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=0}, {X=1}, {X=2} {X=3} and {X=4}.

## This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a PDF file that contains the following items:

## i.      Your name and ID

## ii.     Assignment number

## iii.    Problem statement

## iv.    Your solution

## v. Include snapshots of simulation output to illustrate the correctness of your models.