May 15, 2007

COMPUTER ENGINEERING DEPARTMENT

COE 405

DESIGN & MODELING OF DIGITAL SYSTEMS

Major Exam II

Second Semester  (062)

Time: 7:00-9:30 PM

OPEN BOOK EXAM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 30 |  |
| Q3 | 20 |  |
| Q4 | 30 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

[20 Points]

# (Q1)  Given the following Entity Description for a JK Flip-Flop:

# ENTITY JKFF IS 
 	GENERIC (delay : TIME := 4 NS); 
 	PORT (j, k, clk, reset : IN BIT; q, qb : OUT BIT); 
END JKFF;

## Model the JK-FF using a BLOCK statement with a GUARD expression and slective signal assignment, assuming that reset is synchronous and the JK-FF is rising-edge triggered.

## Model the JK-FF using a BLOCK statement with a GUARD expression and conditional signal assignment, assuming that reset is asynchronous and the JK-FF is rising-edge triggered.

[30 Points]

(Q2)  Manchester bit-encoding is used in Ethernet and IEEE 802.3 standard. You are to generate a signal with bit information in Manchester encoding. Each bit has a fixed length, bit_time. A bit 0 is encoded as high, H, for the first half of a bit_time and low, L, for the second half. A transition from H to L indicates the presence of a 0 on a line. Likewise, bit 1 is encoded as a transition from L to H. When no data is on a line, the line stays at the null or N value. This scheme of coding combines a clock signal, a data signal, and an enable line all into one signal. As in the example shown below, a data signal that is synchronized with the rising edge of a clock signal, along with its synchronizing clock and its enable line, are combined into a line containing bit-encoded information, be. You are to write a VHDL model to generate the Manchester encoded signal be. The data signal is sampled on the rising edge of the clock and if it is 1, a LH transition is made on the be line, and if it is 0, a HL transition is made. If the enable is off, the be line remains at the N value.

- Given the entity Encode shown below, write an architecture Manchester to produce the encoded signal using conditional signal assignment.

Entity Encode IS

Port  (clock, data, enable: IN bit; be: OUT : bit_encode);

Generic (bit_time: Time := 100 ns);

End Encode;

Assume that type bit_encode is defined as shown below and that it is stored in a package test_utilities in the work library:

Type bit_encode IS (N, L, H);

- Write a test bench to test the Architecture Manchester of Entity Encode. Assume that the input data will be read from a file data.txt and it has the format shown below. Assume that the default bit_time = 100 ns is used. You need to generate the clock signal inside the test bench with a period of bit_time and 50% duty cycle.

| Time | Data | Enable |
| --- | --- | --- |
| 0 ns | 0 | 1 |
| 280 ns | 1 | 1 |
| 460 ns | 0 | 1 |
| 840 ns | 1 | 0 |

[20 Points]

(Q3)  A generic n-bit multiplier can be modeled using BIT_VECTOR type as shown below:

Use work.exam_utility.all;

Entity MUL is

Generic (n : integer :=4);

Port (a, b : IN bit_vector(n-1 downto 0); c: OUT bit_vector(2*n-1 downto 0));

End MUL;

Architecture example of MUL is

Begin

c <= a * b;

End example;

For this architecture to work properly, we need to define the following function in the exam_utility package.

Function "*" (x, y : BIT_VECTOR) Return BIT_VECTOR

- Define the following function assuming unsigned multiplication:

Function "*" (x, y : BIT_VECTOR) Return BIT_VECTOR.

- Define the package exam_utility and put all the required functions and procedures to be used for the MUL architecture in it.

# [30 Points]

# (Q4) The three n-bit registers R1, R2, and R3, are connected through  a tri-state bus (Cbus) to allow the transfer of the content of any register to any other register as shown below:

Assume that the delay across a tri-state buffer is 4 ns and the flip-flop propagation delay is 2 ns. Assume that the signals are of type qit defined as: Type qit is ('0', '1', 'Z', 'X');

- Describe an Entity Datapath showing the inetrface signals assuming R1, R2, R3 as output signals, CLK, Reset,  R1in, R2in, R3in, R1out, R2out, and R3out as input signals, Cbus as input/output signal. Assume that Reset is Asynchronous reset. Use Genric n for determining  the width of registers, bufferdelay for  the delay across a tri-state buffer, and ffdelay  for the flip-flop propagation delay.

- Describe all needed types, subtypes and functions in a Utility package and use that utility package.

- Describe an architecture dataflow for the Entity.

# Text boxes

Reset

Reset

CLK

R3in

R3out

R3

Q

D

CLK

R2in

R1in

D

Q

R1out

R1

R2out

R2

Q

D

CLK

Reset

Cbus