COE 405

Design & Modeling of Digital Systems

Course Project

Simple RISC Computer

Due on: Sunday Jan. 5, 2004

In this project, you are to model a simple RISC processor with 32 general purpose, 32-bit registers, plus a program counter (PC) and an instruction register (IR). Although the main memory is organized as an array of bytes, only 32-bit words can be fetched from or stored into main memory. A word at address A is defined as the 4 bytes at that address and the succeeding three addresses. The byte at the lowest address contains the most significant 8-bits, the byte at the next address contains the next most significant 8 bits, and so on. The programmer’s model of the SRC machine is shown below. It has 23 instructions in 8 different formats:

- Load and Store instructions: There are four load instructions-- ld, ldr, la, and lar—and two store instructions– st and str.

- Branch instructions: There are two branch instructions, br and brl, that allow unconditional and conditional branches to an address contained in a specified register. The conditional branches test a register’s contents and branch when the register contents are . The instruction brl stores the PC in a specified register.

- Arithmetic instructions: There are four arithmetic instructions: add, addi, sub, and neg. All except addi take two register operands and place the result in a register. The instruction addi adds an immediate constant contained in the c2 field to a register and places the result in a register.

- Logical and shift instructions: There are nine logical and shift instructions: and, andi, or, ori, not, shr, sha, shl, and shc. The shift instructions can shift by a count contained as a constant in the instruction or by a count in a register.

- Miscellaneous instructions: There are two zero-operand instructions—nop and stop.

All instructions are 32 bits long. Because the SRC is of the load-store class of machine, operands in memory can be accessed only through load and store instructions. All instructions have a 5-bit opcode field, allowing 32 different instructions. Here we use only 23 of these instructions. The ra, rb, and rc fields are 5-bit fields and specify one of the 32 general purpose registers. A more detailed description of the processor is attached in the Appendix.

- Write a behavioral model for the SRC machine modeling all its specified instruction set.

- Write a behavioral model for the memory interfaced with the CPU.  Assume that the CPU-Memory interface contains the following control signals: Read, Write, and MFC (Memory Function Complete). Both the CPU and Memory are synchronized by the same clock. When a Read or Write request is initiated by the CPU, it remains 1 until the memory indicates that it finished the requested operation by setting the MFC signal to 1. Assume that the MFC signal will remain 1 for 1 clock cycle. Also, assume that the MFC signal changes based on the falling edge of the clock while the CPU signals change on the rising edge of the clock.

- Write a test bench to test your behavioral model of the SRC machine. The test bench should contain Memory, which contains an assembly program for the CPU to execute.

- Partition your CPU into a data path unit and a control unit. Write a register transfer model for the designed CPU. The data path should be described structurally while the components in the data path, i.e. ALU, registers can be described in a behavioral or dataflow style. The control unit is to be modeled as a finite state machine, which can be modeled in a behavioral or dataflow style.

- In the modeling of the data path use the three-bus design given in the Appendix.

- Use std_logic and std_logic_vector for all signals in the design.

- Include all functions, procedures, and user-defined types and constants in a package to be used by the CPU.

- For each entity that you model, test it and include simulation output indicating that it is working properly. The data-path should be tested before it is connected to the control unit. This way you can detect problems in the design and modeling early.

- Assume that the CPU-Memory interface contains the following control signals: Read, Write, and MFC (Memory Function Complete). Both the CPU and Memory are synchronized by the same clock. When a Read or Write request is initiated by the CPU, it remains 1 until the memory indicates that it finished the requested operation by setting the MFC signal to 1. Assume that the MFC signal will remain 1 for 1 clock cycle. Also, assume that the MFC signal changes based on the falling edge of the clock while the CPU signals change on the rising edge of the clock.

- Test the register transfer model of the SRC machine using the same test bench used for the behavioral model.

- If you manage to synthesize your CPU, map it to FPGA and demonstrate its proper operation, you will get a 5% bonus from your total mark in the course.

This project can be conducted by a team of a maximum of three students. If one student or two do the project they will be given a bonus. If you are a team of three students, you can divide the work such that one student does the behavioral model of the CPU, one models the data path and one models the control unit. You have to understand all the work done in the project, the part you do and the parts done by the other team members. Each student will be tested for the three parts and each student in the team will be given a separate grade.

Clearly state your assumptions and have your design well documented. Write a professional report indicating all design stages, modeling and testing of each component and the final design. Include both a hard copy and a soft copy of your report and all VHDL files. The grading policy for the project is shown below:

| Grading Criteria | Mark |
| --- | --- |
| Memory interface Modeling and Test | 5 |
| CPU Behavioral Description & Test Bench | 25 |
| Basic Components Modeling & Test | 10 |
| Data-path Design, Modeling & Test | 15 |
| Control Unit Design, Modeling & Test | 20 |
| Whole CPU Design, Modeling & Test | 20 |
| Report Organization | 5 |
| Total | 100 |

APPENDIX

# Text boxes

Data Path Design

C Bus

B Bus

A Bus

C

B

A

ALU

Y

SHIFTER

MDR

MAR

PC

IR

R31

R2

R1

R0