COE 405, Term 031

Design & Modeling of Digital Systems

HW# 1

Due date: Sunday, Oct. 12

# Consider the 4-bit carry-look-ahead adder (CLA) block shown below:

## Describe an Entity CLA4 in VHDL for this 4-bit CLA using exactly the same port names shown above.

## Write in VHDL an Architecture Arch1 for this 4-bit CLA using concurrent statements.

## Simulate the VHDL model Arch1 and verify that it is working properly. Include a snapshot of the simulated waveform.

## Write in VHDL an Architecture Arch2 for this 4-bit CLA using gate-level description.  Assume that the delay of an n-input gate is n ns.

## Simulate the VHDL model Arch2 and verify that it is working properly. Determine by simulation the critical path of the adder. Include a snapshot of the simulated waveform.

# It is required to model a 4-bit register with a synchronous rising-edge clock, and asynchronous reset.

## Describe an Entity FAR in VHDL for a d-ff with a synchronous rising-edge clock, and asynchronous reset.

## Model Architecture Arch1 for the d-ff using a process.

## Simulate the VHDL model Arch1 of FAR and verify that it is working properly. Include a snapshot of the simulated waveform.

## Describe an Entity Reg4 in VHDL for the 4-bit register with asynchronous reset.

## Model Architecture Arch1 for Reg4 using 4 instantiations of d-ff FAR.

## Simulate the VHDL model Arch1 of Reg4 and verify that it is working properly. Include a snapshot of the simulated waveform.

# It is required to model a 4-bit accumulator circuit using VHDL. The accumulator circuit shown below is designed using a 4-bit register with a synchronous rising-edge clock, CLK, and asynchronous reset, RST. When RST=0, the accumulator is reset to 0 asynchronously.

## Describe an Entity ACC in VHDL for the 4-bit accumulator.

## Model Architecture Arch1 for ACC using the 4-bit adder modeled in Q1 and the 4-bit register modeled in Q2.

## Simulate the VHDL model Arch1 of ACC and verify that it is working properly. Demonstrate that the accumulator can work as an up counter and also as a down counter by specifying proper input values. Include a snapshot of the simulated waveform.

# Text boxes

C3

Cin

S3-S0

B3-B0

A3-A0

4-bit CLA