COE 405										Term: 031

HW#1 Solution

Q1-i

Entity CLA4 is

port ( a , b : IN Bit_Vector(3 downto 0) ; s : OUT Bit_Vector(3 downTo 0) ;

Cin : in Bit; C3 : out Bit) ;

End;

-----------------------------------------------------------

Q1-ii

Architecture Arch1 of CLA4 is

SIGNAL P , G : Bit_Vector(3 downto 0);

SIGNAL  c0 , c1 , c2 : bit;

Begin

-- Pi = Ai Xor Bi

-- Gi = Ai And Bi

-- Si = Pi Xor Ci

-- C(i+1) = Gi Or (Pi And Ci)

P(0) <= a(0) Xor b(0);

G(0) <= a(0) And b(0);

P(1) <= a(1) Xor b(1);

G(1) <= a(1) And b(1);

P(2) <= a(2) Xor b(2);

G(2) <= a(2) And b(2);

P(3) <= a(3) Xor b(3);

G(3) <= a(3) And b(3);

s(0) <= P(0) Xor Cin ;

c0   <= G(0) OR (p(0) AND Cin);

s(1) <= P(1) XOR c0;

c1   <= G(1) OR (P(1) And G(0))

OR (P(1) And P(0) And Cin);

s(2) <= P(2) XOR c1;

c2   <= G(2) OR (P(2) AND G(1))

OR (P(2) AND P(1) AND G(0))

OR (P(2) And  P(1) And P(0) And Cin);

s(3) <= P(3) XOR c2;

c3   <= G(3) OR (P(3) And G(2))

OR (P(3) And P(2) And G(1))

OR (P(3) AND P(2) And P(1) And G(0))

OR (P(3) AND P(2) And P(1) AND P(0) And Cin);

End Arch1 ;

Q1-iii

Q1-iv

---------------------------------------------------------------------

---------------------------------------------------------------------

-- Define the entities needed in gate level architecture

---------------------------------------------------------------------

Entity AND2 is

PORT(a , b : IN bit ; c : OUT bit);

End ;

Architecture and2Arch of AND2 is

Begin

c <= a AND b after 2 ns;

End and2Arch;

------------------------------------------------------------------------

------------------------------------------------------------------------

Entity OR2 is

PORT(a , b : IN bit ; c : OUT bit);

End ;

Architecture OR2Arch of OR2 is

Begin

c <= a OR b after 2 ns;

End OR2Arch;

-----------------------------------------------------------------------

-----------------------------------------------------------------------

Entity XOR2 is

PORT(a , b : IN bit ; c : OUT bit);

End ;

Architecture XOR2Arch of XOR2 is

Begin

c <= a XOR b after 2 ns;

End XOR2Arch;

----------------------------------------------------------------------

----------------------------------------------------------------------

Entity C0Eval is

PORT(a , b , c : IN bit ; d : OUT bit);

End ;

----- c0  <= G(0) OR (p(0) AND Cin);

Architecture C0Arch of C0Eval is

Begin

d <= a OR (b And c) after 3 ns; -- since we have 3 inputs

End C0Arch;

----------------------------------------------------------------------

----------------------------------------------------------------------

Entity C1Eval is

PORT(a , b , c , d , e : IN bit ; f : OUT bit);

End ;

----- c1   <= G(1) OR (P(1) And G(0))

-----              OR (P(1) And P(0) And Cin);

Architecture C1Arch of C1Eval is

Begin

f <=  a OR (b And c) OR (b AND d And e) after 5 ns;

End C1Arch;

----------------------------------------------------------------------

----------------------------------------------------------------------

Entity C2Eval is

PORT(a, b , c ,d, e, f , g : IN bit ; h : OUT bit);

End ;

----- c2 <= G(2) OR (P(2) AND G(1))

-----            OR (P(2) AND P(1) AND G(0))

-----            OR (P(2) And  P(1) And P(0) And Cin);

Architecture C2Arch of C2Eval is

Begin

h      <=  a   OR (b AND c)

OR (b AND d AND e)

OR (b AND d AND f And g) after 7 ns; -- since we have 7 inputs

End C2Arch;

---------------------------------------------------------------------

---------------------------------------------------------------------

Entity C3Eval is

PORT(a, b , c ,d, e, f , g , h , i : IN bit ; j : OUT bit);

End ;

----  c3   <= G(3) OR (P(3) And G(2))

----               OR (P(3) And P(2) And G(1))

----               OR (P(3) AND P(2) And P(1) And G(0))

----               OR (P(3) AND P(2) And P(1) AND P(0) And Cin);

Architecture C3Arch of C3Eval is

Begin

j    <=   a  OR  (b And c)

OR (b And d And e)

OR (b AND d And f And g)

OR (b AND d And f AND h And i) after 9 ns;

End C3Arch;

-----------------------------------------------------------------------

-----------------------------------------------------------------------

Architecture Arch2 of CLA4 is

SIGNAL P , G : Bit_Vector(3 downto 0);

SIGNAL  c0 , c1 , c2 : bit;

component AND2

port(a,b:in bit; c:out bit);

end component ;

component OR2

port(a,b:in bit; c:out bit);

end component ;

component XOR2

port(a,b:in bit; c:out bit);

end component ;

component c0Eval

port(a,b,c:in bit; d:out bit);

end component ;

component c1Eval

port(a,b,c,d,e:in bit; f:out bit);

end component ;

component c2Eval

port(a,b,c,d,e,f,g:in bit; h:out bit);

end component ;

component c3Eval

port(a,b,c,d,e,f,g,h,i:in bit; j:out bit);

end component ;

Begin

g0   : AND2 PORT MAP (a(0), b(0), G(0) );

g1   : AND2 PORT MAP (a(1), b(1), G(1) );

g2   : AND2 PORT MAP (a(2), b(2), G(2) );

g3   : AND2 PORT MAP (a(3), b(3), G(3) );

p0   : XOR2 PORT MAP (a(0), b(0), P(0) );

p1   : XOR2 PORT MAP (a(1), b(1), P(1) );

p2   : XOR2 PORT MAP (a(2), b(2), P(2) );

p3   : XOR2 PORT MAP (a(3), b(3), P(3) );

sum0 : XOR2    PORT MAP (P(0) , Cin  , s(0));

car0 : C0Eval  PORT MAP (G(0) , P(0) , Cin , c0 );

sum1 : XOR2    PORT MAP (P(1)  , c0 , s(1));

car1 : c1Eval  PORT MAP (a => G(1) ,b=> P(1) ,c=> G(0) ,d=> P(0) ,e=> Cin , f=> c1);

sum2 : XOR2    PORT MAP (P(2) , c1 , s(2));

car2 : c2Eval  PORT MAP (G(2) , P(2) ,G(1),P(1),G(0),P(0),Cin, c2);

sum3 : XOR2    PORT MAP (P(3) , c2 , s(3));

car3 : c3Eval  PORT MAP (G(3), P(3) , G(2) ,P(2), G(1), P(1) , G(0) , P(0) , Cin , c3);

End Arch2;

Q1-v

Critical path highlighted when carry-in is propagated through all stages to C3. The critical path delay is 11ns.

Q2-i

Entity FAR is

port ( d,clk,reset : in BIT ; q : out BIT);

End FAR;

Q2-ii

Architecture Arch1 of FAR is

Begin

process (clk , reset)

Begin

if reset = '0' then

q <= '0' ;

else

if (clk= '1' and clk'Event) then

q <= d ;

end if;

end if ;

End process;

End Arch1;

Q2-iii

The following figure shows the operation of D-flip flop with a synchronous rising edge clock and asynchronous reset .

Q2-iv

Entity Reg4 is

Port(i:In Bit_Vector(3 downto 0);clock,res:IN BIT;o:OUT bit_Vector(3 downto 0));

End Reg4;

Q2-v

Architecture ArchReg1 of Reg4 is

component FAR

port (d,clk,reset : in bit ; q : OUT bit);

End component;

begin

bit0 : FAR PORT MAP (i(0),clock,res,o(0));

bit1 : FAR PORT MAP (i(1),clock,res,o(1));

bit2 : FAR PORT MAP (i(2),clock,res,o(2));

bit3 : FAR PORT MAP (i(3),clock,res,o(3));

End ArchReg1;

Q2-vi

The following figure shows the operation of the Register that has 4 D-flip flops.

Q3-i

Entity ACC Is

port( reset , clk : in BIT ; a  : inout   BIT_vector(3 downto 0);

b  : in   BIT_vector(3 downto 0));

End ACC;

Q3-ii

Architecture Arch1 of ACC is

signal sum : Bit_Vector(3 downto 0);

signal out_of_reg :  bit_vector(3 downto 0);

signal ci : bit:= '0';

signal c3 : bit;

component Reg4

Port(i:In Bit_Vector(3 downto 0);clock,res:IN BIT;o:OUT bit_Vector(3 downto 0));

End component ;

component CLA4

port ( a , b : IN Bit_Vector(3 downto 0) ; s : OUT Bit_Vector(3 downTo 0) ;

Cin : in Bit; C3 : out Bit) ;

End component ;

Begin

Addi  :  CLA4  PORT MAP(a,b,sum,ci,c3);

rege  :  Reg4  PORT MAP(sum,clk,reset,out_of_reg);

process (out_of_reg)

Begin

a <= out_of_reg;

end process ;

End Arch1;

Q3-iii

up counter

down counter