COE 405, Term 152

Design & Modeling of Digital Systems

HW# 2

Due date: Thursday, Feb. 25

# It is required to design a sequential circuit that has a single input X representing a signed 2's complement number and a single output Y. The circuit receives the number serially through the input X from the least significant bit (LSB) to the most significant bit (MSB), and computes the equation Y=3*X-2 and generates the output serially from the least significant bit to the most significant bit. The circuit has an additional asynchronous reset input R that resets the circuit into an initial state. The following are examples of input and output data:

Examples:

| Input | X | 0 | 1 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 0 | 0 | 0 | 0 | 1 |

| Input | X | 1 | 1 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 1 | 1 | 1 | 0 | 0 |

## Draw the state diagram of the circuit assuming a Mealy model.

## Implement the circuit using D-FFs.

## Verify the correctness of your circuit by simulation.

# Consider the given FSM that has 6 states, two inputs X and Y, and one output Z, represented by the following state table:

| Present State | Next State | Output |
| --- | --- | --- |
|  | XY=00 | XY=01 | XY=10 | XY=11 | Z |
| S0 | S0 | S1 | S2 | S3 | 1 |
| S1 | S0 | S3 | S1 | S4 | 0 |
| S2 | S1 | S3 | S2 | S4 | 1 |
| S3 | S1 | S0 | S4 | S5 | 0 |
| S4 | S0 | S1 | S2 | S5 | 1 |
| S5 | S1 | S4 | S0 | S5 | 0 |

## Determine the equivalent states.

## Reduce the state table into the minimum number of states and show the reduced state table.

# Consider the given FSM that has 4 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S0, 1 | S2, 0 |
| S1 | S0, 0 | S2, 0 |
| S2 | S1, 0 | S3, 0 |
| S3 | S1, 0 | S3, 1 |

## Implement the FSM using the following state assignment: S0=00, S1=01, S2=10, S3=11.

## Implement the FSM using the following state assignment: S0=01, S1=10, S2=11, S3=00.

## Compare the area of the two resulting circuits.

# Consider the circuit given below representing a serial adder. Assume that the delay of a 2-input AND gate is 2 unit delays, the delay of a 2-input OR gate is 2 unit delays and the delay of a 2-input XOR gate is 4 unit delays.

## Determine the critical path of this circuit and the maximum propagation delay.

## Using only the Retiming transformation, reduce the critical path of this circuit with the minimum number of flip-flops possible.

# Text boxes

LSB

MSB

Input=6

Output=16

MSB

LSB

Input=3

Output=7