COE 405

Homework#2 Solution

Solution to Q.1:

(i)

entity count3 is

port(reset,clk,dir:in bit;			--inputs

c:buffer bit_vector(2 downto 0)); --outputs

end count3;

(ii)

architecture behave of count3 is

begin

process(clk)

subtype cnt8 is integer range 0 to 7;--subtype to round the counter

variable cnt:cnt8 :=0;--variable cnt to follow the count

begin

if (clk = '1' and clk'event) then --check for rising edge of the clk

if reset = '1' then cnt:=0;

else

if dir='0' then  --count up and check if you reach the end(7)

if cnt=7 then cnt:=0; else cnt:=cnt+1; end if;

else 	--count down and check if you reach the end(0)

if cnt=0 then cnt:=7; else cnt:=cnt-1; end if;

end if;

end if;

case cnt is   --output the count

when 0 => 		c<="000";

when 1 => 		c<="001";

when 2 => 		c<="010";

when 3 => 		c<="011";

when 4 => 		c<="100";

when 5 => 		c<="101";

when 6 => 		c<="110";

when 7 => 		c<="111";

end case;

end if;

end process;

end behave;

(iii)

entity inv is  --inverter to be used in the circuit of the counter

port(i:in bit; o:out bit);

end inv;

architecture behavior of inv is

begin

o<= not(i);

end behavior;

entity and2 is  --2-input and gate to be used in the circuit of the counter

port(i1,i2:in bit;o:out bit);

end and2;

architecture behavior of and2 is

begin

o<= i1 and i2;

end behavior;

entity and3 is   --3-input and gate to be used in the circuit of the counter

port(i1,i2,i3:in bit;o:out bit);

end and3;

architecture behavior of and3 is

begin

o<= i1 and i2 and i3;

end behavior;

entity or2 is  --2-input or gate to be used in the circuit of the counter

port(i1,i2:in bit;o:out bit);

end or2;

architecture behavior of or2 is

begin

o<= i1 or i2;

end behavior;

entity t_flop is  --t_flip-flop to be used in the circuit of the counter

port(rst,t,clk:in bit;

q:buffer bit);

end t_flop;

architecture arch of t_flop is

begin

process(clk)

begin

if(clk='1' and clk'event)then

if rst='1' then q<='0';

else

if t='0' then q<=q;

else q<= not q;

end if;

end if;

end if;

end process;

end arch;

architecture struct of count3 is

component inv is

port(i:in bit; o:out bit);

end component;

component and2 is

port(i1,i2:in bit;o:out bit);

end component and2;

component and3 is

port(i1,i2,i3:in bit;o:out bit);

end component and3;

component or2 is

port(i1,i2:in bit;o:out bit);

end component or2;

component t_flop is

port(rst,t,clk:in bit;

q:buffer bit);

end component t_flop;

--internal signals(refer to the circuit diagram)

signal s1,s2,s3,s4,s5,s6,s7,s8,s9,s10,s11:bit;

begin

g1:inv port map(c(0),s2);

g2:inv port map(dir,s1);

g3:inv port map(c(1),s6);

g4:and2 port map(s2,dir,s3);

g5:and2 port map(s1,c(0),s4);

g6:and3 port map(s2,s6,dir,s7);

g7:and3 port map(c(0),c(1),s1,s8);

g8:or2 port map(s3,s4,s5);

g9:or2 port map(s7,s8,s9);

f0:t_flop port map(reset,'1',clk,c(0));

f1:t_flop port map(reset,s5,clk,c(1));

f2:t_flop port map(reset,s9,clk,c(2));

end struct;

Solution to Q.2:

(i)

entity shifter4 is

port(reset,clk,dir,si:in bit;			--inputs

s:buffer bit_vector(3 downto 0)); --outputs

end shifter4;

(ii)

architecture behave of shifter4 is

begin

process(clk)

begin

if (clk = '1' and clk'event) then   --check for rising edge of the clock

if reset = '1' then s<="0000";

else

if dir='0' then

s<= s(2 downto 0) & si; --shift left

else

s<=si & s(3 downto 1); --shift right

end if;

end if;

end if;

end process;

end behave;

(iii)

entity inv is  --inverter to be used in the circuit of the mux

port(i:in bit; o:out bit);

end inv;

architecture behavior of inv is

begin

o<= not(i);

end behavior;

entity and2 is --and gate to be used in the circuit of the mux

port(i1,i2:in bit;o:out bit);

end and2;

architecture behavior of and2 is

begin

o<= i1 and i2;

end behavior;

entity or2 is  --or gate to be used in the circuit of the mux

port(i1,i2:in bit;o:out bit);

end or2;

architecture behavior of or2 is

begin

o<= i1 or i2;

end behavior;

entity d_flop is  -- defining the d flip-flop

port(rst,d,clk:in bit;

q:buffer bit);

end d_flop;

architecture arch of d_flop is --architecture of the flop

begin

process(clk)

begin

if(clk='1' and clk'event)then

if rst='1' then q<='0';

else q<= d;

end if;

end if;

end process;

end arch;

entity mux is  --defining the mux

port(i0,i1,d:in bit;

o:out bit);

end mux;

architecture struct of mux is --structral architecture of the mux

component inv is				--using many gates

port(i:in bit; o:out bit);

end component inv;

component and2 is

port(i1,i2:in bit;o:out bit);

end component and2;

component or2 is

port(i1,i2:in bit;o:out bit);

end component or2;

signal s1,s2,s3:bit;  --internal signals of the mux

begin

g1:inv 	port map(d,s1);

g2:and2 port map(d,i1,s2);

g3:and2 port map(s1,i0,s3);

g4:or2 port map(s2,s3,o);

end struct;

architecture struct of shifter4 is

component mux is

port(i0,i1,d:in bit;

o:out bit);

end component mux;

component d_flop is

port(rst,d,clk:in bit;

q:buffer bit);

end component d_flop;

signal m0,m1,m2,m3:bit; --internal signals: mi represents the output of the

begin			--mux and the input of flip-flop

x3:mux port map(s(2),si,dir,m3);

x2:mux port map(s(1),s(3),dir,m2);

x1:mux port map(s(0),s(2),dir,m1);

x0:mux port map(si,s(1),dir,m0);

f3:d_flop port map(reset,m3,clk,s(3));

f2:d_flop port map(reset,m2,clk,s(2));

f1:d_flop port map(reset,m1,clk,s(1));

f0:d_flop port map(reset,m0,clk,s(0));

end struct;