Design & Modeling of Digital Systems

HW# 2   Solution

Q1.

(i)

ENTITY SHIFTREG4 IS

PORT (	SEL: IN BIT_VECTOR(1 DOWNTO 0);

SI, CLK, RESET: IN BIT;

S: BUFFER BIT_VECTOR(3 DOWNTO 0):= "0000");

END SHIFTREG4;

-------------------------------------------------

(ii)

ARCHITECTURE BEHAV OF SHIFTREG4 IS

SIGNAL S0, S3: BIT;

BEGIN

PROCESS (CLK)

BEGIN

IF((CLK = '1' AND CLK'EVENT)) THEN

IF RESET = '1' THEN

S <= "0000";

-- SHIFT LEFT

ELSE IF (SEL(1) = '0' AND SEL(0) = '0') THEN

S <= S(2 DOWNTO 0) & SI;

-- SHIFT RIGHT

ELSE IF (SEL(1) = '0' AND SEL(0) = '1') THEN

S <= SI & S(3 DOWNTO 1);

-- ROTATE LEFT

ELSE IF (SEL(1) = '1' AND SEL(0) = '0') THEN

S <= S(2 DOWNTO 0) & S(3);

-- ROTATE RIGHT

ELSE

S <= S(0) & S(3 DOWNTO 1);

END IF;

END IF;

END IF;

END IF;

END IF;

END PROCESS;

END BEHAV;

-------------------------------------------------

(iii)

ARCHITECTURE STRUCT OF SHIFTREG4 IS

COMPONENT MUX2X1

PORT (SEL: IN BIT; S1, S0: IN BIT; RES: OUT BIT := '0');

END COMPONENT;

COMPONENT MUX4X1

PORT (SEL: IN BIT_VECTOR (1 DOWNTO 0); S3, S2, S1, S0: IN BIT; RES: OUT BIT := '0');

END COMPONENT;

COMPONENT FAR

PORT (CLK, RESET, D: IN BIT; Q: BUFFER BIT := '0');

END COMPONENT;

SIGNAL RES3, RES2, RES1, RES0: BIT;

BEGIN

-- MUXES

U00: MUX4X1 PORT MAP (SEL, S(0), S(2), SI, S(2), RES3);

U01: MUX2X1 PORT MAP (SEL(0), S(3), S(1), RES2);

U02: MUX2X1 PORT MAP (SEL(0), S(2), S(0), RES1);

U03: MUX4X1 PORT MAP (SEL, S(1), S(3), S(1), SI, RES0);

-- FLIP FLOPS

U04: FAR PORT MAP (CLK, RESET, RES3, S(3));

U05: FAR PORT MAP (CLK, RESET, RES2, S(2));

U06: FAR PORT MAP (CLK, RESET, RES1, S(1));

U07: FAR PORT MAP (CLK, RESET, RES0, S(0));

-- FINISH

END STRUCT;

-------------------------------------------------

ENTITY MUX2X1 is

port (	SEL: IN BIT;

S1, S0: IN BIT;

RES: OUT BIT:='0');

END MUX2X1;

-------------------------------------------------

ARCHITECTURE BEHAV OF MUX2X1 is

BEGIN

PROCESS (SEL, S0, S1)

BEGIN

IF SEL = '0' THEN

RES <= S0;

ELSE

RES <= S1;

END IF;

END PROCESS;

END BEHAV;

-------------------------------------------------

ENTITY MUX4X1 is

port (	SEL: IN BIT_VECTOR(1 DOWNTO 0);

S3, S2, S1, S0: IN BIT;

RES: OUT BIT:='0');

END MUX4X1;

-------------------------------------------------

ARCHITECTURE BEHAV OF MUX4X1 is

BEGIN

PROCESS (SEL(1), SEL(0), S0, S1, S2, S3)

BEGIN

IF (SEL(1) = '0' AND SEL(0)='0') THEN

RES <= S0;

ELSE IF (SEL(1) = '0' AND SEL(0)='1') THEN

RES <= S1;

ELSE IF (SEL(1) = '1' AND SEL(0)='0') THEN

RES <= S2;

ELSE

RES <= S3;

END IF;

END IF;

END IF;

END PROCESS;

END BEHAV;

-------------------------------------------------

ENTITY FAR is

port (	CLK, RESET: IN BIT;

D: IN BIT;

Q: BUFFER BIT:='0');

END FAR;

-------------------------------------------------

ARCHITECTURE Arch1 OF FAR is

BEGIN

PROCESS (CLK)

BEGIN

IF((CLK = '1' AND CLK'EVENT)) THEN

IF RESET = '1' THEN

Q <= '0' AFTER 8 ns;

ELSE

Q <= D AFTER 8 ns;

END IF;

END IF;

END PROCESS;

END Arch1;

Q2.

|  | 0 | δ | 2δ | 5 ns | 10 ns | 10 + δ | 15 ns |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 0 | 0 | 0 | 0 | 1 | 1 | 1 |
|  | ('1' , 10 ns) | ('1' , 10 ns) | ('1' , 10 ns) | ('1' , 5 ns) | ('0' , 10 ns) | ('0' , 10 ns) | ('0' , 5 ns) |
| B | 0 | Z | Z | Z | Z | Z | Z |
|  | ('Z', δ) ('0' , 25 ns) ('0' , 35 ns) | ('0' , 25 ns) ('0' , 35 ns) | ('0' , 25 ns) ('0' , 35 ns) | ('0' , 20 ns) ('0' , 30 ns) | ('0' , 15 ns) ('0' , 25 ns) ('Z' , δ) ('1' , 25 ns) ('0' , 35 ns) | ('1' , 25 ns) ('0' , 35 ns) | ('1' , 20 ns) ('0' , 30 ns) |
| C | 0 | 1 | 1 | 0 | 0 | 1 | 1 |
|  | ('1' , δ) ('0' , 5 ns) ('0' , 20 ns) | ('1' , δ) ('0' , 5 ns) ('Z' , 20 ns) | ('0' , 5 ns) ('Z' , 20 ns) | ('Z' , 15 ns) | ('Z' , 10 ns) ('1' , δ ) ('1' , 5 ns) ('Z' , 20 ns) | ('1' , 5 ns) ('Z' , 20 ns) | ('Z' , 15 ns) |

|  | 15 ns | 20 ns | 20 + δ | 25 ns | 30 ns | 30 + δ | 35 ns |
| --- | --- | --- | --- | --- | --- | --- | --- |
| A | 1 | 0 | 0 | 0 | 1 | 1 | 1 |
|  | ('0' , 5 ns) | ('1' , 10 ns) | ('1' , 10 ns) | ('1' , 5 ns) | ('0' , 10 ns) | ('0' , 10 ns) | ('0' , 5 ns) |
| B | Z | Z | Z | Z | Z | Z | Z |
|  | ('1' , 20 ns) ('0' , 30 ns) | ('1' , 15 ns) ('0' , 25 ns) ('Z', δ) ('0' , 25 ns) ('0' , 35 ns) | ('0' , 25 ns) ('0' , 35 ns) | ('0' , 20 ns) ('0' , 30 ns) | ('0' , 15 ns) ('0' , 25 ns) ('Z', δ) ('1' , 25 ns) ('0' , 35 ns) | ('1' , 25 ns) ('0' , 35 ns) | ('1' , 20 ns) ('0' , 30 ns) |
| C | 1 | 1 | 1 | 0 | 0 | 1 | 1 |
|  | ('Z' , 15 ns) | ('Z' , 10 ns) ('1' , δ) ('0' , 5 ns) ('Z' , 20 ns) | ('0' , 5 ns) ('Z' , 20 ns) | ('Z' , 15 ns) | ('Z' , 10 ns) ('1' , δ) ('1' , 5 ns) ('Z' , 20 ns) | ('1' , 5 ns) ('Z' , 20 ns) | ('Z' , 20 ns) |

|  | 35 ns | 40 ns | 40 + δ | 45 ns | 60 ns | 65 ns | 65 + δ | 70 ns |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
|  | ('0' , 5 ns) | ----- | ----- | ----- | ----- | ----- | ----- | ----- |
| B | Z | Z | Z | Z | Z | 0 | 0 | 0 |
|  | ('1' , 20 ns) ('0' , 30 ns) | ('1' , 15 ns) ('0' , 25 ns) ('Z', δ) ('0' , 25 ns) ('0' , 35 ns) | ('0' , 25 ns) ('0' , 35 ns) | ('0' , 20 ns) ('0' , 30 ns) | ('0' , 5 ns) ('0' , 15 ns) | ('0' , 10 ns) | ('0' , 10 ns) | ('0' , 5 ns) |
| C | 1 | 1 | 1 | 0 | Z | Z | 1 | 0 |
|  | ('Z' , 20 ns) | ('Z' , 15 ns) ('1' , δ) ('0' , 5 ns) ('Z' , 20 ns) | ('0' , 5 ns) ('Z' , 20 ns) | ('Z' , 15 ns) | ----- | ('1' , δ) ('0' , 5 ns) ('0' , 20 ns) | ('0' , 5 ns) ('0' , 20 ns) | ('0' , 15 ns) |

|  | 70 ns | 75 ns | 75+ δ | 80 | 95 |
| --- | --- | --- | --- | --- | --- |
| A | 0 | 0 | 0 | 0 | 0 |
|  | ----- | ------ | ----- | ------ | ----- |
| B | 0 | 0 | 0 | 0 | 0 |
|  | ('0' , 5 ns) | ----- | ----- | ------ | ----- |
| C | 0 | 0 | 1 | 0 | 0 |
|  | ('0' , 15 ns) | ('0' , 10 ns) ('1' , δ) ('0' , 5 ns) ('0' , 20 ns) | ('0' , 5 ns) ('0' , 20 ns | ('0' , 15 ns) | ---- |