COE 405, Term 152

Design & Modeling of Digital Systems

HW# 2   Solution

Due date: Thursday, Feb. 25

# It is required to design a sequential circuit that has a single input X representing a signed 2's complement number and a single output Y. The circuit receives the number serially through the input X from the least significant bit (LSB) to the most significant bit (MSB), and computes the equation Y=3*X-2 and generates the output serially from the least significant bit to the most significant bit. The circuit has an additional asynchronous reset input R that resets the circuit into an initial state. The following are examples of input and output data:

Examples:

| Input | X | 0 | 1 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 0 | 0 | 0 | 0 | 1 |

| Input | X | 1 | 1 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 1 | 1 | 1 | 0 | 0 |

## Draw the state diagram of the circuit assuming a Mealy model.

| Present State | Next State, Y |
| --- | --- |
|  | X=0 | X=1 |
| S0 (B=2) | S1, 0 | S2, 1 |
| S1 (B=1) | S1, 1 | S3, 0 |
| S2 (B=0) | S2, 0 | S3, 1 |
| S3 (C=1) | S2, 1 | S4, 0 |
| S4 (C=2) | S3, 0 | S4, 1 |

## Implement the circuit using D-FFs.

## Since we have 5 states, we need 3 FFs: F2, F1, and F0. We will use the following encoding: S0=000, S1=001, S2=010, S3=011, S4=100.

| Present State F2F1F0 | Next State, Y |
| --- | --- |
|  | X=0 | X=1 |
| 0 0 0 | 0 0 1, 0 | 0 1 0, 1 |
| 0 0 1 | 0 0 1, 1 | 0 1 1, 0 |
| 0 1 0 | 0 1 0, 0 | 0 1 1, 1 |
| 0 1 1 | 0 1 0, 1 | 1 0 0, 0 |
| 1 0 0 | 0 1 1, 0 | 1 0 0, 1 |

Y = F0' X + F0 X' = F0 ( X

F0+ = F1' F0 + F1' X' + F1 F0' X = F1' (F0 + X') + F1 F0' X = F1 ( (F0 + X')

F1+ = F2'F1' X + F1 F0' + F1 X' + F2 X' =  F2'F1' X + X' (F1 + F2) + F1 F0'

= X  ( (F1 + F2) + F1 F0'

F2+ = F2 X + F1 F0 X = X (F2 + F1 F0)

## Verify the correctness of your circuit by simulation.

Input: 01100 (X=6)  Output: 00001 (Y=16)

Input: 11000 (X=3)  Output: 11100 (Y=7)

# Consider the given FSM that has 6 states, two inputs X and Y, and one output Z, represented by the following state table:

| Present State | Next State | Output |
| --- | --- | --- |
|  | XY=00 | XY=01 | XY=10 | XY=11 | Z |
| S0 | S0 | S1 | S2 | S3 | 1 |
| S1 | S0 | S3 | S1 | S4 | 0 |
| S2 | S1 | S3 | S2 | S4 | 1 |
| S3 | S1 | S0 | S4 | S5 | 0 |
| S4 | S0 | S1 | S2 | S5 | 1 |
| S5 | S1 | S4 | S0 | S5 | 0 |

## Determine the equivalent states.

| S1 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| S2 | (0,1), (1,3), (3,4) |  |  |  |  |
| S3 |  | (0,1), (0,3), (1,4), (4,5) |  |  |  |
| S4 | (3,5) |  | (0,1), (1,3), (4,5) |  |  |
| S5 |  | (0,1), (3,4), (4,5) |  | (0.4) |  |
|  | S0 | S1 | S2 | S3 | S4 |

## Thus, the equivalent states are (S0, S4) and (S3, S5).

## Reduce the state table into the minimum number of states and show the reduced state table.

The reduced state table is as follows:

| Present State | Next State | Output |
| --- | --- | --- |
|  | XY=00 | XY=01 | XY=10 | XY=11 | Z |
| S0 | S0 | S1 | S2 | S3 | 1 |
| S1 | S0 | S3 | S1 | S0 | 0 |
| S2 | S1 | S3 | S2 | S0 | 1 |
| S3 | S1 | S0 | S0 | S3 | 0 |

# Consider the given FSM that has 4 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S0, 1 | S2, 0 |
| S1 | S0, 0 | S2, 0 |
| S2 | S1, 0 | S3, 0 |
| S3 | S1, 0 | S3, 1 |

## Implement the FSM using the following state assignment: S0=00, S1=01, S2=10, S3=11.

Y = F1' F0' X' + F1 F0 X

F0+ = F1

F1+= X

## Implement the FSM using the following state assignment: S0=01, S1=10, S2=11, S3=00.

Z = F1' F0' X + F1' F0 X' = F1' (F0' X + F0 X') = F1' (F0 ( X)

F0+ = F1' F0 + F1 F0' = F1 ( F0

F1+ = F1' F0' X' + F1' F0 X + F1 F0' X + F1 F0 X' = F1' (F0' X' + F0 X) + F1 (F0' X + F0 X')

= F1 ( F0 ( X

## Compare the area of the two resulting circuits.

The number of literals using the first state assignment is 6 while it is 14 using the second state assignment. We could also say that the first assignment uses an equivalent of 5 2-input primitive gates while the second state assignment uses 10 2-input primitive gates. Therefore, the first assignment produces a significantly lower area than the second assignment.

# Consider the circuit given below representing a serial adder. Assume that the delay of a 2-input AND gate is 2 unit delays, the delay of a 2-input OR gate is 2 unit delays and the delay of a 2-input XOR gate is 4 unit delays.

## Determine the critical path of this circuit and the maximum propagation delay.

## Using only the Retiming transformation, reduce the critical path of this circuit with the minimum number of flip-flops possible.

# Text boxes

LSB

MSB

Input=6

Output=16

MSB

LSB

Input=3

Output=7