COE 405								Dr. Aiman El-Maleh

HW#3 Solution

Q.1. It is required to model in VHDL a parametrizable n-bit Ripple Carry Adder.

- Describe the entity of the n-bit adder using GNERIC for passing the adder size.

entity FA is

port (a, b, cin    : in BIT;

sum, cout  : out BIT);

end FA;

-- description of adder using concurrent signal assignments

architecture behave of FA is

begin

sum <= (a xor b) xor cin;

cout <= (a and b) or (cin and a) or (cin and b);

end behave;

==============

entity RCA is

generic(N : integer := 4);

port (a    : in BIT_vector(N downto 1);

b    : in BIT_vector(N downto 1);

cin  : in BIT;

sum  : out BIT_vector(N downto 1);

cout : out BIT);

end RCA;

(ii) Model architecture for the n-bit adder using GENERATE statement.

-- structural implementation of the N-bit adder

Use work.HW3.all;

architecture structural of RCA is

FOR ALL : n1 USE ENTITY WORK.FA;

signal carry : BIT_vector(0 to N);

begin

carry(0) <= cin;

cout <= carry(N);

-- instantiate a single-bit adder N times

gen: for I in 1 to N generate

add: n1 port map(

a => a(I),

b => b(I),

cin => carry(I - 1),

sum => sum(I),

cout => carry(I));

end generate;

end structural;

(iii) Define a package called HW3 where you store all used components, functions and

procedures inside the package and use the package when needed.

------------------------------------------------

--		PACKAGE DECLERATION

------------------------------------------------

Package HW3 is

Type integers IS ARRAY (0 to 9) OF INTEGER;

COMPONENT n1 port (a : in BIT;b : in BIT; cin : in BIT;sum : out BIT;cout : out BIT); END COMPONENT ;

component RCA

generic(N : integer);

port (a    : in Bit_vector(N downto 1);

b    : in Bit_vector(N downto 1);

cin  : in Bit;

sum  : out Bit_vector(N downto 1);

cout : out Bit);

end component;

Procedure Int2Bin (Int: IN Integer; Bin : OUT BIT_VECTOR);

Procedure Bin2Int (Bin : IN BIT_VECTOR;  Int: OUT Integer);

Procedure Apply_Data ( Signal Target: OUT Bit_Vector;		Constant Values: IN Integers;	Constant Period: IN Time) ;

END HW3;

------------------------------------------------

--		PACKAGE BODY

------------------------------------------------

Package Body HW3 IS

Procedure Int2Bin (Int: IN Integer; Bin : OUT BIT_VECTOR)  IS

Variable Tmp: Integer;

Begin

Tmp := Int;

For I IN 1 To (Bin'Length) Loop

If ( Tmp MOD 2 = 1) Then

Bin(I) :='1' ;

Else Bin(I) := '0' ;

End If;

Tmp := Tmp / 2;

End Loop;

End Int2Bin;

Procedure Bin2Int (Bin : IN BIT_VECTOR;  Int: OUT Integer)  IS

Variable Result: Integer;

Begin

Result := 0;

For I  IN Bin'RANGE  Loop

If Bin(I) = '1' Then

Result := Result + 2**I;

End If;

End Loop;

Int := Result / 2;

End Bin2Int;

Procedure Apply_Data (

Signal Target: OUT Bit_Vector ;

Constant Values: IN Integers;

Constant Period: IN Time) IS

Constant n : INTEGER := target'length;

VARIABLE j: INTEGER;

VARIABLE tmp, pos : INTEGER :=0;

Variable Buf: Bit_Vector (N Downto 1);

Begin

For I IN 0 To (integers'length -1) Loop

tmp := values (i);

j:= 1;

WHILE j <= N LOOP

IF(tmp MOD 2 = 1) THEN

buf (j) := '1';

else buf(j) :='0';

end if;

tmp:= tmp /2;

j:= j +1;

END LOOP;

target <= TRANSPORT buf AFTER i * period;

END LOOP;

End Apply_Data;

end HW3;

(iv) Write a test bench for testing the n-bit ripple carry adder assuming that the input

arguments will be specified using the procedure Apply_Data given in the book..

entity testHW3 is

end;

------------------------------------------------------------------------

-- testbench for 4-bit adder

------------------------------------------------------------------------

Use work.HW3.all;

architecture RCA4 of testHW3 is

FOR ALL : RCA USE ENTITY WORK.RCA;

constant N : integer := 4;

signal a    : Bit_vector(N downto 1);

signal b    : Bit_vector(N downto 1);

signal cin  : Bit;

signal sum  : Bit_vector(N downto 1);

signal cout : Bit;

begin

a1: RCA generic map (n)

port map ( a, b, cin, sum, cout);

apply_data(a, 00&05&06&08&10&11&09&03&15&14, 100 ns);

apply_data(b, 01&06&07&02&05&01&09&11&01&00, 100 ns);

cin <= '1', '0' AFTER 500 ns;

END RCA4;

(v) Write a test bench for testing the n-bit ripple carry adder assuming that the input

arguments will be read as integers from an input file and that the output will be

stored as integer in an output file. Use TEXTIO package for this purpose. Hint:

assignments scheduled on signals inside a process take effect after encountering a

wait statement. Use the statement wait for 0 ns as many times as needed for this

purpose.

entity testHW32 is

end;

------------------------------------------------------------------------

-- testbench for 4-bit adder

------------------------------------------------------------------------

Use work.HW3.all;

USE STD.TEXTIO.ALL;

architecture RCA4 of testHW32 is

constant N : integer := 4;

signal a    : Bit_vector(N downto 1);

signal b    : Bit_vector(N downto 1);

signal cin  : Bit;

signal sum  : Bit_vector(N downto 1);

signal cout : Bit;

FOR a1: RCA USE ENTITY WORK.RCA;

begin

Process

File Infile : Text IS IN "example1.txt" ;

File Outfile: Text IS OUT "Outfile1.txt" ;

Variable Out_Line, My_Line : Line;

Variable Int_Val, Int_Value : Integer;

Variable Buf1: Bit_Vector (N Downto 1);

Variable Buf2: Bit_Vector (N Downto 1);

Variable BufCin : Bit_Vector (1 Downto 1);

Begin

While Not (Endfile(Infile)) Loop

Readline( Infile, My_Line);  -- read a line from the input file

Read( My_Line, Int_Val);	         -- read a value from the line

Int2Bin (Int_Val, BufCin);

cin <= BufCin(1);

wait for 0 ns;

wait for 0 ns;

--Readline( Infile, My_Line);  -- read a line from the input file

Read( My_Line, Int_Val);	         -- read a value from the line

Int2Bin (Int_Val, Buf1);

a <= Buf1;

wait for 0 ns;

wait for 0 ns;

--Readline( Infile, My_Line);  -- read a line from the input file

Read(My_Line, Int_Val);	         -- read a value from the line

Int2Bin (Int_Val, Buf2);

b <= Buf2;

wait for 0 ns;

wait for 0 ns;

-- To let the input settle

wait for 100 ns;

Bin2Int (sum , Int_Val);

Write( Out_Line, Int_Val);	         -- write the squared value to the line

Write( Out_Line, cout);	         -- write the squared value to the line

WriteLine( Outfile, Out_Line);       -- write the line to the output file

End Loop;

wait;

End Process;

a1: RCA generic map (n)

port map ( a, b, cin, sum, cout);

END RCA4;

========================

THE INPUT FILE " example1.txt" :

1 0 1

1 5 6

1 6 7

1 8 2

1 10 5

0 11 1

0 9 9

0 3 11

0 15 1

0 14 0

THE OUTPUT FILE " Outfile1.txt" :

20

120

140

110

01

120

21

140

01

140

The Last digit from each line is the carry out.

Q.2. It is required to model in VHDL a parametrizable n-bit Array Multiplier.

(i) Describe the entity of the n-bit array multiplier using GNERIC for passing the adder

size. Note that while the multiplier inputs are n-bits each, the multiplier output is 2n

bits.

entity AMul IS

generic (	N : INTEGER := 4);

port (   A, B : IN BIT_VECTOR(N downto 1);

SUM : OUT  BIT_VECTOR(2*N downto 1));

end AMul;

(ii) Model architecture for the n-bit array multiplier using GENERATE statement. Use

the n-bit ripple carry adder modeled in Q1 in your solution.

USE WORK.HW3.ALL;

architecture Mine of AMul is

component RCA

generic(N : integer);

port (a,b    : in Bit_vector(N downto 1);

cin  : in Bit;

sum  : out Bit_vector(N downto 1);

cout : out Bit);

end component;

type  MULARRAY  is array  (N+1 downto 1) of BIT_VECTOR((2*N+1) downto 1);

signal ANDING_BITS, FIRST, SECOND : MULARRAY;

signal TEMP_CIN, TEMP_COUT : BIT_VECTOR ((N+1) downto 1);

constant SIZE : INTEGER := 2*N+1;

BEGIN

FIRST_NUMBER_BITS: FOR I IN 1 TO N generate

begin

SECOND_NUMBER_BITS: FOR J IN  1 TO N generate

begin

ANDING_BITS(I)(J+I-1) <= A(J) and B(I);

end generate;

end generate;

-- first row

FIRST(1) <= ANDING_BITS(1);

TEMP: FOR I IN 1 TO N generate

begin

SECOND(I) <= ANDING_BITS(I+1);

SUMMING: RCA generic map (SIZE) port map (FIRST(I), SECOND(I), TEMP_CIN(I), FIRST(I+1), TEMP_COUT(I));

TEMP_CIN(I+1) <= TEMP_COUT(I);

end generate;

sum <= FIRST(N+1)(2*N downto 1);

end mine;

(iii) Modify the test bench developed for the adder in Q1(v) to test the n-bit multiplier.

Assume that the input arguments will be read as integers from an input file and that

the output will be stored as integer in an output file. Use TEXTIO package for this

purpose.

entity testMul is

end;

------------------------------------------------------------------------

-- testbench for 4-bit adder

------------------------------------------------------------------------

Use work.HW3.all;

USE STD.TEXTIO.ALL;

architecture mul of testMul is

constant N : integer := 4;

signal a    : Bit_vector(N downto 1);

signal b    : Bit_vector(N downto 1);

signal product  : Bit_vector(2*N downto 1);

FOR a1: AMul USE ENTITY WORK.AMul;

begin

Process

File Infile : Text IS IN "example2.txt" ;

File Outfile: Text IS OUT "Outfile2.txt" ;

Variable Out_Line, My_Line : Line;

Variable Int_Val, Int_Value : Integer;

Variable Buf1: Bit_Vector (N Downto 1);

Variable Buf2: Bit_Vector (N Downto 1);

Begin

While Not (Endfile(Infile)) Loop

Readline( Infile, My_Line);  -- read a line from the input file

Read( My_Line, Int_Val);	         -- read a value from the line

Int2Bin (Int_Val, Buf1);

a <= Buf1;

wait for 0 ns;

wait for 0 ns;

--Readline( Infile, My_Line);  -- read a line from the input file

Read(My_Line, Int_Val);	         -- read a value from the line

Int2Bin (Int_Val, Buf2);

b <= Buf2;

wait for 0 ns;

wait for 0 ns;

wait for 100 ns;

Bin2Int (product , Int_Val);

Write( Out_Line, Int_Val);	         -- write the squared value to the line

WriteLine( Outfile, Out_Line);       -- write the line to the output file

End Loop;

wait;

End Process;

a1: AMul generic map (n)

port map ( a, b, product);

END mul;

THE INPUT FILE " example2.txt" :

15 15

9 13

8 4

12 3

6 6

1 1

15 0

11 11

13 12

10 10

THE OUTPUT FILE " Outfile2.txt" :

225

117

32

36

36

1

0

121

156

100