COE 405, Term 031

Design & Modeling of Digital Systems

HW# 5

Due date: Tuesday, Dec. 16, 2003

# It is required to model in VHDL arithmetic and logic unit (ALU) with inputs A and B and output C, that can perform any of the following functions shown below based on the three selection lines AS2, AS2, and AS0:

| AS2 AS1 AS0 | Operation |
| --- | --- |
| 000 | C=A+B |
| 001 | C=A-B |
| 010 | C=A+1 |
| 011 | C=A-1 |
| 100 | C=B |
| 101 | C=NOT A |
| 110 | C= A AND B |
| 111 | C= A OR B |

## Assume that all the inputs and outputs are of type std_logic. Model the ALU to be of generic size such that the size of the ALU is specified by a generic map.

## Simulate a 4-bit ALU to verify the correctness of your model and include simulation results.

## Synthesize a 2-bit ALU using Xilinx FPGA tools and demonstrate the functionality of your design.

# Write a VHDL description for a CMOS memory element with read/write control, enable, and a shared input-output line. When enabled and rw = 1, the output is driven by the memory. When enabled and rw = 0, the input will be written into the memory. Use qit type.

## Using this memory element, write a structural VHDL description for modeling a 2n x m bit memory array (2n rows and m columns) that has n bit address size and m bit data size. All input-output lines in a column are wired. The address and data sizes should be generic. Use an n x 2n row decoder for decoding the address.

## Simulate a 23 x 4 (i.e. 8 x 4 with 3-bit address) memory and verify its correct functionality by writing and reading from all addresses.

## Synthesize a 23 x 4 (i.e. 8 x 4 with 3-bit address) memory and verify its correct functionality using Xilinx FPGA tools.