COE 405, Term 122

Design & Modeling of Digital Systems

HW# 5   Solution

Due date: Monday, April 15

# It is required to design an unsigned 4-bit sequential multiplier. The multiplier is assumed to have an 8-bit register to hold the result, a 4-bit register to hold the multiplicand and a 3-bit counter. When reset is 1, the multiplicand, the product and counter registers are reset. When operation is started, the multiplicand register is loaded with word1 while the least significant 4-bits of the product are loaded with word2.  The block diagram and the ASMD chart of the sequential multiplier are given below. Ready signals that the unit is ready to accept a command to multiply. If word1 or word2 are 0, Empty is set to 1. Flush loads the product with 0. C_is_mx is set when the counter is equal to 3. P0 is the least significant bit of the product i.e. product[0].

## Write a Verilog model to model the data-path.

module Multiplier_DPU #(parameter word_size=4)(

output [2*word_size-1: 0] product,

output Empty, c_is_mx, p0,

input [word_size-1:0] word1, word2,

input Load_words,Flush, Add_shift, Shift, Ready, clock, reset

);

reg [word_size-1:0] multiplicand;

reg [2*word_size:0] tproduct;

reg [1:0] counter;

assign product = tproduct[2*word_size-1:0];

assign p0 = tproduct[0];

assign w1z = ~| word1;

assign w2z = ~| word2;

assign Empty = w1z | w2z;

assign c_is_mx = & counter;

always @ (posedge clock)

if (reset == 1'b1) counter <= 0;

else if (Shift || Add_shift) counter <= counter + 1;

always @ (posedge clock)

if (reset || Flush) tproduct <= 0;

else if (Load_words) begin

tproduct[word_size-1:0] <= word2;

end

else if (Shift) tproduct <= tproduct >> 1;

else if (Add_shift)

tproduct <= {tproduct[2*word_size:word_size]+{1'b0,multiplicand}, product[word_size-1:0]} >>1;

always @ (posedge clock)

if (Load_words) multiplicand <= word1;

endmodule

## Write a Verilog model to model the control unit based on the ASMD chart i.e. not based on equations.

module Multiplier_CU  (output reg Load_words,

Flush, Add_shift, Shift, Ready,

input Start, p0, c_is_mx, Empty, clock, reset);

parameter S_idle = 1'b0, S_running=1'b1;

reg state, next_state;

always @(posedge clock)

if (reset) state <= S_idle;

else state <= next_state;

always @(state, Start, p0, c_is_mx, Empty) begin

Load_words=0; Flush=0; Add_shift=0; Shift=0; Ready=0;

case (state)

S_idle: begin

Ready=1;

if (Start) begin

if (Empty) begin

next_state=S_idle; Flush=1; end

else begin

next_state=S_running; Load_words=1; end

end

else next_state=S_idle;

end

S_running:

if (p0) begin

Add_shift=1;

if (c_is_mx) next_state=S_idle;

else   next_state=S_running;

end

else begin

Shift=1;

if (c_is_mx) next_state=S_idle;

else   next_state=S_running;

end

endcase

end

endmodule

## Write a Verilog test bench to test the correctness of a 4-bit sequential multiplier.

module Multiplier #(parameter word_size=4)(

output [2*word_size-1: 0] product,

output Ready,

input  [word_size-1:0] word1, word2,

input  Start, clock, reset

);

Multiplier_CU  M1 (Load_words,Flush, Add_shift, Shift, Ready,

Start, p0, c_is_mx, Empty, clock, reset);

Multiplier_DPU M2 ( product, Empty, c_is_mx, p0, word1, word2,

Load_words, Flush, Add_shift, Shift, Ready, clock, reset);

endmodule

module t_Multiplier ();

wire [7: 0] product;

wire Ready;

reg  [3:0] word1, word2;

reg  Start, clock, reset;

Multiplier M1 (product, Ready, word1, word2, Start, clock, reset);

initial #220 $finish;

initial begin clock = 0; forever #5 clock = ~clock; end

initial fork

#10 word1 = 'd5;

#10 word2 = 'd8;

#10 reset = 0; // Power-up reset

#20 reset = 1;

#40 reset = 0;

#50 Start = 1;

#60 Start = 0;

#130 reset = 1;

#140 reset = 0;

#150 word1 = 'd8;

#150 word2 = 'd10;

#150 Start = 1;

#160 Start = 0;

join

endmodule

## Implement the 4-bit sequential multiplier using FPGA and demonstrate its correctness.

Input = 3 Output=9

Input = 5 Output=25