COE 405, Term 131

Design & Modeling of Digital Systems

HW# 5 Solution

Due date: Sunday, Dec. 8

# Consider the logic network below with inputs {a, b, c, d, e, f, g, h} and output {X}:

# Assume that the delay of a gate is related to the number of its inputs i.e. the delay of a 2-input AND gate is 2.  Also, assume that the input data-ready times are zero for all inputs.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path(s).

## Suggest an implementation of the function X to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# It is required to design a circuit to compute the equation Y=A+B+C+D+E+F using only two adders. Assume that the inputs will hold their values until the end of the operation. Also, assume that the inputs will be ready when a Start input is asserted and a Done signal will be set when the result is ready.

## Show a schedule with minimum latency (i.e., clock cycles) satisfying the area constraints.

## Show the DataPath design of your circuit.

## Show the ASMD diagram of your control unit.

## Model the DataPath and Control units in Verilog and verify the correctness of your model.

module ADD6 #(parameter n=4)(output done, output [n+1:0] Y,

input [n-1:0] A, B, C, D, E, F, input start, clk, reset);

DPADD6  M1 (Y, A, B, C, D, E, F, MS1, MS2, MS3, MS4, R1E, R2E, clk, reset);

CUADD6  M2 (done, MS1, MS2, MS3, MS4, R1E, R2E, start, clk, reset);

endmodule

module DPADD6 #(parameter n=4)

(output [n+1:0] Y, input [n-1:0] A, B, C, D, E, F,

input MS1, MS2, MS3, MS4, R1E, R2E, clk, reset);

reg [n+1:0] R1, R2;

wire [n+1:0] Mux1, Mux2, Mux3, Mux4, add1, add2;

assign Mux1 = MS1?E:C;

assign Mux2 = MS2?F:D;

assign Mux3 = MS3?R1:A;

assign Mux4 = MS4?R2:B;

assign add2 = Mux1 + Mux2;

assign add1 = Mux3 + Mux4;

assign Y = add1;

always @ (posedge clk, posedge reset) begin

if (reset) begin

R1 <= 0; R2 <= 0;

end

else begin

if (R1E)

R1 <= add1;

if (R2E)

R2 <= add2;

end

end

endmodule

module CUADD6 (output reg done, MS1, MS2, MS3, MS4, R1E, R2E,

input start, clk, reset);

parameter S0 = 2'b00, S1=2'b01, S2=2'b10;

reg [1:0] state, next_state;

always @(posedge clk, posedge reset)

if (reset) state <= S0;

else state <= next_state;

always @(state, start) begin

done=0; MS1=0; MS2=0; MS3=0; MS4=0; R1E=0; R2E=0;

case (state)

S0:

if (start)  begin

next_state=S1; R1E=1; R2E=1; end

else next_state=S0;

S1: begin

MS1=1; MS2=1; MS3=1; MS4=1; R1E=1; R2E=1;

next_state=S2;

end

S2: begin

done=1; MS3=1; MS4=1;

next_state=S0;

end

default: begin

done='bx; MS1='bx; MS2='bx; MS3='bx; MS4='bx; R1E='bx; R2E='bx;

next_state='bx;

end

endcase

end

endmodule

To verify the correctness of the design, we add the numbers 1, 2, 3, 4, 5, and 6 and it is evident from simulation results we get the correct output in the third clock cycle at Y=21.