COE 405, Term 152

Design & Modeling of Digital Systems

HW# 6

Due date: Sunday, April 17

# It is required to design a circuit that computes the average, maximum and minimum of a number of scores N (assuming 0<N≤15), each score with a value in the range [0,15].  Once a user presses a Start button, the number of scores N will be entered. Then, scores will be entered in subsequent clock cycles one score at a time. Once the circuit finishes computation, it will assert a Done signal and will generate the average, maximum and minimum scores. The average will be shown as an integer number resulting from dividing the sum by N with rounding the result to the nearest integer. The Done signal will remain asserted unless the user presses a Reset button.

# Develop an ASMD chart for the circuit.

# Show the design of your data path unit. Write a Verilog module to model your data path.

# Write a Behavioral Verilog module to model the ASMD chart of your circuit.

# Write a test bench to verify the correct functionality of your circuit. Show snapshots of your simulation to demonstrate its correctness.

# Implement your circuit on FPGA and demonstrate its correct functionality. Include a link for a video snapshot to demonstrate correct functionality of your circuit on FPGA.

This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a word file that contains the following items:

#### Your name and ID

#### Assignment number

#### Problem statement

#### Your solution

#### Include snapshots of simulation output to illustrate the correctness of your models.