COE 405, Term 152

Design & Modeling of Digital Systems

HW# 7  Solution

Due date: Sunday, May 1

# Consider the logic network below with inputs {a, b, c, d, e} and output {k}:

# Assume that the delay of the inverter gate is 1 and that the delay of the 2-input NAND gate is 2.  Also, assume that the input data-ready times are zero except for input a, which is equal to 2.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function k using only inverters and 2-input NAND gates to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# It is required to design a circuit to compute the equation Y=A+B-C-D, where A, B, C and D are N-bit inputs. Assume that inputs are available only during the first cycle when a START input is asserted.  Assume that a DONE signal will be set when the result is ready and the result will remain held until the next Start operation.

## Show a schedule of the operations with minimum latency (i.e., clock cycles) assuming that the clock cycle is limited by the time for performing one addition/subtraction operation. Store the output Y in a register.

## Show the Data Path design of your circuit indicating all the control signals and the used adder/subtractor sizes.

## Show the ASMD diagram of your control unit.

## Write the necessary Verilog modules to module the data path unit, control unit and the overall circuit.

module HW7 #(parameter N=4) (output [N:0] Y, output DONE, input [N-1:0] A, B, C, D, input START, RESET, CLK);

HW7_DPU #(N) M1 ( Y, A, B, C, D, SEL, R1IN, R2IN, CIN,  CLK);

HW7_CU M2 (SEL, R1IN, R2IN, CIN, DONE, START, RESET, CLK);

endmodule

module HW7_DPU #(parameter N=4) (output [N:0] Y, input [N-1:0] A, B, C, D, input SEL, R1IN, R2IN, CIN,  CLK);

reg [N:0] R1, R2;

wire [N:0] MUX1, MUX2;

assign MUX1 = SEL? R1 : A;

assign MUX2 = SEL? ~{1'b0,R2} : B;

assign Y = R1;

always @(posedge CLK) begin

if (R1IN)

R1 = MUX1 + MUX2 + CIN;

if (R2IN)

R2 = C + D;

end

endmodule;

module HW7_CU (output reg SEL, R1IN, R2IN, CIN, DONE, input START, RESET, CLK);

parameter S0 = 2'b00, S1=2'b01, S2=2'b10;

reg [2:0] state, next_state;

always @(posedge CLK, posedge RESET)

if (RESET) state <= S0;

else state <= next_state;

always @(state, START) begin

SEL=0; R1IN=0; R2IN=0; CIN=0; DONE=0;

case (state)

S0:

if (START)  begin

next_state=S1; R1IN=1; R2IN=1; end

else next_state=S0;

S1: begin SEL=1; CIN=1; R1IN=1; next_state=S2; end

S2: begin DONE=1;

if (START)  begin

next_state=S1; R1IN=1; R2IN=1; end

else next_state=S2;

end

default: next_state='bx;

endcase

end

endmodule

## Write a test bench to test the correct operation of your circuit. Include simulation snapshots.

module HW7_Test();

wire [4:0] Y;

wire DONE;

reg  [3:0] A, B, C, D;

reg  START, RESET, CLK;

HW7 #(4) M1 ( Y,  DONE, A, B, C, D, START, RESET, CLK);

initial begin

CLK = 0;

forever

#50 CLK = ~ CLK;

end

initial begin

RESET=1;

#100 RESET=0; START=1; A=15; B=15; C=1; D=2;

#100 START=0;

end

endmodule

## Implement your circuit on FPGA assuming N=2 bits. Include a link for a video snapshot to demonstrate correct functionality of your circuit.