Name:									Id#

COE 405, Term 152

Design & Modeling of Digital Systems

Quiz# 1

Date: Thursday, Feb. 11, 2016

# Assume that the area and delay of a gate is related to the number of its inputs i.e., a 2-input AND gate has an area and delay = 2. Consider the given circuit below implementing the function F:

# Determine the area and maximum delay of this circuit.

# Provide an implementation of this function with an improved delay and determine its area and maximum delay.

# Consider the function:

# Compute the expansion of using the Orthonormal Basis {(1=, (2=, (3=, (4=}.

# Compute the functionutilizing the orthonormal based expansion of the function.

# It is required to design a combinational circuit that computes the equation Z=2X + Y - 1, where X and Y are n-bit signed 2's complement numbers.

## Design the circuit as a modular iterative circuit where each module receives a single bit of the inputs, Xi and Yi.

## Derive the truth table of your 1-bit module in (i).