Name: KEY									Id#

COE 405, Term 031

Design & Modeling of Digital Systems

Quiz# 2

Date: Sunday, Nov. 2, 2003

# It is required to design a 3-bit register that has the capability to count up, count down, shift left logically, or shift right logically based on a 2-input select. The interface description of the 3-bit register is shown below, where sel determines the operation. When sel=00, the register will count up, when sel=01, it will count down, when sel=10, it will shift left logically, and when sel =11, it will shift right logically. The reset is an asynchronous reset and the register is rising-edge triggered.

## Describe an Entity CS3 for the 3-bit register using type BIT and BIT_VECTOR for the interface signals.

Entity CS3 IS

PORT (reset, clk: IN BIT; sel: IN BIT_VECTOR(1 downto 0); C: OUT Bit_Vector(2 Downto 0));

Constant limit: INTEGER :=7;

END CS3 ;

## Model a behavioral Architecture Behave for this 3-bit register.

Architecture Behave OF CS3 IS

Begin

Process(clk, reset)

Variable count: INTEGER := 0;

Begin

IF reset = '1' THEN 	count := 0;

ELSIF (clk = '1' AND clk'Event ) THEN

CASE sel is

when "00" => count := count+1;

when "01" => count := count-1;

when "10" => count := count*2;

when "11" => count := count/2;

END case;

IF (count > limit) Then count := count-limit-1;

ELSIF count= -1 Then count := limit;

END IF;

END IF;

Case count is

when 0 => c <= "000";

when 1 => c <= "001";

when 2 => c <= "010";

when 3 => c <= "011";

when 4 => c <= "100";

when 5 => c <= "101";

when 6 => c <= "110";

when 7 => c <= "111";

when others => c <= "000";

End Case;

END process;

END Behave ;

# Given the following signal assignments, show all transactions placed on each signal. At each event, show transactions that are appended, overwritten, and expired including those occurring at delta time. Show resulting waveforms on each signal.

Architecture dataflow of signals IS

Signal A, B, C, D: Bit := ‘0’;

Begin

A <= ‘1’ after 10 ns, ‘0’ after 13 ns, ‘1’ after 17 ns, ‘0’ after 25 ns, ‘1’ after 26 ns;

B <= transport A after 5 ns;

C <= A after 5 ns;

D <= Reject 2 ns Inertial A after 5 ns;

End dataflow;

|  |  | 0ns | 5ns | 10ns | 13ns | 15ns | 17ns | 18ns | 22ns | 25ns | 26ns | 30ns | 31ns |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | Current Value | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 |
|  | Projected Waveform | (1,10) (0,13) (1,17) (0,25) (1,26) | (1,5) (0,8) (1,12) (0,20) (1,21) | (0,3) (1,7) (0,15) (1,16) | (1,4) (0,12) (1,13) | (1,2) (0,10) (1,11) | (0,8) (1,9) | (0,7) (1,8) | (0,3) (1,4) | (1,1) |  |  |  |
| B | Current Value | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 |
|  | Projected Waveform | (0,5) |  | (1,5) | (1,2) (0,5) | (0,3) | (0,1) (1,5) | (1,4) |  | (0,5) | (0,4) (1,5) | (1,1) |  |
| C | Current Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 |
|  | Projected Waveform | (0,5) |  | (1,5) | (1,2) (0,5) | (0,3) | (0,1) (1,5) | (1,4) |  | (0,5) | (0,4) (1,5) | (1,1) |  |
| D | Current Value | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 |
|  | Projected Waveform | (0,5) |  | (1,5) | (1,2) (0,5) | (0,3) | (0,1) (1,5) | (1,4) |  | (0,5) | (0,4) (1,5) | (1,1) |  |

# Text boxes

clk

Sel1Sel0

reset

C2-C0

3-bit Special Register