Name:									Id#

COE 405, Term 181

Design & Modeling of Digital Systems

Quiz# 2 Solution

Date: Sunday, October 7, 2018

# The circuit given below is a 3-bit adder/subtractor. The circuit performs addition when OP=0 and performs subtraction otherwise.

## Write a Verilog model to model a 1-bit cell design of the circuit using either primitive gates or assign statement.

module addsubcell (output cout, sum, input a, b, cin, op);

assign op2 = b ^ op;

assign p = a ^ op2;

assign g = a & op2;

assign sum = p ^ cin;

assign cout = g | p & cin;

endmodule

## Write a parametrizable Verilog model for modeling an n-bit adder/subtractor circuit using generate loop construct.

module addsub #( parameter n = 3)

(output cout, output [n-1:0] sum,

input  [n-1:0] a, b, input op);

wire [n:0] carry;

assign carry[0] = op;

assign cout = carry[n];

genvar i;

for ( i = 0; i < n; i = i+1 ) begin : ripple

addsubcell AS(carry[i+1], sum[i], a[i], b[i], carry[i], op);

end

endmodule

## Write a test bench that instantiates and tests a 3-bit adder/subtractor circuit by applying the following input patterns to your circuit with a delay of 30 unit delays between successive input patterns: {(A=1, B=5, OP=0), {(A=1, B=5, OP=1), (A=7, B=7, OP=0), (A=0, B=7, OP=1)}.

module t_addsub();

wire 	[2:0] sum;

reg 	[2:0] a, b;

reg   op;

addsub M1 (cout, sum, a, b, op);

initial begin

a=3'b001; b=3'b101; op=1'b0;

#30	op=1;

#30	a=3'b111; b=3'b111; op=1'b0;

#30	a=3'b000; b=3'b111; op=1'b1;

end

endmodule