Name:									Id#

COE 405, Term 031

Design & Modeling of Digital Systems

Quiz# 3

Date: Sunday, Nov. 30, 2003

# It is required to model in VHDL a parametrizable n-bit Shift Right Register. The register has a shift control input that when enabled it makes the register shift its content to the right. Assume that the value shifted to the most significant bit is taken from the input SI.  Otherwise, the register will be loaded by an external input DI. Assume that register is rising-edge triggered and that it has an Asynchronous reset. Assume that you have the following SFF entity in the work library. Assume that SFF is rising-edge triggered and that its reset is Asynchronous. When shift=0, the SFF is loaded with din otherwise it is loaded with si.

Entity SFF IS

PORT (din, si, shift, reset, clk: IN BIT; qout: OUT BIT);

END SFFf;

## Describe the entity of the n-bit shift register using GNERIC for passing the shift register size.

## Model architecture for the n-bit shift register using GENERATE statement.

# Text boxes

din

dff_in

qout

clk

reset

1C

1D

Q

1R

si

shift

S1

Z

0D

1D