Name:									Id#

COE 405, Term 131

Design & Modeling of Digital Systems

Quiz# 3

Date: Thursday, Nov. 28, 2013

# It is required to model an n-bit iterative magnitude comparator. A 4-bit comparator is shown below:

## The model for a 1-bit comparator is as follows:

## Write a parametrizable Verilog model for modeling an n-bit comparator with a default of n=4.

# The ASMD chart given below describes a state machine that counts 1’s in a word and terminates activity as soon as possible. The machine remains in its reset state, S_idle, until an external agent asserts start. This action asserts the output, load_temp, which will cause data to be loaded into register temp when the state makes a transition to S_counting at the next active edge of clk. The machine remains in S_counting while temp contains a 1. Two actions occur concurrently at each subsequent clock: (1) temp is shifted towards its LSB and (2) temp[0] is added to bit_count. When temp finally has a 1 in only the LSB, the machine’s state moves to S_waiting, where done is asserted. The state remains in S_waiting until start is reasserted. Assume that when the synchrnous reset input is asserted the machine is reset to the state  S_idle and bit_count and temp are initialized to 0.

## Write a Verilog model for modeling the data-path unit.

## Write a Verilog model for modeling the control unit using the following state assignment: S_idle=00, S_counting =01, and S_waiting=10.