Name: KEY									Id#

COE 405, Term 122

Design & Modeling of Digital Systems

Quiz# 3

Date: Monday, March 15, 2013

# The ASMD chart given below describes a state machine that counts 1’s in a word and terminates activity as soon as possible. The machine remains in its reset state, S_idle, until an external agent asserts start. This action asserts the output, load_temp, which will cause data to be loaded into register temp when the state makes a transition to S_counting at the next active edge of clk. The machine remains in S_counting while temp contains a 1. Two actions occur concurrently at each subsequent clock: (1) temp is shifted towards its LSB and (2) temp[0] is added to bit_count. When temp finally has a 1 in only the LSB, the machine’s state moves to S_waiting, where done is asserted. The state remains in S_waiting until start is reasserted. Assume that when the synchrnous reset input is asserted the machine is reset to the state  S_idle and bit_count and temp are initialized to 0.

## Write a Verilog model to model the data-path.

module OnesCount_DPU #(parameter word_size=4, counter_size=3)(

output [counter_size-1: 0] bit_count,

output temp_gt_1,

input [word_size-1:0] data,

input load_temp, shift_add, clear, clock, reset

);

reg [word_size-1:0] temp;

reg [counter_size-1:0] counter;

assign bit_count = counter;

assign temp_gt_1 = | temp[word_size-1:1];

always @ (posedge clock)

if (load_temp) temp <= data;

else if (shift_add) temp <= temp >> 1;

always @ (posedge clock)

if (reset || clear) counter <= 0;

else if (shift_add) counter <= counter + temp[0];

endmodule

## Write a Verilog model to model the control unit based on the ASMD chart i.e. not based on equations.

module OnesCount_CU  (output reg load_temp,

shift_add, clear, done, busy,

input start, temp_gt_1, clock, reset);

parameter S_idle = 2'b00, S_counting = 2'b01, S_waiting = 2'b10;

reg [1:0] state, next_state;

always @(posedge clock)

if (reset) state <= S_idle;

else state <= next_state;

always @(state, start, temp_gt_1) begin

load_temp=0; shift_add=0; clear=0; done=0; busy=0;

case (state)

S_idle:

if (start) begin

load_temp = 1;

next_state = S_counting;

end

else next_state = S_idle;

S_counting: begin

shift_add = 1; busy = 1;

if (temp_gt_1) next_state = S_counting;

else   next_state = S_waiting;

end

S_waiting:  begin

done = 1;

if (start) begin

load_temp = 1;  clear = 1;

next_state = S_counting;

end

else next_state = S_waiting;

end

default: begin

next_state = 2'bxx;

load_temp='bx; shift_add='bx; clear='bx; done='bx; busy='bx;

end

endcase

end

endmodule

## Write a Verilog model to model the whole design.

module OnesCount #(parameter word_size=4, counter_size=3)(

output [counter_size-1: 0] bit_count,

output done, busy,

input  [word_size-1:0] data,

input  start, clock, reset

);

OnesCount_CU  M1 (load_temp,shift_add, clear, done, busy, start, temp_gt_1, clock, reset);

OnesCount_DPU M2 (bit_count, temp_gt_1, data, load_temp, shift_add, clear, clock, reset);

endmodule