Name:									Id#

COE 405, Term 122

Design & Modeling of Digital Systems

Quiz# 4

Date: Monday, April 29, 2013

# Consider the logic network below with inputs {a, b, c, d, e, f} and output {X}:

# Assume that the delay of a gate is related to the number of its inputs i.e. the delay of a 2-input AND gate is 2.  Also, assume that the input data-ready times are zero for all inputs except input a, which has a data-ready time of 2.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function X to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# Determine possible circuits that will be synthesize by each of the following modules:

- module m1  (output y, input e1, e2, x1, x2);

assign y = e1?x1:e2?x2:y;

endmodule

- module m2  (output y, input e1, e2, x1, x2);

assign y = e1?x1:e2?x2:1’bx;

endmodule

- module m3 #(parameter size=2)(

output  reg y,

input [size-1:0] a, b );

integer k;

always @ (a, b) begin

for (k=size-1; k>=0; k=k-1) begin

if (a[k] != b[k])

y = 0;

end

end

endmodule

- module m4 #(parameter size=3)(

output  reg y,

input [size-1:0] x );

always @ (x) begin

y = 0;

if (x[0]) y=1;

else if (x[1]) y=1;

else if (x[2]) y=1;

end

endmodule

- module m5 #(parameter size=3)(

output  reg y,

input [size-1:0] x );

integer k;

always @ (x) begin

y = 1;

for (k=1; k<size; k=k+1)

y = y & x[k];

if (!x[0]) y = 1'bz;

end

endmodule

- module m6 (

output  reg y,

input x1, x2, x3);

always @ (x1, x2, x3) begin

if (x1) y = x2 ^ x3;

end

endmodule