Name:									Id#

COE 405, Term 162

Design & Modeling of Digital Systems

Quiz# 4  Solution

Date: Tuesday, May 1, 2017

# Q1. It is required to design an n-bit signed multiplier circuit. The architecture and the algorithm for performing signed multiplication are given below:

## Write a parametrizable Verilog module to model the signed multiplication circuit as a combinational circuit using for loop.

module MULC #(parameter N=4) (output reg [N-1:0] HI, LO, input [N-1:0] A, B);

integer i;

reg [N-1:0] C;

reg OVF, Sign;

always @(A, B) begin

HI = 0;  LO = B;

for (i=0; i<N; i=i+1) begin

if( LO[0] ) begin

if ( i==N-1 ) begin

C = HI - A;

OVF = (HI[N-1] ^ A[N-1]) & (HI[N-1]^C[N-1]);

end

else begin

C = HI + A;

OVF = (HI[N-1] ~^ A[N-1]) & (HI[N-1]^C[N-1]);

end

Sign = OVF ^ C[N-1];

HI = C;

end

else Sign = HI[N-1];

{HI, LO} = {Sign, HI,  LO[N-1:1]};

end

end

endmodule