Name:									Id#

COE 405, Term 181

Design & Modeling of Digital Systems

Quiz# 6

Date: Sunday, Dec. 9, 2018

# Fill in the blank in each of the following questions:

## Three advantages of using FPGAs over ASICs are ___________________________ ____________________________________________________________________.

## Two types of FPGA technologies are ______________________________________ ____________________________________________________________________.

## In FPGAs, each configurable logic block (CLB) has a number of the following two main blocks: _________________________________________________________.

## Each IOB can be configured to work as ________________ or ________________.

## Modern FPGAs, in addition to having CLBs and IOBs, have the following components: _________________________________________________________.

## In FPGAs, memory can be implemented in two ways either as ___________________ _________________ or using ____________________________________________.

## The difference between simple dual port and true dual port RAM is that __________ _____________________________________________________________________ ____________________________________________________________________.

## To have a RAM with synchronous read, the RAM must be implemented using ____________________________________________________________________.

## Using a Block RAM with Read_First write mode means that when the memory is written it will _________________________________________________________.

## Using a Block RAM with No_Change write mode means that when the memory is written it will _________________________________________________________.

# Write a parametrizable Verilog model for modeling a memory with a simple dual port memory with synchronous read and write by completing the following module:

module Memory_Unit#(parameter word_size=8, address_size=8, memory_size=256)(

output  reg [word_size-1:0] data_out1,

output reg [word_size-1:0] data_out2,

input [word_size-1:0] data_in,

input [address_size-1:0] address1,

input [address_size-1:0] address2,

input clk, write);

# Consider the logic network defined by the following expression:

# x = a b d' e' + a' c' d' e' + a b' d + a b' e + a' c d + a' c e

## Compute the weight of the double cube divisors d1 = a b + a' c' and d2 = d + e. Extract the double cube divisor with the highest weight and show the resulting network after extraction and the number of literals saved.