COE 561, Term 061

Digital System Design and Synthesis

HW# 1

Due date: Sunday, Oct. 29

# Consider the following circuit shown below:

# Find the set of all test vectors that detect the fault h stuck-at-1.

# Consider the following OBDD with the variable ordering {a, b, c, d}. Reduce it based on Reduce function to obtain the ROBDD. Show the details of your work.

# Consider the function f=a3b3’ + (a3’(b3) a2b2’ + (a3’(b3)(a2’(b2)a1b1’

## Implement the function f using 2x1 Multiplexers. Minimize the number of multiplexers used.

## Implement the function f using 4x1 Multiplexers. Minimize the number of multiplexers used.

## Draw the ROBDD for the function f using the variable order {a1, b1, a2, b2, a3, b3}. Is this the best ordering used? If not suggest a better ordering and show its ROBDD.

# Consider the two functions f=a(b(c and g=ac+a’b’+bc’.

## Compute the following functions: f . g, f + g, and f (g.

## Draw the ITE DAG for the function f (g. Show the details of the ITE algorithm step by step.

# Consider the following given matrix representing a covering problem:

## Find a minimum cover using EXACT_COVER procedure. Show the details of the algorithm.