Term 051

COE 561 Digital System Design and Synthesis

HW# 5

Due date: Sunday, Dec. 18

# Consider the logic network defined by the following expressions:

# k =(i . j)’

# j =(d .h)’

# i =(f .e)’

# h =(g)’

# g =(c .f)’

# f =(a .b)’

# Inputs are {a, b, c, d, e} and output is {k}.  Assume that the delay of inverter gate is 1 and that the delay of the 2-input NAND gate is 2.  Also, assume that the input data-ready times are zero except for input a which is equal to 2.

## Draw the logic network graph and compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function k to reduce the delay of the circuit and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# Determine the number of ROBDDs required to be stored for each of the following library cells for Boolean matching. Justify your answer.

## F = a b + b’ c.

## F = a b + c d.

## F = a b + c’ d’.

# Consider a library containing the following cells:

| Cell | Area Cost |
| --- | --- |
| INV | 1 |
| NAND2 | 2 |
| AND2 | 2.5 |
| NOR2 | 2 |
| OR2 | 2.5 |
| AOI21 | 4 |
| AOI22 | 4.5 |

Assume that you have the following network:

i = d’;		j = e’;		k = h’;

l = a b;	m = l + c;	n = i + j;

o = f +g;	p = m +  n;	q = o + k;	r = p  q;

## Decompose the given network using the base cells NAND2 and INV.

## Find a minimal cover (in terms of area) based on the given library for each subject graph using dynamic programming approach. Pattern strings for the library cells are given in Fig. 10.8.

## Using the given library, use the sis command read_libray to read the library. Then, map the network to the library using the sis command map –s –m 0. Compare your solution to the solutions obtained in (iv) & (v). You can save the mapped circuit using the sis command write_blif –n.