## Slide 1: Introduction to Verilog
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Hardware Description Language
Logic Simulation versus Synthesis
Verilog Module
Gate-Level Description and Gate Delays
Module Instantiation
Continuous Assignment
Writing a Simple Test Bench

## Slide 3: Hardware Description Language
Describes the hardware of digital systems in a textual form
Describes the hardware structures and behavior
Can represent logic diagrams, expressions, and complex circuits
NOT a software programming language
Two standard hardware description languages (HDLs)
Verilog (will be studied in this course)
VHDL (harder to learn than Verilog)

## Slide 4: Verilog = "Verifying Logic"
Invented as a simulation language in 1984 by Phil Moorby
Opened to public in 1990 by Cadence Design Systems
Became an IEEE standard in 1995 (Verilog-95)
Revised and upgraded in 2001 (Verilog-2001)
Revised also in 2005 (Verilog-2005)
Verilog allows designers to describe hardware at different levels
  Can describe anything from a single gate to a full computer system
Verilog is supported by the majority of electronic design tools
Verilog can be used for logic simulation and synthesis

## Slide 5: Logic Simulation
Logic simulator interprets the Verilog (HDL) description
Produces timing diagrams
Predicts how the hardware will behave before it is fabricated
Simulation allows the detection of functional errors in a design
  Without having to physically implement the circuit
Errors detected during the simulation can be corrected
  By modifying the appropriate statements in the Verilog description
Simulating and verifying a design requires a test bench
The test bench is also written in Verilog

## Slide 6: Logic Synthesis
Logic synthesis is similar to translating a program
However, the output of logic synthesis is a digital circuit
A digital circuit modeled in Verilog can be translated into a list of components and their interconnections, called netlist
Synthesis can be used to fabricate an integrated circuit
Synthesis can also target a Field Programmable Gate Array
  An FPGA chip can be configured to implement a digital circuit
  The digital circuit can also be modified by reconfiguring the FPGA
Logic simulation and synthesis are automated
  Using special software, called Electronic Design Automation (EDA) tools

## Slide 7: Verilog Module
A digital circuit is described in Verilog as a set of modules
A module is the design entity in Verilog
A module is declared using the module keyword
A module is terminated using the endmodule keyword
A module has a name and a list of input and output ports
A module is described by a group of statements
The statements can describe the module structure or behavior

## Slide 8: Example of a Module in Verilog
// Description of a simple circuit
module simple_circuit(input A, B, C, output x, y);
wire w;
and g1(w, A, B);
not g2(y, C);
or g3(x, w, y);
endmodule
The input keyword defines the input ports: A, B, C
The output keyword defines the output ports: x, y
The wire keyword defines an internal connection: w
The structure of simple_circuit is defined by three gates: and, not, or
Each gate has an optional name, followed by the gate output then inputs
A
B
C
w
x
y
g1
g2
g3
Order is not
important

## Slide 9: Verilog Syntax
Keywords: have special meaning in Verilog
Many keywords: module, input, output, wire, and, or, etc.
Keywords cannot be used as identifiers
Identifiers: are user-defined names for modules, ports, etc.
Verilog is case-sensitive: A and a are different names
Comments: can be specified in two ways (similar to C)
  Single-line comments begin with // and terminate at end of line
  Multi-line comments are enclosed between /* and */
White space: space, tab, newline can be used freely in Verilog
Operators: operate on variables (similar to C: ~ & | ^ + - etc.)

## Slide 10: Basic Gates
Basic gates: and, nand, or, nor, xor, xnor, not, buf
Verilog define these gates as keywords
Each gate has an optional name
Each gate has an output (listed first) and one or more inputs
The not and buf gates can have only one input
Examples:
and g1(x,a,b); // 2-input and gate named g1
or g2(y,a,b,c); // 3-input or gate named g2
nor g3(z,a,b,c,d); // 4-input nor gate named g3
inputs
output
name

## Slide 11: Modeling a Half Adder
A half adder adds two bits: a and b
Two output bits:
Carry bit: cout = a · b
Sum bit: sum = a  b
module Half_Adder(a, b, cout, sum);
input a, b;
output sum, cout;
and (cout, a, b);
xor (sum, a, b);
endmodule
a b | cout | sum
0 0 | 0 | 0
0 1 | 0 | 1
1 0 | 0 | 1
1 1 | 1 | 0
Truth Table
Verilog-95
Syntax
b
a
cout
sum
Half_Adder

## Slide 12: Full Adder
Full adder adds 3 bits: a, b, and c
Two output bits:
Carry bit: cout
Sum bit: sum
Sum bit is 1 if the number of 1's in the input is odd (odd function)
sum = (a  b)  c
Carry bit is 1 if the number of 1's in the input is 2 or 3
cout = a·b + (a  b)·c
a b c | cout | sum
0 0 0 | 0 | 0
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 1
Truth Table

## Slide 13: Full Adder Module
module Full_Adder(input a, b, c, output cout, sum);
wire w1, w2, w3;
and (w1, a, b);
xor (w2, a, b);
and (w3, w2, c);
xor (sum, w2, c);
or (cout, w1, w3)
endmodule
a
b
c
sum
cout
w1
w2
w3
Full_Adder

## Slide 14: Gate Delays
When simulating Verilog modules, it is sometime necessary to specify the delay of gates using the # symbol
The `timescale directive specifies the time unit and precision
timescale is also used as a simulator option
`timescale 1ns/100ps
module Half_Adder(input a, b, output cout, sum);
and #2 (cout, a, b); // gate delay = 2ns
xor #3 (sum, a, b); // gate delay = 3ns
endmodule
Time unit = 1ns = 10-9 sec
Precision = 100ps = 0.1ns

## Slide 15: Full Adder Module with Gate Delay
module Full_Adder(input a, b, c, output cout, sum);
wire w1, w2, w3;
and #2 (w1, a, b);
xor #3 (w2, a, b);
and #2 (w3, w2, c);
xor #3 (sum, w2, c);
or #2 (cout, w1, w3)
endmodule
a
b
c
sum
cout
w1
w2
w3
Full_Adder

## Slide 16: Continuous Assignment
The assign statement defines continuous assignment
Syntax: assign name = expression;
Assigns expression value to name (output port or wire)
Examples:
assign x = a&b | c&~d; // x = ab + cd'
assign y = (a|b) & ~c; // y = (a+b)c'
assign z = ~(a|b|c); // z = (a+b+c)'
assign sum = (a^b) ^ c; // sum = (a  b)  c
Verilog uses the bit operators: ~ (not), & (and), | (or), ^ (xor)
Operator precedence: (parentheses), ~ , & , | , ^

## Slide 17: Continuous Assignment with Delay
Syntax: assign #delay name = expression;
The optional #delay specifies the delay of the assignment
To have a delay similar to the gate implementation
module Full_Adder (input a, b, c, output cout, sum);
assign #6 sum = (a^b)^c; // delay = 6
assign #7 cout = a&b | (a^b)&c; // delay = 7
endmodule
The order of the assign statements does not matter
They are sensitive to inputs (a, b, c) that appear in the expressions
Any change in value of the input ports (a, b, c) will re-evaluate the outputs sum and cout of the assign statements

## Slide 18: Test Bench
In order to simulate a circuit, it is necessary to apply inputs to the circuit for the simulator to generate an output response
A test bench is written to verify the correctness of a design
A test bench is written as a Verilog module with no ports
It instantiates the module that should be tested
It provides inputs to the module that should be tested
Test benches can be complex and lengthy, depending on the complexity of the design

## Slide 19: Example of a Simple Test Bench
module Test_Full_Adder; // No need for Ports
reg a, b, c; // variable inputs
wire sum, cout; // wire outputs
// Instantiate the module to be tested
Full_Adder FA (a, b, c, cout, sum);
initial begin // initial block
a=0; b=0; c=0; // at t=0 time units
#20 a=1; b=1; // at t=20 time units
#20 a=0; b=0; c=1; // at t=40 time units
#20 a=1; c=0; // at t=60 time units
#20 $finish; // at t=80 finish simulation
end // end of initial block
endmodule

## Slide 20: Difference Between wire and reg
Verilog has two major data types
Net data types: are connections between parts of a design
Variable data types: can store data values
The wire is a net data type
  A wire cannot store a value
  Its value is determined by its driver, such as a gate, a module output, or continuous assignment
The reg is a variable data type
  Can store a value from one assignment to the next
  Used only in procedural blocks, such as the initial block

## Slide 21: The initial Statement
The initial statement is a procedural block of statements
The body of the initial statement surrounded by begin-end is sequential, like a sequential block in a programming language
Procedural assignments are used inside the initial block
Procedural assignment statements are executed in sequence
Syntax: #delay variable = expression;
Procedural assignment statements can be delayed
The optional #delay indicates that the variable (of reg type) should be updated after the time delay

## Slide 22: Running the Simulator
Examine the waveforms to verify the correctness of your design
At t = 0 ns, the values of cout and sum are unknown (shown in red)
The cout and sum signals are delayed by 7ns and 6ns, respectively

## Slide 23: Modular Design: 4-bit Adder
Uses identical copies of a full adder to build a large adder
Simple to implement: the cell (iterative block) is a full adder
Carry-out of cell i becomes carry-in to cell (i +1)
Can be extended to add any number of bits
c0
Full
Adder
a0
b0
s0
c1
Full
Adder
a1
b1
s1
c2
Full
Adder
a2
b2
s2
c3
Full
Adder
a3
b3
s3
c4

## Slide 24: 4-bit Adder using Module Instantiation
module Adder4 (input a0, a1, a2, a3, b0, b1, b2, b3, c0,
output s0, s1, s2, s3, c4
);
wire c1, c2, c3; // Internal wires for the carries
// Instantiate Four Full Adders: FA0, FA1, FA2, FA3
// The ports are matched by position
Full_Adder FA0 (a0, b0, c0, c1, s0);
Full_Adder FA1 (a1, b1, c1, c2, s1);
Full_Adder FA2 (a2, b2, c2, c3, s2);
Full_Adder FA3 (a3, b3, c3, c4, s3);
// Can also match the ports by name
// Full Adder FA0 (.a(a0), .b(b0), .c(c0), .cout(c1), .sum(s0));
endmodule

## Slide 25: Module Instantiation
Module declarations are like templates
Module instantiation is like creating an object
Modules are instantiated inside other modules at different levels
The top-level module does not require instantiation
Module instantiation defines the structure of a digital design
It produces module instances at different levels
The ports of a module instance must match those declared
The matching of the ports can be done by name or by position

## Slide 26: Writing a Test Bench for the 4-bit Adder
module Adder4_TestBench; // No Ports
reg a0, a1, a2, a3; // variable inputs
reg b0, b1, b2, b3, cin; // variable inputs
wire s0, s1, s2, s3, cout; // wire outputs
// Instantiate the module to be tested
Adder4 Add4 (a0,a1,a2,a3, b0,b1,b2,b3, cin, s0,s1,s2,s3, cout);
initial begin // initial block
a0=0;a1=0;a2=0;a3=0; // at t=0
b0=0;b1=0;b2=0;b3=0;cin=0; // at t=0
#100 a1=1;a3=1;b2=1;b3=1; // at t=100
#100 a0=1;a1=0;b1=1;b2=0; // at t=200
#100 a2=1;a3=0;cin=1; // at t=300
#100 $finish; // at t=400 finish simulation
end // end of initial block
endmodule