## Slide 1: Arithmetic Circuits
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Ripple-Carry Adder
Magnitude Comparator
Design by Contraction
Signed Numbers
Addition/Subtraction of Signed 2's Complement

## Slide 3: Binary Addition
Start with the least significant bit (rightmost bit)
Add each pair of bits
Include the carry in the addition
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
+
(54)
(29)
(83)
1
carry
0
1
2
3
4
bit position:
5
6
7
1
1
1
0
1
0
1
0
0
1
1

## Slide 4: Iterative Design: Ripple Carry Adder
Uses identical copies of a full adder to build a large adder
Simple to implement: can be extended to add any number of bits
The cell (iterative block) is a full adder
Adds 3 bits: ai, bi, ci, Computes: Sum si and Carry-out ci+1
Carry-out of cell i becomes carry-in to cell (i +1)
c0
Full
Adder
a0
b0
s0
c1
Full
Adder
a1
b1
s1
c2
Full
Adder
a2
b2
s2
c3
Full
Adder
a3
b3
s3
c4
ci
Full
Adder
ai
bi
si
ci+1

## Slide 5: Full-Adder Equations
K-map:
ai bi ci | ci+1 | si
0 0 0 | 0 | 0
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 1
00
01
11
10
0
1
0
1
0
1
1
0
1
0
K-Map of
00
01
11
10
0
1
0
0
1
0
0
1
1
1
K-Map of
ci
Full
Adder
ai
bi
si
ci+1

## Slide 6: Carry Propagation
Major drawback of ripple-carry adder is the carry propagation
The carries are connected in a chain through the full adders
This is why it is called a ripple-carry adder
The carry ripples (propagates) through all the full adders
a0
c0
s0
b0
a1
s1
b1
c1
a2
s2
b2
c2
a3
s3
b3
c3
c4

## Slide 7: Longest Delay Analysis
Suppose the XOR delay is 1 and AND-OR delay is 2
For an N-bit ripple-carry adder, if all inputs are present at once:
Most-significant sum-bit delay = 21 +(N – 1) 2
Final Carry-out delay = 1 + N 2
a0
c0
s0
b0
a1
s1
b1
c1
a2
s2
b2
c2
a3
s3
b3
c3
c4
2
2
2
2
1
1

## Slide 8: Next . . .
Ripple-Carry Adder
Magnitude Comparator
Design by Contraction
Signed Numbers
Addition/Subtraction of Signed 2's Complement

## Slide 9: Magnitude Comparator
A combinational circuit that compares two unsigned integers
Two Inputs:
  Unsigned integer A (m-bit number)
  Unsigned integer B (m-bit number)
Three outputs:
  A > B (GT output)
  A == B (EQ output)
  A < B (LT output)
Exactly one of the three outputs must be equal to 1
While the remaining two outputs must be equal to 0
m-bit
Magnitude Comparator
A[m–1:0]
m
B[m–1:0]
m
GT: A > B
EQ: A == B
LT: A < B

## Slide 10: Example: 4-bit Magnitude Comparator
Inputs:
  8 bits in total  256 possible combinations
  Not simple to design using conventional K-map techniques
The magnitude comparator can be designed at a higher level
Let us implement first the output ( is equal to )
  ↔ and
  Define:
  Therefore,

## Slide 11: The Greater Than Output
Given the 4-bit input numbers: and
If then , irrespective of the lower bits of and
Define: ( and )
If (), we compare with
Define: ( and )
If and , we compare with
Define: ( and )
If and and , we compare with
Define: ( and )
Therefore,

## Slide 12: The Less Than Output
We can derive the expression for the output, similar to
Given the 4-bit input numbers: and
If then , irrespective of the lower bits of and
Define: ( and )
If (), we compare with
Define: ( and )
Define: ( and )
Define: ( and )
Therefore,
Knowing and , we can also derive

## Slide 13: Iterative Magnitude Comparator Design
The Magnitude comparator can also be designed iteratively
4-bit magnitude comparator is implemented using 4 identical cells
Design can be extended to any number of cells
Comparison starts at least-significant bit
Final comparator output:
Cell 3
Cell 2
Cell 1
0
Cell 0

## Slide 14: Cell Implementation
Each Cell receives as inputs:
Bit of inputs and : and
, , and from cell
Each Cell produces three outputs:
, , and
Outputs of cell are inputs to cell
Output Expressions of Cell
( equals )
( > )
( < )
Third output can be produced for first two:
Cell

## Slide 15: Next . . .
Ripple-Carry Adder
Magnitude Comparator
Design by Contraction
Signed Numbers
Addition/Subtraction of Signed 2's Complement

## Slide 16: Design by Contraction
Contraction is a technique for simplifying the logic
Applying 0s and 1s to some inputs
Equations are simplified after applying fixed 0 and 1 inputs
Converting a function block to a more simplified function
Examples of Design by Contraction
  Incrementing a number by a fixed constant
  Comparing a number to a fixed constant

## Slide 17: Designing an Incrementer
An incrementer is a special case of an adder
Sum = A + 1 (B = 0, C0 = 1)
An n-bit Adder can be simplified into an n-bit Incrementer
1
0
0
0
0
0
0
0
0

## Slide 18: Simplifying the Incrementer Circuit
Many gates were eliminated
No longer needed when an input is a constant
Last cell can be replicated to implemented an n-bit incrementer
Incrementer
4
4
a [3:0]
s [3:0]
c4

## Slide 19: Next . . .
Ripple-Carry Adder
Magnitude Comparator
Design by Contraction
Signed Numbers
Addition/Subtraction of Signed 2's Complement

## Slide 20: Signed Numbers
Several ways to represent a signed number
  Sign-Magnitude
  1's complement
  2's complement
Divide the range of values into two parts
  First part corresponds to the positive numbers (≥ 0)
  Second part correspond to the negative numbers (< 0)
The 2's complement representation is widely used
  Has many advantages over other representations

## Slide 21: Sign-Magnitude Representation
Independent representation of the sign and magnitude
Leftmost bit is the sign bit: 0 is positive and 1 is negative
Using n bits, largest represented magnitude = 2n-1 – 1
Sign
Bit
bit
n-2
bit
2
bit
1
bit
0
. . .
Magnitude = n – 1 bits
n-bit number
1
0
1
1
0
1
0
0
1
0
1
1
0
1
0
1
Sign-magnitude
8-bit representation of +45
Sign-magnitude
8-bit representation of -45

## Slide 22: Properties of Sign-Magnitude
Symmetric range of represented values:
For n-bit register, range is from -(2n-1 – 1) to +(2n-1 – 1)
For example, if n = 8 bits then range is -127 to +127
Two representations for zero: +0 and -0 NOT Good!
Two circuits are needed for addition & subtraction NOT Good!
  In addition to an adder, a second circuit is needed for subtraction
  Sign and magnitude parts should be processed independently
  Sign bit should be examined to determine addition or subtraction
  Addition of numbers of different signs is converted into subtraction
  Increases the cost of the add/subtract circuit

## Slide 23: Sign-Magnitude Addition / Subtraction
Eight cases for Sign-Magnitude Addition / Subtraction
Operation | ADD Magnitudes | Subtract Magnitudes | 
 |  | A >= B | A < B
(+A) + (+B) | +(A+B) |  | 
(+A) + (-B) |  | +(A–B) | -(B–A)
(-A) + (+B) |  | -(A–B) | +(B–A)
(-A) + (-B) | -(A+B) |  | 
(+A) – (+B) |  | +(A–B) | -(B–A)
(+A) – (-B) | +(A+B) |  | 
(-A) – (+B) | -(A+B) |  | 
(-A) – (-B) |  | -(A–B) | +(B–A)

## Slide 24: 1’s Complement Representation
Given a binary number A
The 1’s complement of A is obtained by inverting each bit in A
Example: 1’s complement of (01101001)2 = (10010110)2
If A consists of n bits then:
A + (1’s complement of A) = (2n – 1) = (1…111)2 (all bits are 1's)
Range of values is -(2n-1 – 1) to +(2n-1 – 1)
For example, if n = 8 bits, range is -127 to +127
Two representations for zero: +0 and -0 NOT Good!
1's complement of (0…000)2 = (1…111)2 = 2n – 1
-0 = (1…111)2 NOT Good!

## Slide 25: 2’s Complement Representation
Standard way to represent signed integers in computers
A simple definition for 2’s complement:
Given a binary number A
The 2’s complement of A = (1’s complement of A) + 1
Example: 2’s complement of (01101001)2 =
(10010110)2 + 1 = (10010111)2
If A consists of n bits then
A + (2’s complement of A) = 2n
2’s complement of A = 2n – A

## Slide 26: Computing the 2's Complement
Another way to obtain the 2's complement:
Start at the least significant 1
Leave all the 0s to its right unchanged
Complement all the bits to its left
starting value | 001001002 = +36
step1: Invert the bits (1's complement) | 110110112
step 2: Add 1 to the value from step 1 | + 12
sum = 2's complement representation | 110111002 = -36
Binary Value
= 00100 1 00
2's Complement
= 11011 1 00
least
significant 1
2’s complement of 110111002 (-36) = 001000112 + 1 = 001001002 = +36
The 2’s complement of the 2’s complement of A is equal to A

## Slide 27: Properties of the 2’s Complement
Range of represented values: -2n-1 to +(2n-1 – 1)
For example, if n = 8 bits then range is -128 to +127
There is only one zero = (0…000)2 (all bits are zeros)
The 2’s complement of A is the negative of A
The sum of A + (2’s complement of A) must be zero
The final carry is ignored
Consider the 8-bit number A = 001011002 = +44
2’s complement of A = 110101002 = -44
001011002 + 110101002 = 1 000000002 (8-bit sum is 0)
Ignore final carry = 28

## Slide 28: Values of Different Representations
8-bit Binary Representation | Unsigned Value | Sign Magnitude Value | 1's Complement Value | 2's Complement Value
00000000 | 0 | +0 | +0 | 0
00000001 | 1 | +1 | +1 | +1
00000010 | 2 | +2 | +2 | +2
. . . | . . . | . . . | . . . | . . .
01111101 | 125 | +125 | +125 | +125
01111110 | 126 | +126 | +126 | +126
01111111 | 127 | +127 | +127 | +127
10000000 | 128 | -0 | -127 | -128
10000001 | 129 | -1 | -126 | -127
10000010 | 130 | -2 | -125 | -126
. . . | . . . | . . . | . . . | . . .
11111101 | 253 | -125 | -2 | -3
11111110 | 254 | -126 | -1 | -2
11111111 | 255 | -127 | -0 | -1

## Slide 29: 2's Complement Signed Value
Positive numbers (sign-bit = 0)
  Signed value = Unsigned value
Negative numbers (sign-bit = 1)
  Signed value = Unsigned value – 2n
  n = number of bits
Negative weight for sign bit
  The 2's complement representation assigns a negative weight to the sign bit (most-significant bit)
  -128 + 32 + 16 + 4 = -76
1
0
1
1
0
1
0
0
-128
64
32
16
8
4
2
1
8-bit Binary | Unsigned Value | Signed Value
00000000 | 0 | 0
00000001 | 1 | +1
00000010 | 2 | +2
. . . | . . . | . . .
01111101 | 125 | +125
01111110 | 126 | +126
01111111 | 127 | +127
10000000 | 128 | -128
10000001 | 129 | -127
10000010 | 130 | -126
. . . | . . . | . . .
11111101 | 253 | -3
11111110 | 254 | -2
11111111 | 255 | -1

## Slide 30: Next . . .
Ripple-Carry Adder
Magnitude Comparator
Design by Contraction
Signed Numbers
Addition/Subtraction of Signed 2's Complement

## Slide 31: Converting Subtraction into Addition
When computing A – B, convert B to its 2's complement
A – B = A + (2’s complement of B)
Same adder is used for both addition and subtraction
This is the biggest advantage of 2's complement
Final carry is ignored, because
A + (2's complement of B) = A + (2n – B) = (A – B) + 2n
Final carry = 2n, for n-bit numbers
0 1 0 0 1 1 0 1 0 1 0 0 1 1 0 1
– 0 0 1 1 1 0 1 0 + 1 1 0 0 0 1 1 0 (2's complement)
0 0 0 1 0 0 1 1 0 0 0 1 0 0 1 1 (same result)
borrow:
carry:
-1
-1
-1
1
1
1
1

## Slide 32: Adder/Subtractor for 2's Complement
Same adder is used to compute: (A + B) or (A – B)
Subtraction (A – B) is computed as: A + (2's complement of B)
2's complement of B = (1's complement of B) + 1
Two operations: OP = 0 (ADD), OP = 1 (SUBTRACT)
n-bit Adder
n
A [n-1:0]
S [n-1:0]
n
n
n
B [n-1:0]
c0
OP
cn
n-bit input vectors
n-bit output vector
n XOR
gates
OP = 0 (ADD)
B XOR 0 = B
S = A + B + 0 = A + B
OP = 1 (SUBTRACT)
B XOR 1 = 1's complement of B
S = A + (1's complement of B) + 1
S = A + (2's complement of B)
S = A – B

## Slide 33: Carry versus Overflow
Carry is important when …
  Adding unsigned integers
  Indicates that the unsigned sum is out of range
  Sum > maximum unsigned n-bit value
Overflow is important when …
  Adding or subtracting signed integers
  Indicates that the signed sum is out of range
Overflow occurs when …
  Adding two positive numbers and the sum is negative
  Adding two negative numbers and the sum is positive
Simplest way to detect Overflow: V = Cn–1  Cn
  Cn-1 and Cn are the carry-in and carry-out of the most-significant bit

## Slide 34: Carry and Overflow Examples
0
1
0
0
0
0
0
0
0
1
0
0
1
1
1
1
+
1
0
0
0
1
1
1
1
79
64
143 (-113)
Carry = 0 Overflow = 1
1
1
0
0
1
1
1
0
1
1
1
0
1
1
0
1
0
+
0
1
1
1
0
1
1
1
218 (-38)
157 (-99)
119
Carry = 1 Overflow = 1
1
1
1
We can have carry without overflow and vice-versa
Four cases are possible (Examples on 8-bit numbers)
1
1
1
1
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
0
0
1
1
1
15
248 (-8)
7
Carry = 1 Overflow = 0
1
1
1
1
1
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
1
0
1
1
1
15
8
23
Carry = 0 Overflow = 0
1

## Slide 35: Range, Carry, Borrow, and Overflow
Unsigned Integers: n-bit representation
Signed Integers: 2's complement representation
max = 2n–1
min = 0
Carry = 1 for
Addition
Number > max
Borrow for
Subtraction
Number < 0
Positive
Overflow
Number > max
Negative
Overflow
Number < min
max = 2n-1–1
Finite Set of Signed Integers
0
min = -2n-1
Finite Set of Unsigned Integers