## Slide 1: Functional Blocks
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Decoders
Encoders
Multiplexers
Demultiplexers
Design Examples

## Slide 3: Functional Blocks
A functional block is a combinational circuit
We will study blocks, such as decoders and multiplexers
Functional blocks are very common and useful in design
In the past, functional blocks were integrated circuits
SSI: Small Scale Integration = tens of gates
MSI: Medium Scale Integration = hundreds of gates
LSI: Large Scale Integration = thousands of gates
VLSI: Very Large Scale Integration = millions of gates
Today, functional blocks are part of a design library
Tested for correctness and reused in many projects

## Slide 4: Binary Decoders
Given a n-bit binary code, there are 2n possible code values
The decoder has an output for each possible code value
The n-to-2n decoder has n inputs and 2n outputs
Depending on the input code, only one output is set to logic 1
The conversion of input to output is called decoding
n to 2n
Decoder


n Inputs
2n Outputs
A decoder can have less than 2n outputs if some input codes are unused

## Slide 5: Examples of Binary Decoders
Inputs | Outputs |  |  |  |  |  |  | 
a2 a1 a0 | d0 | d1 | d2 | d3 | d4 | d5 | d6 | d7
0 0 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 0 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 1 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 1 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 0 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 0 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 1 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 1 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs | Outputs |  |  | 
a1 a0 | d0 | d1 | d2 | d3
0 0 | 1 | 0 | 0 | 0
0 1 | 0 | 1 | 0 | 0
1 0 | 0 | 0 | 1 | 0
1 1 | 0 | 0 | 0 | 1
Truth
Tables
2-to-4
Decoder
2 Inputs
4 Outputs
a1
a0
d0
d1
d2
d3
0
1
2
3
1
0
3-to-8
Decoder
8 Outputs
3 Inputs
a2
a1
a0
d0
d1
d2
d3
d4
d5
d6
d7
0
1
2
3
4
5
6
7
1
0
2

## Slide 6: Decoder Implementation
Each decoder output is a minterm
3-to-8 Decoder
2-to-4
Decoder
Inputs | Outputs |  |  | 
a1 a0 | d0 | d1 | d2 | d3
0 0 | 1 | 0 | 0 | 0
0 1 | 0 | 1 | 0 | 0
1 0 | 0 | 0 | 1 | 0
1 1 | 0 | 0 | 0 | 1

## Slide 7: Using Decoders to Implement Functions
A decoder generates all the minterms
A Boolean function can be expressed as a sum of minterms
Any function can be implemented using a decoder + OR gate
Note: the function must not be minimized
Example: Full Adder sum = ∑(1, 2, 4, 7), cout = ∑(3, 5, 6, 7)
Inputs | Outputs | 
a b c | cout | sum
0 0 0 | 0 | 0
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 1
3-to-8
Decoder
a
b
c
d0
d1
d2
d3
d4
d5
d6
d7
2
1
0
sum
cout

## Slide 8: Using Decoders to Implement Functions
Good if many output functions of the same input variables
If number of minterms is large  Wider OR gate is needed
Use NOR gate if number of maxterms is less than minterms
Example: f = ∑(2, 5, 6), g = ∏(3, 6)  g' = ∑(3, 6), h = ∑(0, 5)
Inputs | Outputs |  | 
a b c | f | g | h
0 0 0 | 0 | 1 | 1
0 0 1 | 0 | 1 | 0
0 1 0 | 1 | 1 | 0
0 1 1 | 0 | 0 | 0
1 0 0 | 0 | 1 | 0
1 0 1 | 1 | 1 | 1
1 1 0 | 1 | 0 | 0
1 1 1 | 0 | 1 | 0
3-to-8
Decoder
a
b
c
d0
d1
d2
d3
d4
d5
d6
d7
2
1
0
f
g
h

## Slide 9: 2-to-4 Decoder with Enable Input
Inputs |  | Outputs |  |  | 
EN | a1 a0 | d0 | d1 | d2 | d3
0 | X X | 0 | 0 | 0 | 0
1 | 0 0 | 1 | 0 | 0 | 0
1 | 0 1 | 0 | 1 | 0 | 0
1 | 1 0 | 0 | 0 | 1 | 0
1 | 1 1 | 0 | 0 | 0 | 1
If EN input is zero then all outputs are zeros, regardless of a1 and a0
Truth Table
2-to-4
Decoder
d0
d1
d2
d3
a1
a0
EN
1
0
0
1
2
3

## Slide 10: Building Larger Decoders
Larger decoders can be build using smaller ones
A 3-to-8 decoder can be built using:
Two 2-to-4 decoders with Enable and an inverter (1-to-2 decoder)
Inputs |  | Outputs |  |  |  |  |  |  | 
a2 | a1 a0 | d0 | d1 | d2 | d3 | d4 | d5 | d6 | d7
0 | 0 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Top
2-to-4
Decoder
1
0
d0
d1
d2
d3
EN
Bottom
2-to-4
Decoder
1
0
d4
d5
d6
d7
EN
a1
a0
a2
1-to-2 Decoder
0
1
2
3
0
1
2
3

## Slide 11: Building Larger Decoders
A 4-to-16 decoder with enable can be built using five 2-to-4 decoders with enables
Larger decoders can be built hierarchically in a similar way
a1
a0
2-to-4
Decoder
0
1
0
d0
d1
d2
d3
EN
2-to-4
Decoder
1
1
0
d4
d5
d6
d7
EN
2-to-4
Decoder
2
1
0
d8
d9
d10
d11
EN
2-to-4
Decoder
3
1
0
d12
d13
d14
d15
EN
2-to-4
Decoder
1
0
EN
EN
a3
a2
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3

## Slide 12: BCD to 7-Segment Decoder
Seven-Segment Display:
  Made of Seven segments: light-emitting diodes (LED)
  Found in electronic devices: such as clocks, calculators, etc.
BCD to 7-Segment Decoder
  Called also a decoder, but not a binary decoder
  Accepts as input a BCD decimal digit (0 to 9)
  Generates output to the seven LED segments to display the BCD digit
  Each segment can be turned on or off separately
BCD to
7-Segment
Decoder
I3
I2
I1
I0
a
b
c
d
e
f
g

## Slide 13: BCD to 7-Segment Decoder
Specification:
  Input: 4-bit BCD (I3, I2, I1, I0)
  Output: 7-bit (a, b, c, d, e, f, g)
  Display should be OFF for Non-BCD input codes.
  Implementation can use:
  A binary decoder
  Additional gates
BCD input I3 I2 I1 I0 | 7-Segment Output a b c d e f g
0 0 0 0 | 1 1 1 1 1 1 0
0 0 0 1 | 0 1 1 0 0 0 0
0 0 1 0 | 1 1 0 1 1 0 1
0 0 1 1 | 1 1 1 1 0 0 1
0 1 0 0 | 0 1 1 0 0 1 1
0 1 0 1 | 1 0 1 1 0 1 1
0 1 1 0 | 1 0 1 1 1 1 1
0 1 1 1 | 1 1 1 0 0 0 0
1 0 0 0 | 1 1 1 1 1 1 1
1 0 0 1 | 1 1 1 1 0 1 1
1010 to 1111 | 0 0 0 0 0 0 0
Truth Table

## Slide 14: Implementing a BCD to 7-Segment Decoder
I3 I2 I1 I0 | a b c d e f g
0 0 0 0 | 1 1 1 1 1 1 0
0 0 0 1 | 0 1 1 0 0 0 0
0 0 1 0 | 1 1 0 1 1 0 1
0 0 1 1 | 1 1 1 1 0 0 1
0 1 0 0 | 0 1 1 0 0 1 1
0 1 0 1 | 1 0 1 1 0 1 1
0 1 1 0 | 1 0 1 1 1 1 1
0 1 1 1 | 1 1 1 0 0 0 0
1 0 0 0 | 1 1 1 1 1 1 1
1 0 0 1 | 1 1 1 1 0 1 1
1010 – 1111 | 0 0 0 0 0 0 0
Truth Table
a
b
c
d
f
e
g
Input > 9
NOR gate is used for 0's
I2
I1
I0
I3
4-to-10
Binary
Decoder
0
1
2
3
4
5
6
7
8
9

## Slide 15: NAND Decoders with Inverted Outputs
Inputs |  | Outputs |  |  | 
EN | a1 a0 | d0 | d1 | d2 | d3
1 | X X | 1 | 1 | 1 | 1
0 | 0 0 | 0 | 1 | 1 | 1
0 | 0 1 | 1 | 0 | 1 | 1
0 | 1 0 | 1 | 1 | 0 | 1
0 | 1 1 | 1 | 1 | 1 | 0
Some decoders are constructed with NAND gates. Their outputs are inverted. The Enable input is also active low (Enable if zero)
Truth Table
2-to-4
Decoder
d0
d1
d2
d3
a1
a0
EN
1
0
0
1
2
3

## Slide 16: Using NAND Decoders
f
g
h
NAND decoders can be used to implement functions
Use NAND gates to output the minterms (if fewer ones)
Use AND gates to output the maxterms (if fewer zeros)
Example: f = ∑(2, 5, 6), g = ∏(3, 6), h = ∑(0, 5)
Inputs | Outputs |  | 
a b c | f | g | h
0 0 0 | 0 | 1 | 1
0 0 1 | 0 | 1 | 0
0 1 0 | 1 | 1 | 0
0 1 1 | 0 | 0 | 0
1 0 0 | 0 | 1 | 0
1 0 1 | 1 | 1 | 1
1 1 0 | 1 | 0 | 0
1 1 1 | 0 | 1 | 0
a
b
c
3-to-8
Decoder
Inverted
Outputs
(NAND)
d0
d1
d2
d3
d4
d5
d6
d7
2
1
0

## Slide 17: Next . . .
Decoders
Encoders
Multiplexers
Demultiplexers
Design Examples

## Slide 18: Encoders
An encoder performs the opposite operation of a decoder
It converts a 2n input to an n-bit output code
The output indicates which input is active (logic 1)
Typically, one input should be 1 and all others must be 0's
The conversion of input to output is called encoding
2n to n
Encoder


n Outputs
2n Inputs
A encoder can have less than 2n inputs if some input lines are unused

## Slide 19: Example of an 8-to-3 Binary Encoder
8 inputs, 3 outputs, only one input is 1, all others are 0's
Encoder generates the output binary code for the active input
Output is not specified if more than one input is 1
Inputs |  |  |  |  |  |  |  | Outputs |  | 
d7 | d6 | d5 | d4 | d3 | d2 | d1 | d0 | a2 | a1 | a0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
8-to-3
Binary
Encoder
3 Outputs
a2
a1
a0
8 Inputs
d0
d1
d2
d3
d4
d5
d6
d7
0
1
2
3
4
5
6
7
1
0
2

## Slide 20: 8-to-3 Binary Encoder Implementation
a2 = d4 + d5 + d6 + d7
a1 = d2 + d3 + d6 + d7
a0 = d1 + d3 + d5 + d7
a2
d4
d5
d6
d7
a1
d2
d3
d6
d7
a0
d1
d3
d5
d7
8-to-3 binary encoder implemented using three
4-input OR gates
Inputs |  |  |  |  |  |  |  | Outputs |  | 
d7 | d6 | d5 | d4 | d3 | d2 | d1 | d0 | a2 | a1 | a0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
8-to-3
Binary
Encoder
a2
a1
a0
d0
d1
d2
d3
d4
d5
d6
d7
0
1
2
3
4
5
6
7
1
0
2

## Slide 21: Binary Encoder Limitations
Exactly one input must be 1 at a time (all others must be 0's)
If more than one input is 1 then the output will be incorrect
For example, if d3 = d6 = 1
Then a2 a1 a0 = 111 (incorrect)
Two problems to resolve:
If two inputs are 1 at the same time, what should be the output?
If all inputs are 0's, what should be the output?
Output a2 a1 a0 = 000 if d0 = 1 or all inputs are 0's
How to resolve this ambiguity?
a2 = d4 + d5 + d6 + d7
a1 = d2 + d3 + d6 + d7
a0 = d1 + d3 + d5 + d7

## Slide 22: Priority Encoder
Eliminates the two problems of the binary encoder
Inputs are ranked from highest priority to lowest priority
If more than one input is active (logic 1) then priority is used
Output encodes the active input with higher priority
If all inputs are zeros then the V (Valid) output is zero
Indicates that all inputs are zeros
Inputs |  |  |  | Outputs |  | 
d3 | d2 | d1 | d0 | a1 | a0 | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1
Condensed
Truth Table
All 16 cases
are listed
4-to-2 Priority
Encoder
a1
a0
V
d3
d2
d1
d0
3 = highest priority
0 = lowest priority
1
0
2
1

## Slide 23: Implementing a 4-to-2 Priority Encoder
Output Expressions:
a1
a0
V
d3
d2
d1
d0
Inputs |  |  |  | Outputs |  | 
d3 | d2 | d1 | d0 | a1 | a0 | V
0 | 0 | 0 | 0 | X | X | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | X | 0 | 1 | 1
0 | 1 | X | X | 1 | 0 | 1
1 | X | X | X | 1 | 1 | 1
00
01
11
10
00
X
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
K-Map of
00
01
11
10
00
X
01
11
10
1
1
1
1
1
1
1
1
1
1
K-Map of

## Slide 24: Next . . .
Decoders
Encoders
Multiplexers
Demultiplexers
Design Examples

## Slide 25: Multiplexers
Selecting data is an essential function in digital systems
Functional blocks that perform selecting are called multiplexers
A Multiplexer (or Mux) is a combinational circuit that has:
  Multiple data inputs (typically 2n) to select from
  An n-bit select input S used for control
  One output Y
The n-bit select input directs one of the data inputs to the output
Mux
d0
d1
d2
.
.
.
Y
2n Inputs
n
S
d2n–1

## Slide 26: Examples of Multiplexers
2-to-1 Multiplexer
if (S == 0) Y = d0 ;
else Y = d1;
Logic expression:
4-to-1 Multiplexer
if (S1S0 == 00) Y = d0 ;
else if (S1S0 == 01) Y = d1;
else if (S1S0 == 10) Y = d2;
else Y = d3;
Logic expression:
Mux
1 0
S1S0
d0
d1
d2
d3
0
1
2
3
Inputs |  |  | Output
S | d0 | d1 | Y
0 | 0 | X | 0 = d0
0 | 1 | X | 1 = d0
1 | X | 0 | 0 = d1
1 | X | 1 | 1 = d1
Inputs |  |  |  |  |  | Output
S1 | S0 | d0 | d1 | d2 | d3 | Y
0 | 0 | 0 | X | X | X | 0 = d0
0 | 0 | 1 | X | X | X | 1 = d0
0 | 1 | X | 0 | X | X | 0 = d1
0 | 1 | X | 1 | X | X | 1 = d1
1 | 0 | X | X | 0 | X | 0 = d2
1 | 0 | X | X | 1 | X | 1 = d2
1 | 1 | X | X | X | 0 | 0 = d3
1 | 1 | X | X | X | 1 | 1 = d3
Mux
d0
d1
Y
S
0
1

## Slide 27: Implementing Multiplexers
Enabling
AND Gates
Enabling
AND Gates
Y
d0
d1
S
d1
Y
d2
S0
d0
d3
S1
Mux
d0
d1
S
0
1
Mux
1 0
S1S0
d0
d1
d2
d3
0
1
2
3

## Slide 28: 3-State Gate
Logic gates studied so far have two outputs: 0 and 1
Three-State gate has three possible outputs: 0, 1, Z
  Z is the Hi-Impedance output
  Z means that the output is disconnected from the input
  Gate behaves as an open switch between input and output
Input c connects input to output
  c is the control (enable) input
  If c is 0 then f = Z
  If c is 1 then f = input x
c | x | f
0 | 0 | Z
0 | 1 | Z
1 | 0 | 0
1 | 1 | 1
3-state gate

## Slide 29: Variations of the 3-State Gate
Control input c and output f can be inverted
A bubble is inserted at the input c or output f
inverted c
inverted f
inverted c, f
c | x | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | Z
1 | 1 | Z
c | x | f
0 | 0 | Z
0 | 1 | Z
1 | 0 | 1
1 | 1 | 0
c | x | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | Z
1 | 1 | Z

## Slide 30: Wired Output
  This will result in a short circuit that will burn the gates
  Logic gates with 0 and 1 outputs cannot have their outputs wired together
c1 | c2 | c3 | f
0 | 0 | 0 | Z
1 | 0 | 0 | x1
0 | 1 | 0 | x2
0 | 0 | 1 | x3
0 | 1 | 1 | Burn
1 | 0 | 1 | Burn
1 | 1 | 0 | Burn
1 | 1 | 1 | Burn
  3-state gates can wire their outputs together
  At most one 3-state gate can be enabled at a time
  Otherwise, conflicting outputs will burn the circuit

## Slide 31: Implementing Multiplexers with 3-State Gates
3-State Gates
1-to-2
Decoder
3-State Gates
Y
d0
d1
S
A Multiplexer can also be implemented using:
A decoder
Three-state gates
Mux
d0
d1
Y
S
0
1
S0
S1
Y
d0
d1
d2
d3
2-to-4
Decoder
0
1
2
3
1
0
Mux
1 0
S1S0
d0
d1
d2
d3
0
1
2
3

## Slide 32: Building Larger Multiplexers
Larger multiplexers can be built hierarchically using smaller ones
Building 4-to-1
Mux using three
2-to-1 Muxes
Building 8-to-1 Mux
using two 4-to-1 Muxes
and a 2-to-1 Mux
Y
Mux
d0
d1
S0
Mux
d2
d3
S0
Mux
S1
0
1
0
1
0
1
8-to-1 Mux
Y
2 1 0
S2S1S0
d0
d1
d2
d3
d4
d5
d6
d7
0
1
2
3
4
5
6
7
Y
Mux
S2
0
1
Mux
d4
d5
S1S0
d6
d7
0
1
2
3
1 0
Mux
d0
d1
S1S0
d2
d3
0
1
2
3
1 0

## Slide 33: Multiplexers with Vector Input and Output
The inputs and output of a multiplexer can be m-bit vectors
2-to-1 Multiplexer with m bits
Inputs and output are m-bit vectors
Using m copies of a 2-to-1 Mux
4-to-1 Multiplexer with m bits
Inputs and output are m-bit vectors
Using m copies of a 4-to-1 Mux
Mux
S
A [m–1:0]
m
B [m–1:0]
m
Y [m–1: 0]
m
0
1
m
Mux
A [m–1:0]
m
B [m–1:0]
m
C [m–1:0]
m
D [m–1:0]
m
Y [m–1: 0]
0
1
2
3
S1S0
1 0

## Slide 34: Implementing a Function with a Multiplexer
A Multiplexer can be used to implement any logic function
The function must be expressed using its minterms
Example: Implement F(a, b, c) = ∑(1, 2, 6, 7) using a Mux
Solution:
Inputs |  |  | Output
a | b | c | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
The inputs are
used as select
lines to a Mux.
An 8-to-1
Mux is used
because there
are 3 variables
a b c
8-to-1 Mux
F
S2 S1 S0 =
0
1
1
0
0
0
1
1
0
1
2
3
4
5
6
7
0
1
2

## Slide 35: Better Solution with a Smaller Multiplexer
Re-implement F(a, b, c) = ∑(1, 2, 6, 7) using a 4-to-1 Mux
We will use the two select lines for variables a and b
Variable c and its complement are used as inputs to the Mux
Inputs |  |  | Output | Comment
a | b | c | F | F
0 | 0 | 0 | 0 | F = c
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 1 | F = c'
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | F = 0
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 
4-to-1 Mux
F
S1 S0 = a b
c
c'
0
1
0
1
2
3
1
0

## Slide 36: Implementing Functions: Example 2
Implement F(a, b, c, d) = ∑(1,3,4,11,12,13,14,15) using 8-to-1 Mux
Inputs |  |  |  | Output | Comment
a | b | c | d | F | F
0 | 0 | 0 | 0 | 0 | F = d
0 | 0 | 0 | 1 | 1 | 
0 | 0 | 1 | 0 | 0 | F = d
0 | 0 | 1 | 1 | 1 | 
0 | 1 | 0 | 0 | 1 | F = d'
0 | 1 | 0 | 1 | 0 | 
0 | 1 | 1 | 0 | 0 | F = 0
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 0 | F = 0
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 0 | 0 | F = d
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 1 | F = 1
1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 0 | 1 | F = 1
1 | 1 | 1 | 1 | 1 | 
a b c
8-to-1 Mux
F
S2 S1 S0 =
d
0
1
0
1
2
3
4
5
6
7
0
1
2

## Slide 37: Shannon’s Expansion
Shannon’s Expansion Theorem:
and
Example:
(absorption)
Therefore,
Shannon’s Expansion can be applied recursively:

## Slide 38: Shannon’s Expansion (cont’d)
Used to implement functions with multiplexers
Example:
f
Mux
0
c
b
Mux
c
1
b
Mux
a
0
1
0
1
0
1
Three
2×1 muxes
4-to-1 Mux
f
S1 S0 = a b
0
c
c
1
0
1
2
3
1
0
4×1 mux

## Slide 39: Shannon’s Expansion (cont’d)
Can be implemented using a 2×1 mux
The truth table method uses a 4×1 mux
Can be implemented using a 4×1 mux
The truth table method uses an 8×1 mux
4-to-1 Mux
h
S1 S0 = a b
c’
d
d’
c
0
1
2
3
1
0
Mux
b
c
g
a
0
1

## Slide 40: Demultiplexer
Performs the inverse operation of a Multiplexer
A Demultiplexer (or Demux) is a combinational circuit that has:
One data input I
An n-bit select input S
A maximum of 2n data outputs
The Demux directs the data input to one of the outputs
According to the select input S
.
.
.
I
2n Outputs
n
S
d0
d1
d2
d2n–1
Demux

## Slide 41: Examples of Demultiplexers
1-to-2 Demultiplexer
if (S == 0) { d0 = I ; d1 = 0; }
else { d1 = I ; d0 = 0 ; }
Output expressions:
;
1-to-4 Demultiplexer
if (S1S0 == 00) { d0 = I ; d1 = d2 = d3 = 0; }
else if (S1S0 == 01) { d1 = I ; d0 = d2 = d3 = 0; }
else if (S1S0 == 10) { d2 = I ; d0 = d1 = d3 = 0; }
else { d3 = I ; d0 = d1 = d2 = 0; }
Output expressions:
; ; ;
I
4 Outputs
S1S0
d0
d1
d2
d3
Demux
0
1
2
3
0
1
I
2 Outputs
S
d0
d1
Demux
0
1

## Slide 42: Demultiplexer = Decoder with Enable
A 1-to-4 demux is equivalent to a 2-to-4 decoder with enable
Demux select input S1 is equivalent to Decoder input a1
Demux select input S0 is equivalent to Decoder input a0
Demux Input I is equivalent to Decoder Enable EN
In general, a demux with n select inputs and 2n outputs is equivalent to a n-to-2n decoder with enable input
Think of a decoder as directing the Enable signal to one output
2-to-4
Decoder
d0
d1
d2
d3
S1 = a1
S0 = a0
I = EN
1
0
0
1
2
3
I
4 Outputs
S1S0
d0
d1
d2
d3
Demux
0
1
2
3
0
1

## Slide 43: Next . . .
Decoders
Encoders
Multiplexers
Demultiplexers
Design Examples

## Slide 44: 2-by-2 Crossbar Switch
A 2×2 crossbar switch is a combinational circuit that has:
Two m-bit Inputs: A and B
Two m-bit outputs: X and Y
1-bit select input S
Implement the 2×2 crossbar switch using multiplexers
Solution: Two 2-input multiplexers are used
if (S == 0) { X = A; Y = B; }
else { X = B; Y = A; }
2×2
Crossbar
Switch
m
A[m-1:0]
m
B[m-1:0]
X [m-1:0]
m
Y [m-1:0]
m
S
S
A[m–1:0]
m
B[m–1:0]
m
Mux
0
1
Mux
0
1
X [m-1:0]
m
Y [m-1:0]
m

## Slide 45: Sorting Two Unsigned Integers
Design a circuit that sorts two m-bit unsigned integers A and B
Inputs: Two m-bit unsigned integers A and B
Outputs: X = min(A, B) and Y = max(A, B)
Solution:
We will use a magnitude comparator to compare A with B, and
2×2 crossbar switch implemented using two 2-input multiplexers
m-bit
Magnitude Comparator
A[m–1:0]
m
B[m–1:0]
m
A < B
A = B
A > B
S
B[m–1:0]
m
A[m–1:0]
m
Mux
0
1
Mux
0
1
X [m-1:0] = min(A, B)
m
m
Y [m-1:0] = max(A, B)

## Slide 46: Arithmetic and Logic Unit (ALU)
Can perform many functions
Most common ALU functions
Arithmetic functions: ADD, SUB (Subtract)
Logic functions: AND, OR, XOR, etc.
We will design an ALU with 8 functions
The function F is coded with 3 bits as follows:
Function | ALU Result | Function | ALU Result
F = 000 (ADD) | R = A + B | F = 100 (AND) | R = A & B
F = 001 (ADD + 1) | R = A + B + 1 | F = 101 (OR) | R = A ¦ B
F = 010 (SUB – 1) | R = A – B – 1 | F = 110 (NOR) | R = ~(A ¦ B)
F = 011 (SUB) | R = A – B | F = 111 (XOR) | R = (A ^ B)
ALU
F[2:0]
3
n
A[n-1:0]
n
B[n-1:0]
R [n-1:0]
n
V C
ALU Symbol

## Slide 47: Designing a Simple ALU
n
B[n-1:0]
n-bit Adder
n
n
c0
n
n XOR
gates
n
n
n
n AND
gates
n
n
n XOR
gates
n
n OR
gates
n
n
n
F[2:0] = 3-bit Function code
cn-1
cn
A[n-1:0]
Result = R[n-1:0]
V
C
V = Overflow
C = Carry output
mux
3
2
1
0
0
1
n
mux
1
0
n