## Slide 1: Behavioral Modeling in Verilog
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Introduction to Dataflow and Behavioral Modeling
Verilog Operators
Module Parameters
Modeling Adders, Comparators, Multiplexers
Always Block with Sensitivity List
Procedural Statements: IF and CASE
Modeling Decoder, Priority Encoder, and ALU

## Slide 3: Verilog Four-Valued Logic
Verilog Value Set consists of four basic values:
  0 – represents a logic zero, or false condition
  1 – represents a logic one, or true condition
  X – represents an unknown logic value
  Z – represents a high-impedance value
x or X represents an unknown or uninitialized value
z or Z represents the output of a disabled tri-state buffer

## Slide 4: Nets and Variables
Verilog has two major data types:
Net data types: are connections between parts of a design
Variable data types: can store data values
The wire is a net data type (physical connection)
  A wire cannot store the value of a procedural assignment
  However, a wire can be driven by continuous assignment
The reg is a variable data type
  Can store the value of a procedural assignment
  However, cannot be driven by continuous assignment
  Other variable types: integer, time, real, and realtime

## Slide 5: Modeling Circuits in Verilog
Four levels of modeling circuits in Verilog
Gate-Level Modeling
  Lowest-level modeling using Verilog primitive gates
Structural Modeling using module instantiation
  Describes the structure of a circuit with modules at different levels
Dataflow Modeling using concurrent assign statements
  Describes the flow of data between input and output
Behavioral Modeling using procedural blocks and statements
  Describes what the circuit does at a higher level of abstraction
  Can also mix different models in the same design

## Slide 6: Dataflow and Behavioral Modeling
Dataflow Modeling using Continuous Assignment
  Used mostly for describing Boolean equations and combinational logic
  Verilog provides a rich set of operators
  Can describe: adders, comparators, multiplexers, etc.
  Synthesis tool can map a dataflow model into a target technology
Behavioral Modeling using Procedural Blocks and Statements
  Describes what the circuit does at a functional and algorithmic level
  Encourages designers to rapidly create a prototype
  Can be verified easily with a simulator
  Some procedural statements are synthesizable (Others are NOT)

## Slide 7: Continuous Assignment
The assign statement defines continuous assignment
Syntax: assign [#delay] net_name = expression;
Assigns expression value to net_name (wire or output port)
The optional #delay specifies the delay of the assignment
Continuous assignment statements are concurrent
Can appear in any order inside a module
Continuous assignment can model combinational circuits
Describes the flow of data between input and output

## Slide 8: Verilog Operators
Bitwise Operators | 
~a | Bitwise NOT
a & b | Bitwise AND
a ¦ b | Bitwise OR
a ^ b | Bitwise XOR
a ~^ b | Bitwise XNOR
a ^~ b | Same as ~^
Arithmetic Operators | 
a + b | ADD
a – b | Subtract
-a | Negate
a * b | Multiply
a / b | Divide
a % b | Remainder
Shift Operators | 
a << n | Shift Left
a >> n | Shift Right
Reduction Operators | 
&a | AND all bits
¦a | OR all bits
^a | XOR all bits
~&a | NAND all bits
~¦a | NOR all bits
~^a | XNOR all bits
Relational Operators | 
a == b | Equality
a != b | Inequality
a < b | Less than
a > b | Greater than
a <= b | Less or equal
a >= b | Greater or equal
Reduction operators produce a 1-bit result
Relational operators produce a 1-bit result
{a, b} concatenates the bits of a and b
Miscellaneous Operators | 
sel?a:b | Conditional
{a, b} | Concatenate

## Slide 9: Bit Vectors in Verilog
A Bit Vector is multi-bit declaration that uses a single name
A Bit Vector is specified as a Range [msb:lsb]
msb is most-significant bit and lsb is least-significant bit
Examples:
input [15:0] A; // A is a 16-bit input vector
output [0:15] B; // Bit 0 is most-significant bit
wire [3:0] W; // Bit 3 is most-significant bit
Bit select: W[1] is bit 1 of W
Part select: A[11:8] is a 4-bit select of A with range [11:8]
The part select range must be consistent with vector declaration

## Slide 10: Reduction Operators
module Reduce
( input [3:0] A, B, output X, Y, Z );
// A, B are input vectors, X, Y, Z are 1-bit outputs
// X = A[3] | A[2] | A[1] | A[0];
assign X = |A;
// Y = B[3] & B[2] & B[1] & B[0];
assign Y = &B;
// Z = X & (B[3] ^ B[2] ^ B[1] ^ B[0]);
assign Z = X & (^B);
endmodule

## Slide 11: Concatenation Operator { }
module Concatenate
( input [7:0] A, B, output [7:0] X, Y, Z );
// A, B are input vectors, X, Y, Z are output vectors
// X = A is right-shifted 3 bits using { } operator
assign X = {3'b000, A[7:3]};
// Y = A is right-rotated 3 bits using { } operator
assign Y = {A[2:0], A[7:3]};
// Z = selecting and concatenating bits of A and B
assign Z = {A[5:4], B[6:3], A[1:0]};
endmodule

## Slide 12: Integer Literals (Constant Values)
Syntax: [size]['base]value
size (optional) is the number of bits in the value
'base can be: 'b(binary), 'o(octal), 'd(decimal), or 'h(hex)
value can be in binary, octal, decimal, or hexadecimal
If the 'base is not specified then decimal value
Examples:
8'b1011_1101 (8-bit binary), 'hA3F0 (16-bit hexadecimal)
16'o56377 (16-bit octal), 32'd999 (32-bit decimal)
The underscore _ can be used to enhance readability of value
When size is fewer bits than value, upper bits are truncated

## Slide 13: Ripple Carry Adder
Using identical copies of a full adder to build a large adder
The cell (iterative block) is a full adder
Adds 3 bits: ai, bi, ci, Computes: Sum si and Carry-out ci+1
Carry-out of cell i becomes carry-in to cell (i +1)
c0
Full
Adder
a0
b0
s0
c1
Full
Adder
a1
b1
s1
c2
. . .
cn-1
Full
Adder
an-1
bn-1
sn-1
cn
ci
Full
Adder
ai
bi
si
ci+1

## Slide 14: 16-Bit Adder with Array Instantiation
// Input ports: 16-bit a and b, 1-bit cin (carry input)
// Output ports: 16-bit sum, 1-bit cout (carry output)
module Adder_16 (input [15:0] a, b, input cin,
output [15:0] sum, output cout);
wire [16:0] c; // carry bits
assign c[0] = cin; // carry input
assign cout = c[16]; // carry output
// Instantiate an array of 16 Full Adders
// Each instance [i] is connected to bit select [i]
Full_Adder FA [15:0] (a[15:0], b[15:0], c[15:0],
c[16:1], sum[15:0]);
endmodule
Array Instantiation of identical modules by a single statement

## Slide 15: 16-Bit Adder with Continuous Assignment
// Input ports: 16-bit a and b, 1-bit cin (carry input)
// Output ports: 16-bit sum, 1-bit cout (carry output)
module Adder_16 (input [15:0] a, b, input cin,
output [15:0] sum, output cout);
wire [16:0] c; // carry bits
assign c[0] = cin; // carry input
assign cout = c[16]; // carry output
// assignment of 16-bit vectors
assign sum[15:0] = (a[15:0] ^ b[15:0]) ^ c[15:0];
assign c[16:1] = (a[15:0] & b[15:0]) |
(a[15:0] ^ b[15:0]) & c[15:0];
endmodule

## Slide 16: 16-bit Adder with the + Operator
module Adder16
( input [15:0] A, B, input cin,
output [15:0] Sum, output cout );
// A and B are 16-bit input vectors
// Sum is a 16-bit output vector
// {cout, Sum} is a concatenated 17-bit vector
// A + B + cin is 16-bit addition + input carry
// The + operator is translated into an adder
assign {cout, Sum} = A + B + cin;
endmodule

## Slide 17: Modeling a Parametric n-bit Adder
// Parametric n-bit adder, default value for n = 16
module Adder #(parameter n = 16)
( input [n-1:0] A, B, input cin,
output [n-1:0] Sum, output cout );
// A and B are n-bit input vectors
// Sum is an n-bit output vector
// The + operator is translated into an n-bit adder
// Only one assign statement is used
assign {cout, Sum} = A + B + cin;
endmodule

## Slide 18: Instantiating Adders of Various Sizes
// Instantiate a 16-bit adder (parameter n = 16)
// A1, B1, and Sum1 must be 16-bit vectors
Adder #(16) adder16 (A1, B1, Cin1, Sum1, Cout1);
// Instantiate a 32-bit adder (parameter n = 32)
// A2, B2, and Sum2 must be 32-bit vectors
Adder #(32) adder32 (A2, B2, Cin2, Sum2, Cout2);
// If parameter is not specified, it defaults to 16
Adder adder16 (A1, B1, Cin1, Sum1, Cout1);

## Slide 19: Modeling a Magnitude Comparator
// n-bit magnitude comparator, No default value for n
module Comparator #(parameter n)
(input [n-1:0] A, B,
output GT, EQ, LT);
// A and B are n-bit input vectors (unsigned)
// GT, EQ, and LT are 1-bit outputs
assign GT = (A > B);
assign EQ = (A == B);
assign LT = (A < B);
endmodule
n-bit
Magnitude Comparator
A[n–1:0]
n
B[n–1:0]
n
GT
EQ
LT

## Slide 20: Instantiating Comparators of Various Sizes
// Instantiate a 16-bit comparator (n = 16)
// A1 and B1 must be declared as 16-bit vectors
Comparator #(16) comp16 (A1, B1, GT1, EQ1, LT1);
// Instantiate a 32-bit comparator (n = 32)
// A2 and B2 must be declared as 32-bit vectors
Comparator #(32) comp32 (A2, B2, GT2, EQ2, LT2);
// WRONG Instantiation: Must specify parameter n
Comparator comp32 (A2, B2, GT2, EQ2, LT2);

## Slide 21: Conditional Operator
Syntax:
Boolean_expr ? True_expression : False_expression
If Boolean_expr is true then select True_expression
Else select False_Expression
Examples:
assign max = (a>b)? a : b; // maximum of a and b
assign min = (a>b)? b : a; // minimum of a and b
Conditional operators can be nested

## Slide 22: Modeling a 2x1 Multiplexer
// Parametric 2x1 Mux, default value for n = 1
module Mux2 #(parameter n = 1)
( input [n-1:0] A, B, input sel,
output [n-1:0] Z);
// A and B are n-bit input vectors
// Z is the n-bit output vector
// if (sel==0) Z = A; else Z = B;
// Conditional operator used for selection
assign Z = (sel == 0)? A : B;
endmodule
Z
n
sel
0
A
n
1
B
n

## Slide 23: Modeling a 4x1 Multiplexer
// Parametric 4x1 Mux, default value for n = 1
module Mux4 #(parameter n = 1)
( input [n-1:0] A, B, C, D,
input [1:0] sel,
output [n-1:0] Z );
// sel is a 2-bit vector
// Nested conditional operators
assign Z = (sel[1] == 0) ?
((sel[0] == 0) ? A : B) :
((sel[0] == 0) ? C : D);
endmodule
Z
n
sel
0
A
n
1
B
n
2
C
n
3
D
n
2

## Slide 24: Behavioral Modeling
Uses procedural blocks and procedural statements
There are two types of procedural blocks in Verilog
The initial block
  Executes the enclosed statement(s) one time only
The always block
  Executes the enclosed statement(s) repeatedly until simulation terminates
The body of the initial and always blocks is procedural
  Can enclose one or more procedural statements
  Procedural statements are surrounded by begin … end
Multiple procedural blocks can appear in any order inside a module and run in parallel inside the simulator

## Slide 25: Example of Initial and Always Blocks
module behave;
reg clk; // 1-bit variable
reg [15:0] A; // 16-bit variable
initial begin // executed once
clk = 0; // initialize clk
A = 16'h1234; // initialize A
#200 $finish
end
always begin // executed always
#10 clk = ~clk; // invert clk every 10 ns
end
always begin // executed always
#20 A = A + 1; // increment A every 20 ns
end
endmodule

## Slide 26: Always Block with Sensitivity List
Syntax:
always @(sensitivity list) begin
procedural statements
end
An always block can have a sensitivity list
Sensitivity list is a list of signals: @(signal1, signal2, …)
The sensitivity list triggers the execution of the always block
When there is a change of value in any listed signal
Otherwise, the always block does nothing until another change occurs on a signal in the sensitivity list

## Slide 27: Sensitivity List for Combinational Logic
For combinational logic, the sensitivity list must include:
ALL the signals that are read inside the always block
Example: A, B, and sel must be in the sensitivity list below:
always @(A, B, sel) begin
if (sel == 0) Z = A;
else Z = B;
end
Combinational logic can also use: @(*) or @*
@(*) is automatically sensitive to all the signals that are read inside the always block
A, B, and sel are read inside the always block

## Slide 28: If Statement
The if statement is procedural
Can only be used inside a procedural block
Syntax:
if (expression) statement
[ else statement ]
The else part is optional
A statement can be simple or compound
A compound statement is surrounded by begin ... end
if statements can be nested
Can be nested under if or under else part

## Slide 29: Modeling a 2x1 Multiplexer
// Behavioral Modeling of a Parametric 2x1 Mux
module Mux2 #(parameter n = 1)
( input [n-1:0] A, B, input sel,
output reg [n-1:0] Z);
// Output Z must be of type reg
// Sensitivity list = @(A, B, sel)
always @(A, B, sel) begin
if (sel == 0) Z = A;
else Z = B;
end
endmodule
Z
n
sel
0
A
n
1
B
n

## Slide 30: Modeling a 3x8 Decoder
module Decoder3x8 (input [2:0] A, output reg [7:0] D);
// Sensitivity list = @(A)
always @(A) begin
if (A == 0) D = 8'b00000001;
else if (A == 1) D = 8'b00000010;
else if (A == 2) D = 8'b00000100;
else if (A == 3) D = 8'b00001000;
else if (A == 4) D = 8'b00010000;
else if (A == 5) D = 8'b00100000;
else if (A == 6) D = 8'b01000000;
else D = 8'b10000000;
end
endmodule

## Slide 31: Modeling a 4x2 Priority Encoder
module Priority_Encoder4x2
(input [3:0] D, output reg V, output reg [1:0] A);
// sensitivity list = @(D)
always @(D) begin
if (D[3]) {V, A} = 3'b111;
else if (D[2]) {V, A} = 3'b110;
else if (D[1]) {V, A} = 3'b101;
else if (D[0]) {V, A} = 3'b100;
else {V, A} = 3'b000;
end
endmodule

## Slide 32: Modeling a Magnitude Comparator
// Behavioral Modeling of a Magnitude Comparator
module Comparator #(parameter n = 1)
(input [n-1:0] A, B, output reg GT, EQ, LT);
// Sensitivity list = @(A, B)
always @(A, B) begin
if (A > B)
{GT,EQ,LT}='b100;
else if (A == B)
{GT,EQ,LT}='b010;
else
{GT,EQ,LT}='b001;
end
endmodule
n-bit
Magnitude Comparator
A[n–1:0]
n
B[n–1:0]
n
GT
EQ
LT

## Slide 33: Case Statement
The case statement is procedural (used inside always block)
Syntax:
case (expression)
case_item1: statement
case_item2: statement
. . .
default: statement
endcase
The default case is optional
A statement can be simple or compound
A compound statement is surrounded by begin ... end

## Slide 34: Modeling a Mux with a Case Statement
module Mux4 #(parameter n = 1)
( input [n-1:0] A, B, C, D, input [1:0] sel,
output reg [n-1:0] Z );
// @(*) is @(A, B, C, D, sel)
always @(*) begin
case (sel)
2'b00: Z = A;
2'b01: Z = B;
2'b10: Z = C;
default: Z = D;
endcase
end
endmodule
Z
n
sel
0
A
n
1
B
n
2
C
n
3
D
n
2

## Slide 35: Modeling a Multifunction ALU
// Behavioral Modeling of an ALU
module ALU #(parameter n = 16)
( input [n-1:0] A, B, input [1:0] F,
output reg [n-1:0] Z, output reg Cout );
// @(*) is @(A, B, F)
always @(*) begin
case (F)
2'b00: {Cout,Z} = A+B;
2'b01: {Cout,Z} = A-B;
2'b10: {Cout,Z} = A&B;
default: {Cout,Z} = A|B;
endcase
end
endmodule
ALU
F [1:0]
2
n
A [n-1:0]
n
B [n-1:0]
Z [n-1:0]
n
Cout
ALU Symbol

## Slide 36: Modeling a BCD to 7-Segment Decoder
module BCD_to_7Seg_Decoder
( input [3:0] BCD, output reg [6:0] Seg )
always @(BCD) begin
case (BCD)
0: Seg = 7'b1111110; 1: Seg = 7'b0110000;
2: Seg = 7'b1101101; 3: Seg = 7'b1111001;
4: Seg = 7'b0110011; 5: Seg = 7'b1011011;
6: Seg = 7'b1011111; 7: Seg = 7'b1110000;
8: Seg = 7'b1111111; 9: Seg = 7'b1111011;
default: Seg = 7'b0000000;
endcase
end
endmodule