## Slide 1: Analysis of Clocked Sequential Circuits
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Analysis of Clocked Sequential circuits
  State and Output Equations
  State Table
  State Diagram
Mealy versus Moore Sequential Circuits
  State and Timing Diagrams

## Slide 3: Analysis of Clocked Sequential Circuits
Analysis is describing what a given circuit will do
The output of a clocked sequential circuit is determined by
Inputs
State of the Flip-Flops
Analysis Procedure:
Obtain the equations at the inputs of the Flip-Flops
Obtain the output equations
Fill the state table for all possible input and state values
Draw the state diagram

## Slide 4: Analysis Example
Is this a clocked sequential circuit?
YES!
What type of Memory?
D Flip-Flops
How many state variables?
Two state variables: and
What are the Inputs?
One Input:
What are the Outputs?
One Output:

## Slide 5: Flip-Flop Input Equations
What are the equations on the inputs of the flip-flops?
and are the current state
and are the next state
The values of and will be
and at the next clock edge

## Slide 6: Next State and Output Equations
The next state equations define the next state
At the inputs of the Flip-Flops
Next state equations?
There is only one output
What is the output equation?

## Slide 7: State Table
State table shows the Next State and Output in a tabular form
Next State Equations: and
Output Equation:
Another form of the state table

## Slide 8: State Diagram
State diagram is a graphical representation of a state table
The circles are the states
Two state variable  Four states (ALL values of and )
Arcs are the state transitions
Labeled with: Input / Output

## Slide 9: Combinational versus Sequential Analysis
Analysis of Combinational Circuits
Obtain the Boolean Equations
Fill the Truth Table
Analysis of Sequential Circuits
Obtain the Next State Equations
Obtain the Output Equations
Fill the State Table
Draw the State Diagram
Output is a function of input only
Output is a function of input and current state
Next state is a function of input and current state

## Slide 10: Example with Output = Current State
Analyze the sequential circuit shown below
Two inputs: and
One state variable
No separate output  Output = current state
Obtain the next state equation, state table, and state diagram

## Slide 11: Example with Output = Current State
Flip-Flop Input Equation:
⨁ ⨁
Next State Equation: ⨁ ⨁

## Slide 12: Sequential Circuit with T Flip-Flops
Circuit has two T Flip-Flops
One Input
One output
Two state variables: and
Obtain the T-FF input equations
Obtain the next state equations
Fill the state table
Draw the state diagram

## Slide 13: Recall: Flip-Flop Characteristic Equation
For D Flip-Flop:
For T Flip-Flop: ⨁
For JK Flip-Flop:
D Flip-Flop | 
D | Q(t+1)
0 | 0 Reset
1 | 1 Set
JK Flip-Flop | 
J K | Q(t+1)
0 0 | Q(t) No change
0 1 | 0 Reset
1 0 | 1 Set
1 1 | Q'(t) Complement
T Flip-Flop | 
T | Q(t+1)
0 | Q(t) No change
1 | Q'(t) Complement
These equations define the Next State

## Slide 14: Sequential Circuit with T Flip-Flops
T Flip-Flop Input Equations:
Next State Equations:
⨁ ⨁
⨁ ⨁
Output Equation:

## Slide 15: From Next State Equations to State Table
T Flip-Flop Input Equations:
Next State Equations:
⨁
⨁
Output Equation:
Notice that the output is a function of the present state only.
It does NOT depend on the input

## Slide 16: From State Table to State Diagram
Four States: (drawn as circles)
Output Equation: (does not depend on input )
Output is shown inside the state circle ()

## Slide 17: Sequential Circuit with a JK Flip-Flops
One Input and two state variables: and (outputs of Flip-Flops)
No separate output  Output = Current state
Obtain the JK input equations
Obtain the next state equations
Fill the state table
Draw the state diagram

## Slide 18: JK Input and Next State Equations
JK Flip-Flop Input Equations:
and
and ⨁
Next State Equations:
Substituting:

## Slide 19: From JK Input Equations to State Table
JK Input Equations: , , and ⨁

## Slide 20: From State Table to State Diagram
Four states: (drawn as circles)
Arcs show the input value on the state transition

## Slide 21: Mealy versus Moore Sequential Circuits
There are two ways to design a clocked sequential circuit:
Mealy Machine: Outputs depend on present state and inputs
Moore Machine: Outputs depend on present state only

## Slide 22: Mealy Machine
The outputs are a function of the present state and Inputs
The outputs are NOT synchronized with the clock
The outputs may change if inputs change during the clock cycle
The outputs may have momentary false values (called glitches)
The correct outputs are present just before the edge of the clock

## Slide 23: Mealy State Diagram
An example of a Mealy state diagram is shown on the right
Each arc is labeled with:
Input / Output
The output is shown on the arcs of the state diagram
The output depends on the current state and input
Notice that State 11 cannot be reached from the other states

## Slide 24: Tracing a Mealy State Diagram
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Output z | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
When the circuit is powered, the initial state (AB) is unknown
Even though the initial state is unknown, the input x = 0 forces a transition to state AB = 00, regardless of the present state
Sometimes, a reset input is used to initialize the state to 00

## Slide 25: False Output in the Timing Diagram
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
Output z | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
A
B
Negative edge-triggered

## Slide 26: Moore Machine
The outputs are a function of the Flip-Flop outputs only
The outputs depend on the current state only
The outputs are synchronized with the clock
Glitches cannot appear in the outputs (even if inputs change)
A given design might mix between Mealy and Moore

## Slide 27: Moore State Diagram
An example of a Moore state diagram is shown on the right
Arcs are labeled with input only
The output is shown inside the state: (State / Output)
The output depends on the current state only
00
0
01
0
10
0
11
1
1
1
1
0
0
0
1
0

## Slide 28: Tracing a Moore State Diagram
When the circuit is powered, the initial state (AB) and output are unknown
Input x = 0 resets the state AB to 00. Can also be done with a reset signal.
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1
Output z | ? | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
00
0
01
0
10
0
11
1
1
1
1
0
0
0
1
0

## Slide 29: Timing Diagram of a Moore Machine
Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input x | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
Present State A B | ? | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
 | ? | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1
Output z | ? | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Negative edge-triggered
A
B
The output is synchronized with the clock. No false output (or glitch) can appear.

## Slide 30: Summary
To analyze a clocked sequential circuit:
Obtain the equations at the Inputs of the flip-flops
Obtain the Next State equations
  For a D Flip-Flop, the Next State = D input equation
  For T and JK, use the characteristic equation of the Flip-Flop
Obtain the Output equations
Fill the State Table
  Put all the combinations of current state and input
  Fill the next state and output columns
Draw the State Diagram
Two types of clocked sequential circuits: Mealy versus Moore