Symbolic Matlab

First : you need to define the symbols that you will be using

syms  x  t  w  f  Xf  y

Symbolic Integration

int(x)

ans =

1/2*x^2

pretty(ans)

>>1/2 x2

>> int(x,3,6)

ans =

27/2

Symbolic Differention

>> diff(x^2)

ans =

2*x

>> y=x^2

y =

x^2

>> ezplot(y,[-10,10])

Note heaviside(t) and dirac(t) is the step function and impulse function respectively which are  already defined in Symbolic Matlab

syms t w f  x y X Y H Xs;

x=exp(-t)*heaviside(t);

diff(heaviside(t))

ans =

dirac(t)

>> diff(x)

ans =

-exp(-t)*heaviside(t)+exp(-t)*dirac(t)

Finding Fourier Transform using Symbolic Matlab

>> x=exp(-3*t)*heaviside(t) ;

>>X=fourier(x)

X =

1/(3+w*i)

% Using Substitute command to replace variable from w to f

>> subs(X, w, '2*pi*f')

ans =

1/(3+2*i*pi*f)

>> pretty(ans)

1

------------

3 + 2 i pi f

Now to reconstruct the signal from the Fourier Transform (Inverse Fourier Transform) , we use ifourier

>>ifourier(X)

ans =

exp(-3*x)*heaviside(x)

Note : the reconstructed function is in terms of x.

To make it in terms of t , you use the following

>> xt=ifourier(X,t)

xt =

exp(-3*t)*heaviside(t)

Laplace Transform

>> x=exp(-3*t);

>> X=laplace(x)

X =

1/(s + 3)

Note there is no need to multiply it by step function (heaviside(t) )

If you want to inverse back ( i.e , obtainning x(t))

>> ilaplace(X)

ans =

1/exp(3*t)

% Generate Pulse function symbolicaly

>> x=heaviside(t)-heaviside(t-1)

>>  ezplot(x,[-2,3])

>>  X=fourier(x);

>>  ifourier(X)

ans =

heaviside(x)-heaviside(x-1)

Note you can put the answer in terms of time by using  ifourier(X,t)

Laplace

>> laplace(x)

ans =

1/s*(1-exp(-s))

>> pretty(ans)

1 - exp(-s)

-----------

s