# University Diploma Programs

# Electronic Equipment Maintenance

EET-029: Introduction to Communications

## Quiz # 2

Name: ________________________________	ID #: ___________

- When the modulation index of an AM wave is doubled, the antenna current is also doubled. The AM system being used is:

  - Single-sideband, full carrier

  - Vestigial sideband.

  - Single-sideband, suppressed carrier

  - Double sideband, full carrier

- Indicate which one of the following advantages of the phase cancellation method of obtaining SSB over the filter method is false:

  - Switching from one sideband to the other is simpler

  - It is possible to generate SSB at any frequency

  - SSB with lower audio frequencies present can be generated

  - There are more balanced modulators; therefore the carrier is suppressed better.

- The most commonly used filters in SSB generation are:

  - Mechanical

  - RC

  - LC

  - Low-pass

- In an SSB transmitter, one is most likely to find a:

  - Class C audio amplifier

  - Tuned modulator

  - Class B RF amplifier

  - Class A RF output amplifier

- Indicate in which one of the following only one sideband is transmitted:

  - H3E

  - A3E

  - B8E

  - C3F

- One of the following cannot be used to removed the unwanted sideband is SSB. This is the:

  - Filter system

  - Phase-shift method

  - Third method

  - Balanced modulator

- R3E modulation is sometimes used to:

  - Allow the receiver to have a frequency synthesizer

  - Simplify the frequency stability problem in reception

  - Reduce the power that must be transmitted

  - Reduce the bandwidth required for transmission

- Vestigial sideband modulation (C3F) is normally used for:

  - HF point-to-point communications

  - Monaural broadcasting

  - TV broadcasting

  - Stereo broadcasting