# University Diploma Programs

##### Electronic Equipment Maintenance

##### EET-027, Electronics Instrumentation

##### Lab Quiz # 2

- In the following bridge circuit shown below, R1=120 ohms and R2=120 ohms, resistance R3 is varied to balance the bridge and the value of R3 is set at 4.596 ohms. Find the value of X.

- In the following figure, the J-type thermocouple is used and heated, the value of V is measured as 5.159 Volts. Find the voltage V1 and temperature T1. The seebeck coefficient for J-type thermocouple is 51 V/oC.

- Experiment is setup according to the following figure with J-type thermocouple. The ambient temperature is found to be 21 oC. The voltage V is measured as 7.290 Volts. Find the voltage V1 and temperature T1. The seebeck coefficient for J-type thermocouple is 51 V/oC.