# University Diploma Program

# Electronic Equipment Maintenance

Lab Instructor: Muhammad Ajmal Khan

##### EET-027, Experiment # 5

# Thermocouple Voltage Measurement

Objectives:

To examine the thermocouple voltage and find corresponding temperature under the following conditions:

- To measure voltage of thermocouple without considering the intermediate thermocouple effect of measurement setup.

- To measure voltage of thermocouple with ice-point reference junction and fine corresponding voltage using the thermocouple table.

- To measure voltage of thermocouple using ambient reference block and calculate the corrected voltage and then find the corresponding temperature.

Apparatus:

J type thermocouples

4-1/2 digit DVM.

Temperature Indicator.

Ice point water

Boiling water

Theory:

Theory as per attached sheets.

Procedure:

- Setup the experiment as Figure 4 in theory sheets and measure voltage V.

V = _____________________

T = _____________________

- Setup the experiment as Figure 6 of theory sheets and measure voltage V and calculate V1. Find temperature (T1) corresponding to V1 from table.

where,

| V | V1 | T | T1 |
| --- | --- | --- | --- |

- Setup the experiment according to figure 12.

  - Note reference temperature, which will be ambient temperature from temperature indicator.

  - Measure V and find V1.

  - Find the temperature from table corresponding to V.

| TREF | V | V1 | T | T1 |
| --- | --- | --- | --- | --- |

- Compare voltages from setup 1, 2 and 3 and write your conclusions below.

Conclusions:

Explain:

Which set up gives the correct temperature?

Which set up gives maximum error?