Experiment # 7

MAGNETIC INDUCTION

# OBJECTIVE

To verify Faraday's law of induction. The induced voltage in the secondary circuit is measured as a function of the amplitude and frequency of the current in the primary circuit. The variation of the induced voltage with the number of turns and the cross-sectional area of the secondary circuit is also studied.

EQUIPMENT REQUIRED

- Frequency counter.

- Function generator.

- Digital multimeter.

- Analog multimeter.

- Voltage transformers 125/220 (two).

- Field coil 485 turns/meter, 750 mm long.

- Induction coil, 300 turns, 41 mm diameter.

- Induction coil, 300 turns, 33 mm diameter.

- Induction coil, 300 turns, 26 mm diameter.

- Induction coil, 200 turns, 41 mm diameter.

- Induction coil, 100 turns, 41 mm diameter.

INTRODUCTION

According to Faraday's law of induction, voltage can be induced in a circuit due to current passing through a nearby circuit. In this experiment, a large solenoidal field coil (item 6 in the equipment list) is used to generate a time-varying magnetic field by passing an AC current (I1) through it. Smaller coils (items 7-11 in the equipment list) are used for induction (see Figure 1).

The AC current I1 passing through the field coil produces a time-varying magnetic field given by:

(1)

where n is the turns density (turns/meter) of the coil. If the current I1 is sinusoidal and given by:

(2)

then, the induced voltage, v, in the induction coil is given by:

(3)

where a and N are the radius and the number of turns of the induction coil, respectively.

PROCEDURE

##### PART A: Induced voltage vs. current

- Connect the function generator to the field coil and to the frequency counter.

- Adjust the frequency to 10.7 kHz.

- Measure the amplitude of I1, using the analog multimeter.

- Insert the 300-turn, 41 mm diameter coil into the field coil. Insure that the coil is well into the field coil. Measure the induced voltage in the coil using the digital multimeter.

- Repeat for a range of I1 from 0 to 30mA.

Table 1: Induced Voltage vs. Current

f = 10.7 kHz,    N = 300 turns,   diameter = 2a = 41 mm

| Current I1 (mA) | Induced Voltage ‘v’ (Volts) | Theoretical ‘v’ (Volts) |
| --- | --- | --- |
| 0 |  |  |
| 5 |  |  |
| 10 |  |  |
| 15 |  |  |
| 20 |  |  |
| 25 |  |  |
| 30 |  |  |

##### PART B: Induced voltage vs. number of turns

- Fix the current I1 to 30mA and the frequency to 10.7 kHz. Measure the induced voltage across the 300-tum, 41 mm diameter coil.

- Repeat step (1) for the 200-turn, 41 mm diameter and the 100-turn, 41 mm diameter coils.

- Repeat step (1) for a 400-turn, 41 mm diameter coil (not provided but a combination can be used).

- Repeat step (1) for a 500-turn, 41 mm diameter coil.

Table 2: Induced Voltage vs. Number of Turns

f = 10.7 kHz,    I1 = 30 mA turns,   diameter = 2a = 41 mm

| No. of Turns N | Induced Voltage ‘v’ (Volts) | Theoretical ‘v’ (Volts) |
| --- | --- | --- |
| 200 |  |  |
| 300 |  |  |
| 400 |  |  |
| 500 |  |  |

##### PART C: Induced voltage vs. coil diameter

- Fix the current I1 to 30mA and the frequency to 10.7kHz. Measure the induced voltage across the 300-tum, 41 mm diameter coil.

- Repeat step (1) for the 300-tum coils of diameters 33 mm and 26 mm.

Table 3: Induced Voltage vs. Coil Diameter

f = 10.7 kHz,    I1 = 30 mA turns,   N = 300 turns

| Diameter mm | Induced Voltage ‘v’ (Volts) | Theoretical ‘v’ (Volts) |
| --- | --- | --- |
| 26 |  |  |
| 33 |  |  |
| 41 |  |  |

##### PART D: Induced voltage vs. frequency

- Fix the current I1 to 30mA and the frequency to 1 kHz. Measure the induced voltage across the 300-turn, 41 mm diameter coil.

- Repeat step (1) for a frequency range from 1 to 12 kHz (make sure that the current is maintained at 30mA each time you change the frequency).

Table 4: Induced Voltage vs. Frequency

I1 = 30 mA turns,   N = 300 turns,    Diameter = 2a = 41 mm.

| Frequency kHz | Induced Voltage ‘v’ (Volts) | Theoretical ‘v’ (Volts) |
| --- | --- | --- |
| 1 |  |  |
| 2 |  |  |
| 4 |  |  |
| 6 |  |  |
| 8 |  |  |
| 10 |  |  |
| 12 |  |  |

QUESTIONS FOR DISCUSSION

- Plot the experimental and the theoretical relations between the induced voltage and current, number of turns, coil diameter and frequency.

- From your experimental curves, find the induced voltage for the case: N=350, a= 15 mm, I1= 10mA and f=10 kHz.

- Use equation (3) to find a theoretical value of the induced voltage for the case in question (2). Compare with your answer of question (2). This is a good measure of the accuracy of your experimental results.