KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

University Diploma Programs

PHYS 012: Solid State Physics

Preparatory Classroom Building, Portable # 10

Hussein Tawfiq Magharbi (Office: 14/214, Tel: 4010)

E-mail: huseintm@kfupm.edu.sa

Lab Experiment _ Introduction to Oscilloscope.

NAME: ___________________________________________	ID: ___________________

==================================================================

Introduction To oscilloscopes: Vacuum Tubes (diodes, Triodes, thyratrons), CRTs (capacitive and inductive beam deflection mechanisms), Oscilloscopes.

- Plug the oscilloscope to the electric mains. Identify the oscilloscope switches:

  - Power on/off switch and turn the equipment on.

  - The vertical (A) input scale adjustment, range, calibration, and AC/DC/Ground selector switches.

  - The vertical (B) input scale adjustment, range, calibration, and AC/DC/Ground selector switches.

  - Time Base calibration and range switches.

  - Screen illumination switch.

  - Trigger selector switch.

  - Vertical and Horizontal trace beam alignment switches.

  - Inputs selector, add, and chop switches.

  - Grounding pins.

2.	Plug the function generator to the electric mains and turn on equipment. Select the sinusoidal waveform. Adjust he amplitude and frequency to 5 volts peak-to-peak (P-P) volts, and 1 KHz respectively. Display the waveform on the screen. Trace on paper the displayed waveform to scale. Measure and record the amplitude of the signal peak-to-peak and its frequency.

3.	Select the square waveform on the function generator. Adjust he amplitude and frequency to 10 volts (P-P) volts, and 2 KHz respectively. Display the waveform on the screen. Trace on paper the displayed waveform to scale. Measure and record the amplitude of the signal (P-P) and its frequency.

4.	Select the triangular waveform on the function generator. Adjust he amplitude and frequency to 15 volts (P-P) volts, and 2 Hz respectively. Display the waveform on the screen. Trace on paper the displayed waveform to scale. Measure and record the amplitude of the signal (P-P) and its frequency.

(Note: Attach all traces with the report and return to instructor on next lab period.)

Sunday, September 15, 2002.