# University Diploma Program

# Electronic Equipment Maintenance

Lab Instructor: Muhammad Ajmal Khan

##### EET-027, Experiment # 7

Strain Gauge Measurement using Strain Indicator

Objectives:

Find strain of the strain gauge using Strain Indicator.

Apparatus:

Strain gauge

Different Weights 1 kg, 2k, 5 kg.

Strain Indicator

Theory:

The strain gauge is a transducer employing electrical resistance variation to sense the strain produced by a force or weight. It is a very versatile detector for measuring weight, pressure, mechanical force, or displacement.

The Model P-3500 Strain Indicator is a portable, battery-powered instrument with unique features for use in stress analysis testing, and for use with strain gage based transducers. In use, the operator follows a logical sequence of setup steps by activating color-coded push-button controls to prepare the instrument for making accurate and reliable measurements. The P-3500 also incorporates a highly stable DC amplifier, precisely regulated bridge excitation supply, and precisely settable gage factor controls.

Static measurements are displayed directly on the indicator's readout with 1 micro-strain resolution. The instrument will accept full-, half-, or quarter-bridge strain gage inputs, and all required bridge completion components for 120, 350 and 1000 ohm gages are built in.

Gage factor is precisely settable (to a resolution of 0.001) by a front-panel 10-turn potentiometer, and is displayed on the digital readout when the gage factor push button is depressed.

Strain Indicator P-3500 Front Panel

Procedure:

The P-3500 is designed for ease of operation, the push-button switches and front panel controls are arranged such that the proper setup procedure generally follows a straightforward left-to-right sequence. To measure the strain, the steps is outlined below:

- Select 1/4-1 /2 position of BRIDGE push button.

- Select Xl position of MULT push button.

- Connect strain gage to binding posts connector. These binding posts are color-coded in accordance with conventional practice, and are clearly labeled. Input connections are shown on the inside cover of the instrument.

- Depress AMP ZERO push button. Allow instrument to warm up for two minutes minimum. Set AMP ZERO control for a readout display of ±0000. This adjustment must be made with MULT in Xl position.

- Depress GAGE FACTOR push button. Set GAGE FACTOR range switch and GAGE FACTOR control for the desired gage factor.

- Depress the RUN push button. Set the BALANCE switch and the BALANCE control for a reading of ±0000. This setting must be made with the MULT in the Xl position.

- Depress the CAL push button and verify calibration of the instrument.

- Select the Xl or Xl 0 MUL T position as required.

- Depress the RUN push button. Load the strain gage system using and record the reading in the table 1.

Table 1

| Load (kg) | Strain (micro-strain) |
| --- | --- |
| 0 |  |
| 1 |  |
| 2 |  |
| 3 |  |
| 4 |  |
| 5 |  |
| Unknown |  |

Find Unknown Load using Graph:

- Plot the readings obtained from tables 1 on the graph paper as strain versus load.

- Find the unknown load using strain versus load graph (obtained from table 1).

Unknown Load : _____________________ kg.

Conclusions: