Experiment 6: XOR Implementation And Parity Code

Objectives:

- Design and implementation of logic circuits using only XOR gates

- Design and implementation of a simple Parity Code Error Detection System

Equipment and IC’s:

- Proto-Board PB 503

- 1-IC 7493 4-bit Ripple Counter

- 3-IC’s 7486 Quadrable 2-input XOR gates

- IC 7404 Hex Inverter gates

- 5 PCB mount SPDT switches

- 8 extra LED’s

Part 1: XOR as an Odd function

| 1. A B C D L 0 0 0 0 0 0 0 1 0 0 1 0 0 0 1 1 0 1 0 0 0 1 0 1 0 1 1 0 0 1 1 1 1 0 0 0 1 0 0 1 1 0 1 0 1 0 1 1 1 1 0 0 1 1 0 1 1 1 1 0 1 1 1 1 | 2. F= 4. Distribution of 1’s in K-map does not allow any simplification |
| --- | --- |
| 3. |

3. Continue

| Functoin | Number of |
| --- | --- |
|  | Literals | Terms | Gates | IC’s |
| L using basic gates |  |  |  |  |
| L using XOR gates |  |  |  |  |

Part 2: Parity Bit Error Detection Circuit

1. The truth table for 4-bit Parity Generator function Pg is shown bellow:

2. Implementation of Pg with XOR gates is shown bellow: