Binary Arithmetic Operations

Objectives:

- Design and implementation of a circuit that performs  basic binary arithmetic operations such as addition, subtraction, increment and decrement.

- Use a multiplixer as a data selector:

Equipment:

- Proto-Board Pb-503

- Two IC’s 7493 4 bit- ripple counter

- Two IC’s 7408 2-in AN D

- One IC 7404 Hex Inverter

- Two IC’s 7432 2-in OR

- Two IC’s  7483 4-bit Full Adder

- One IC 2-in XOR

- Two IC’s 74153 Dual 4x1 Multiplexer

- Eight extra LED’s

Part 1: Binary Adder Circuits:

1.

3. The 4-bit binary adder operation test by a table;

| A3 | A2 | A1 | A1 | B3 | B2 | B1 | B0 | S3 | S2 | S1 | S0 | Cout |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |  |  |  |  |  |
| 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 |  |  |  |  |  |
| 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |

Part 2: Binary Arithmetic Circuit:

- The circuit is shown bellow for the decrement case. This circuit is taken directly from your lab manual