Abstract:

Gyrotropic planar phase shifters are widely used to control the radiation properties of phased array antennas. The design and performance of a microstrip array antenna with integrated ferrite phase-shifter is described. Calculated tunable differential phase shift and simulated beam scanning properties of the linear phased array antenna is presented and corroborated with measured results.