King Fahd University of 	Petroleum and Minerals

Department of Electrical Engineering

EE 418 Introduction to Satellite Communication

Section 01 (071)

Homework Assignment # 2 (Due Sunday, 25 November 2007)

As this homework set is relatively simple, you are asked to work on it alone. No cooperation between students is allowed in solving this homework assignment

- A satellite receiver has an overall System Temperature of TS = 97.45 K, and the following other specifications:

TIn  = 35 K

TRF = 50 K				GRF = 1000

TM  = 250 K			GM = 0.125

TIF  = Unknown			GRF = 10

- Find the noise temperature of the IF stage (TIF),

- If the bandwidth of the signal we are interested in is 20 MHz, find the noise power that would be accompanying this signal at  i) the output of the antenna, ii) the output of the RF stage, iii) the output of the mixer, and  iv) the output of the IF stage.

- We know that the System Noise Temperature   TS  is given by

So,

- The noise power that would accompany the signal at

- the output of the antenna is a function of  TIn  only

- the output of the RF stage is a function of  TIn  ,  TRF , and  GRF

- the output of the Mixer stage is a function of  TIn  ,  TRF , TM , GM and  GRF

- the output of the IF stage is a function of  TIn  ,  TRF , TM , TIF , GIF , GM and  GRF

Note that this could have also been obtained using

- A circular antenna on a GEO satellite is transmitting signals in the frequency range 10.2 GHz to 12.5 GHz. Determine the minimum diameter of the antenna in each case (consider the worst situation in each case) that will be able to provide:

  - a minimum 3-dB coverage area on Earth with a circular shape around the sub-satellite point with radius of 500 km,

  - a minimum antenna gain of 56.80 dB given that the antenna reflector has an efficiency of 0.7

a)	The altitude (not radius) of a GEO is (42,164 – 6,378 = 35,786 km)

So, a circular coverage area of radius 500 km will represent an angle of

So,

Now, consider the two frequency extremes knowing that the 3 dB beamwidth in degrees is given by   or  :

For an antenna to work for all of our frequency range and provide coverage to our area with radius of 500 km, it must have a radius of  1.125 m to do so. If the larger diameter was used, it will provide coverage for low frequencies around 10.2 GHz, but when frequency is increased, coverage area will become smaller than 500 km in radius.

a)	Consider the two frequency extremes knowing that the gain is given by     or    :

For an antenna to work for all of our frequency range and provide the minimum required gain, it must have a radius of  7.738 m to do so. If the smaller diameter was used, it will provide the required gain at the high frequency around 12.5 GHz, but when frequency is reduced, the gain will become smaller than 56.8 dB.

- Solve Problem 3 on page 93 of your textbook (Remember that the sun provides 1.39 kW/m2 of power. Part of this is absorbed by solar cells depending on their efficiency and that spinner satellites have an effective area of the satellites illuminated by the sun that is equal to Height * Width = Height * Circumference / π).

  - For the 3-axis stabilized satellite,

So,

Therefore,

If the width of the solar sail is 2 m, the length of would be  9.59 m.

  - For the spinner satellite,

So,

Therefore,

If the Diameter of the satellite is 3.5 m, its height would be  4.56 m.

- For a satellite downlink with the following specifications

| Satellite Output Power |  | 15.00 | W |
| --- | --- | --- | --- |
| Satellite Output Backoff |  | 2.5 | dB |
| Satellite Antenna Gain | Antenna Efficiency | 0.85 |  |
|  | Diameter | 1.20 | m |
| Edge of Beam Loss for Sat. Antenna |  | 3 | dB |
| Signal Bandwidth |  | 22 | MHz |
| Carrier Signal Frequency |  | 11.3 | GHz |
| Minimum Permitted C/N ratio at receiver |  | 16 | dB |
| Earth Station Antenna Gain | Antenna Efficiency | 0.6 |  |
|  | Diameter | 0.85 | m |
| Receiver Noise Specifications | Tin = 25 K |  |  |
|  | TRF = 35 K | GRF = 100 |  |
|  | TM = 100 K | GM = 0.1 |  |
|  | TIF = 200 K | GIF = 20 |  |
| Maximum Sat.-Earth Station Distance |  | 40000 | km |
| Clear Air Atmospheric Loss |  | 2 | dB |
| Rain Loss |  | 8 | dB |
| Other Losses |  | 1 | dB |

- Fill in the table given below with the proper results obtained from the table above both in linear units and in dB units (Include a sheet that shows all of your work). Remember that losses represent gains that are smaller than zero or negative dBs.

| Carrier Results |
| --- |
|  | Effective Satellite Transmitted Power |  |  | W |  | dBW |
|  | Satellite Antenna Gain |  |  | Linear |  | dB |
|  | Earth Station Antenna Gain |  |  | Linear |  | dB |
|  | Free Space Path Loss at Edge of Beam |  |  | Linear |  | dB |
|  | All Other Losses |  |  | Linear |  | dB |
|  | Earth Station Received Carrier Power |  |  | Linear |  | dB |
| Noise Results |
|  | Boltzmann's Constant |  |  | J/K |  | dB(W/K/Hz) |
|  | System Noise Temperature |  |  | K |  | dBK |
|  | Noise Bandwidth |  |  | MHz |  | dBHz |
|  | Earth Station Received Noise Power |  |  | W |  | dBW |
| C/N Ratio |
|  | C/N Ratio at Earth Station Antenna Output |  |  | Linear |  | dB |

- Determine if this system will satisfies the minimum system carrier to noise ratio (C/N) of not. Determine the (C/N) margin in dBs (remember that the (C/N) margin is positive if the system performs better than minimum (C/N) permitted and negative if does not).

- If you were able to modify the satellite antenna diameter only, what would be the new satellite antenna diameter that will give a (C/N) margin of +3 dB?

- If you were able to modify the satellite transmitted power, how much would the satellite transmit in W for the downlink to have (C/N) margin of +1 dB?

- Statistics indicate that the coverage area of this satellite experiences rain attenuation according to table below. If the (C/N) margin obtained in (b) is completely allocated to rain attenuation, how many hours a year will this downlink provide a (C/N) ratio below the minimum allowed (called outage time). Use interpolation between two points to find an accurate outage time.

| Attenuation (dB) | Duration (Hours a year) |
| --- | --- |
| 1 dB | 350 |
| 2 dB | 300 |
| 3 dB | 250 |
| 4 dB | 210 |
| 5 dB | 160 |
| 6 dB | 130 |
| 7 dB | 100 |
| 8 dB | 85 |
| 9 dB | 70 |
| 10 dB | 55 |
| 11 dB | 30 |
| 12 dB | 22 |
| 13 dB | 15 |
| 14 dB | 10 |
| 15 dB | 7 |
| 16 dB | 3 |

- To fill in the table, first consider the quantities given in the first table. Assume that these quantities are represented by the variables shown below:

| Satellite Output Power |  | Pmax | W |
| --- | --- | --- | --- |
| Satellite Output Backoff |  | Pbackoff | dB |
| Satellite Antenna Gain | Antenna Efficiency | (S |  |
|  | Diameter | DS | m |
| Edge of Beam Loss for Sat. Antenna |  | Ledge | dB |
| Signal Bandwidth |  | BWSignal | MHz |
| Carrier Signal Frequency |  | fc | GHz |
| Minimum Permitted C/N ratio at receiver |  | (C/N)min | dB |
| Earth Station Antenna Gain | Antenna Efficiency | (ES |  |
|  | Diameter | DES | m |
| Receiver Noise Specifications | Tin = 25 K |  |  |
|  | TRF = 35 K | GRF = 100 |  |
|  | TM = 100 K | GM = 0.1 |  |
|  | TIF = 200 K | GIF = 20 |  |
| Maximum Sat.-Earth Station Distance |  | Dist | km |
| Clear Air Atmospheric Loss |  | LA | dB |
| Rain Loss |  | LR | dB |
| Other Losses |  | LO | dB |

Now, the requested table can be filled easily using the following formulas (either the linear of the dB value is found in each case, the other one can be obtained easily using the 10 log (.) or 10( . /10)

| Carrier Results |
| --- |
|  | Effective Satellite Transmitted Power |  |  | W |  | dBW |
|  | Satellite Antenna Gain |  |  | Linear |  | dB |
|  | Earth Station Antenna Gain |  |  | Linear |  | dB |
|  | Free Space Path Loss at Edge of Beam |  |  | Linear |  | dB |
|  | All Other Losses |  |  | Linear |  | dB |
|  | Earth Station Received Carrier Power |  |  | Linear |  | dB |
| Noise Results |
|  | Boltzmann's Constant |  | 1.39*10-23 | J/K |  | dB(W/K/Hz) |
|  | System Noise Temperature |  |  | K |  | dBK |
|  | Noise Bandwidth |  | BWSignal | MHz |  | dBHz |
|  | Earth Station Received Noise Power |  | PN = (1.39*10-23)Ts BWSignal | W |  | dBW |
| C/N Ratio |
|  | C/N Ratio at Earth Station Antenna Output |  |  | Linear |  | dB |

b)	If (C/N) is greater than (C/N)min , the system is working fine, otherwise it is not working properly.

- The satellite antenna needs to be modified so that the C/N margin is only 3 dB. Weather the (C/N) in dB was positive or negative, the satellite antenna gain will be changed to make such that the new (C/N) is greater than (C/N)min  by only 3 dB. That is,

The new gain of the antenna    GS,new = GS,old – [(C/N) – ((C/N)min + 3)]   (All in dB)

Once the new gain is obtained, use  to obtain the new diameter

- The same concept as in (c) is applied here to make the C/N margin only 3 dB. Weather the (C/N) in dB was positive or negative, the satellite needs to transmit an amount of power in dB that is equal to

The new transmitted power    PT,new = PT,old – [(C/N) – ((C/N)min + 3)]   (All in dB)

- We will have to first obtain the total loss allocated to rain in dB. This can be obtained by adding using the following formula

LR,max = LR (8 dB as given in problem)  + [(C/N) – (C/N)min]    (All in dB)

Once this is found, use interpolation to find the amount of time (using the last table) by interpolation in the following form (for illustration, let   LR,max =  12.35 dB)

Solving for Toutage gives the required value.