| King Fahd University |  | of Petroleum & Minerals |
| --- | --- | --- |

Department of Electrical Engineering

EE 418 Introduction to Satellite Communications

Course Project II

(13 Marks out of 100)

Instructor

Dr. Wajih A. Abu–Al–Saud

Due Wednesday, 16 January 2008

(Last day of classes)

Note

Work on this project alone. No cooperation between students is allowed.

1.	Introduction

Project I of EE 418 discussed satellite orbits and how to get full coverage of the whole earth surface. In this project, we will study the process of designing a complete but simple satellite system including the uplink and downlink parts. So, you will have to design the (1) uplink earth station, (2) Satellite uplink receiving components, (3) Satellite downlink transmitting components, and (4) downlink earth station. The completed design of the satellite system is supposed to meet specific probability of bit error at the lowest cost for building the whole system and launching the satellite (we will assume that the cost of designing the system is zero as we are getting free service from you).

Since the design procedure requires a lot of computations especially that a trial and error process is generally employed to optimize the design and reduce the system cost, a computer program that will automate the computations is almost necessary. However, writing a program that will determine the carrier to noise ratio of a particular satellite link and the cost of the system is beyond the scope of this project. To assist you in the design, an MS Excel sheet is provided that will take your parameters and provide you with results. However, you as a designer will have to make many decisions to improve the system performance and keep the cost to a minimum. You will have to design the uplink and downlink parts separately and then combine your results, so you will have to try different scenarios and check if the whole system works in each case or not. The system you are designing involves a single uplink earth station, a single GEO satellite, and single downlink earth station. Certainly, if money was not an issue, you can pick the best components for your design. However, in real life, the better the components you pick for your design, the higher the cost of the system will be. In addition to the Excel sheet, a Matlab function that will compute the look angles from any point on earth to a satellite at any location is also provided.

2.	Project Description

The satellite system that you will design will link an Earth Station (uplink Earth Station) located at KFUPM, Dhahran, SA to another Earth Station (downlink Earth Station) at the Hong Kong University of Science and Technology (HKUST), Hong Kong, China using a GEO satellite that is located at 95.0( E. This link will use 64-QAM modulation to transmit digital data at a rate of 150 Mb/s. You do not need to know much about 64-QAM modulation other than that it uses 64 different pulses to transmit digital information. The provided Matlab program will give you the required look angles, the distances from the earth stations to the satellite to compute the path loss, and an approximate distance that the transmitted signal in the uplink and downlink will travel through the atmosphere to compute resulting atmospheric losses.

3.	Satellite System Specifications

The satellite system that you will design will be transmitting digital data from KFUPM to HKUST at the rate of RB =150 Mb/s and a maximum Bit Error Rate of   PB = 1*10-5 using 64-QAM. The figure below allows you determine the minimum needed Eb/No that corresponds to the required PB  in the following form:

- Using maximum PB given above ( determine the corresponding Eb/No from figure ( determine C/N using the throughput of the used modulation technique ( this C/N is the overall (C/N)overall that the combination of (C/N)uplink  with (C/N)downlink will have to satisfy.

- Knowing the required bit rate RB  ( use the thruput to determine the symbol rate RS ( Using RS  you can determine the minimum signal bandwidth required for zero-ISI transmission. This represents your signal and noise bandwidths.

To build your system, assume that you are picking components for the satellite and earth stations from a storehouse that contains components with different specifications and prices according to the following table (prices include the cost of launching the satellite so components that are used for satellites cost more than components used for earth stations).

Important Comments:

- Note that you will have to use the provided Excel sheet twice: once for computing the (C/N)uplink and uplink cost (call this Excel file “Uplink”) and once for computing the (C/N)downlink and downlink cost (call this Excel file “Downlink”). The total Carrier to noise ratio (C/N)overall  will be a combination of both and the total cost will be the cost of the uplink components plus the cost of the downlink components.

- It may be easier to design a system using the best components with the highest prices first, and then optimize your system by using a cheaper item for each component and observing the change in price (so use the cheapest components that do not reduce the performance (C/N) a lot).

- Our satellite is a simple relay satellite that does not process the data. We will assume that it uses a single frequency translation systems so it has (uplink RF stage, Mixer, downlink RF stage instead of the IF stage). The procedure for computing C/N using this configuration is exactly the same as what we learned in class.

- Assume that the earth station at KFUPM (uplink earth station) is a                 noiseless ideal system so the transmitted signal at its antenna contains no noise at all. Therefore, noise will result from the uplink path (TIN at satellite), the satellite components (TS of satellite), downlink path (TIN at receiving earth station), and downlink earth station components (TS of receiving earth station) only. This means that you have two complete satellite links.

The following Table gives the specification of the satellite system and costs of different components based on their specifications. Some specifications are given in terms of ranges so you can choose any value within the given range for each parameter. Some parameters have different ranges for satellites from earth stations (for example, a reflector antenna for an earth station may have a diameter of 5 m but this is to big for a satellite, so satellites rarely have reflector antennas with diameters more than 3 m or so). Also, the cost of components for earth stations are always lower than the cost of the same components for satellites because satellite components need to be space qualified and their cost includes the cost of launching into space.

a) 	Specifications of Satellite Components

(Assume other parameters not specified in table as you wish. These parameters have no effect on computations or cost)

|  |  |  | A |  | B |  | Cost Description | Cost (Million SR) of Component per Unit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameters of Transmitter Part of Satellite |  |  |
|  | Transmitter Maximum Output Power |  | 2 – 20 | W |  | dBW | Million SR per W of actual transmitted power | 0.50 |
|  | Transmitter Power Amplifier Backoff |  | 0.5 | Linear |  | dB |  |  |
|  | Transmitter Antenna Specifications | Antenna Efficiency () | 0.8 | Linear |  | dB | Million SR per unit of  | 1.00 |
|  |  | Diameter D (Assuming Circular) | 0.2 – 3.0 | m |  |  | Million SR per m2 of D2 | 0.50 |
|  |  | Theta 3dB [ = 75 * λ / D ] | - | Degrees |  |  |  |  |
|  |  | Gain [ = ( πD / λ)² ] | - | Linear |  | dB |  |  |
|  | Edge of Beam Loss (Specify loss at edge of area if transmitter is a satellite that covers an area of Earth. Set to 0 dB for point-to-point transmission) |  | Always = 0 Because earth station is at the center of Satellite antenna beam | Linear |  | dB |  |  |
| Parameters of Receiver Part of Satellite |  |  |
|  | Receiver Antenna Specifications | Antenna Efficiency () | 0.8 | Linear |  | dB | Million SR per unit of  | 1.00 |
|  |  | Diameter D (Assuming Circular) | 0.2 – 3.0 | m |  |  | Million SR per m2 of D2 | 0.50 |
|  |  | Theta 3dB [ = 75 * λ / D ] | - | Degrees |  |  |  |  |
|  |  | Gain [ = ( πD / λ)² ] | - | Linear |  | dB |  |  |
|  | Received Noise (at output of antenna) | Received Noise Temp TIN | 80 | K |  | dBK |  |  |
|  | RF Stage Noise and Gain | RF Stage Noise Temp TRF | 30 – 45 | K |  | dBK | Million SR per K lower than 50 | 0.05 |
|  |  | RF Stage Gain | 10 – 100 | Linear |  | dB | Million SR per Unit of Gain | 0.01 |
|  | Mixer Stage Noise and Gain | Mixer Stage Noise Temp TM | 100 – 300 | K |  | dBK | Million SR per K lower than 350 | 0.02 |
|  |  | Mixer Stage Gain | 0.2 | Linear |  | dB | Million SR per Unit of Gain | 3 |
|  | IF Stage Noise and Gain | IF Stage Noise Temp TIF | 200 – 900 | K |  | dBK | Million SR per K lower than 1000 | 0.01 |
|  |  | IF Stage Gain | 10 – 100 | Linear |  | dB | Million SR per Unit of Gain | 0.01 |

b)	Specifications of Earth Stations Components

(Assume other parameters not specified in table as you wish. These parameters have no effect on computations or cost)

|  |  |  | A |  | B |  | Cost Description | Cost (Million SR) of Component per Unit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Parameters of Transmitter Part of Earth Stations |  |  |
|  | Transmitter Maximum Output Power |  | 2 – 50 | W |  | dBW | Million SR per W of actual transmitted power | 0.10 |
|  | Transmitter Power Amplifier Backoff |  | 0.5 | Linear |  | dB |  |  |
|  | Transmitter Antenna Specifications | Antenna Efficiency () | 0.6 | Linear |  | dB | Million SR per unit of  | 1.00 |
|  |  | Diameter D (Assuming Circular) | 0.2 – 5.0 | m |  |  | Million SR per m2 of D2 | 0.20 |
|  |  | Theta 3dB [ = 75 * λ / D ] | - | Degrees |  |  |  |  |
|  |  | Gain [ = ( πD / λ)² ] | - | Linear |  | dB |  |  |
|  | Edge of Beam Loss (Specify loss at edge of area if transmitter is a satellite that covers an area of Earth. Set to 0 dB for point-to-point transmission) |  | Always = 0 Because satellite is at the center of Earth station antenna beam | Linear |  | dB |  |  |
| Parameters of Receiver Part of Earth Stations |  |  |
|  | Receiver Antenna Specifications | Antenna Efficiency () | 0.6 | Linear |  | dB | Million SR per unit of  | 1.00 |
|  |  | Diameter D (Assuming Circular) | 0.2 – 5.0 | m |  |  | Million SR per m2 of D2 | 0.20 |
|  |  | Theta 3dB [ = 75 * λ / D ] | - | Degrees |  |  |  |  |
|  |  | Gain [ = ( πD / λ)² ] | - | Linear |  | dB |  |  |
|  | Received Noise (at output of antenna) | Received Noise Temp T_IN | 60 | K |  | dBK |  |  |
|  | RF Stage Noise and Gain | RF Stage Noise Temp T_RF | 30 – 45 | K |  | dBK | Million SR per K lower than 50 | 0.05 |
|  |  | RF Stage Gain | 10 – 100 | Linear |  | dB | Million SR per Unit of Gain | 0.005 |
|  | Mixer Stage Noise and Gain | Mixer Stage Noise Temp T_M | 100 – 300 | K |  | dBK | Million SR per K lower than 350 | 0.01 |
|  |  | Mixer Stage Gain | 0.2 | Linear |  | dB | Million SR per Unit of Gain | 1.5 |
|  | IF Stage Noise and Gain | IF Stage Noise Temp T_IF | 200 – 900 | K |  | dBK | Million SR per K lower than 1000 | 0.005 |
|  |  | IF Stage Gain | 10 – 100 | Linear |  | dB | Million SR per Unit of Gain | 0.005 |

c)	Specifications of the Two Transmission Paths (Uplink and Downlink)

(Assume other parameters not specified in table as you wish. These parameters have no effect on computations or cost)

| Transmission Path |
| --- |
|  | Satellite-Earth Station Distance | R | From Matlab function | km |  |  |
|  | Clear Air Atmospheric Loss | L_A | 0.04 dB / km |  |  |  |
|  | Rain Loss (for each path) | L_R | 20 dB (per path) |  |  |  |
|  | Other Losses (for each path) | L_O | 8 dB (per path) |  |  |  |
| Uplink Parameters |  |  |
|  | Signal Bandwidth |  | 1 – 200 | MHz |  |  | Million SR per MHz of BW | 0.1 |
|  | Carrier Signal Frequency | Frequency fc | 4.00 | GHz |  |  |  |  |
| Downlink Parameters |  |  |
|  | Signal Bandwidth |  | 1 – 200 | MHz |  |  | Million SR per MHz of BW | 0.1 |
|  | Carrier Signal Frequency | Frequency fc | 3.00 | GHz |  |  |  |  |

4.	MS Excel Sheet

You are provided with a fully functioning MS Excel Sheet that will do most of the needed computations for you. All you have to do is provide it with a set of parameters and it will determine the resulting carrier to noise ratio, the cost of each component, and total cost of the satellite system one link at a time.

The following table is a copy of the table in the Excel sheet (this table is for illustration only. Values in this table are not correct).

| Satellite Link Design |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | A |  | B |  | Cost Description | Cost (Million SR) of Component per Unit | Total Cost (Million SR) for Component |
| Transmitter Parameters |  |  |  |
|  | Transmitter Maximum Output Power |  | 100.00 | W | 20 | dBW | Million SR per W of actual transmitted power | 0.50 | 2.51 |
|  | Transmitter Power Amplifier Backoff |  | 0.501 | Linear | -3.00 | dB |  |  |  |
|  | Transmitter Antenna Specifications | Antenna Efficiency () | 0.50 | Linear | -3.01 | dB | Million SR per unit of  | 1.00 | 2.96 |
|  |  | Diameter D (Assuming Circular) | 2.22 | m |  |  | Million SR per m2 of D2 | 0.50 |  |
|  |  | Theta 3dB [ = 75 * λ / D ] | 1.01 | Degrees |  |  |  |  |  |
|  |  | Gain [ = ( πD / λ)² ] | 27000.00 | Linear | 44.31 | dB |  |  |  |
|  | Edge of Beam Loss (Specify loss at edge of area if transmitter is a satellite that covers an area of Earth. Set to 0 dB for point-to-point transmission) |  | 0.501 | Linear | -3.00 | dB |  |  |  |
|  | Maximum Transmitter Bandwidth |  | 50.00 | MHz |  |  |  |  |  |
|  | Link Frequency range |  | 3.700 | GHz (MIN) | 4.5 | GHz (Max) |  |  |  |
| Transmitted Information Signal |  |  |  |
|  | Signal Bandwidth |  | 22.00 | MHz |  |  | Million SR per MHz of BW | 0.20 | 4.4 |
|  | Carrier Signal Frequency | Frequency fc | 10.00 | GHz |  |  |  |  |  |
|  | Carrier Signal Wavelength | Wavelength λ | 0.030 | m |  |  |  |  |  |
|  | Minimum Permitted C/N ratio at receiver |  | 40.00 | Linear | 16.02 | dB |  |  |  |
| Receiver Parameters |  |  |  |
|  | Receiver Antenna specifications | Antenna Efficiency () | 0.50 | Linear | -3.01 | dB | Million SR per unit of  | 1.00 | 2.96 |
|  |  | Diameter D (Assuming Circular) | 2.22 | m |  |  | Million SR per m2 of D2 | 0.50 |  |
|  |  | Theta 3dB [ = 75 * λ / D ] | 1.01 | Degrees |  |  |  |  |  |
|  |  | Gain [ = ( πD / λ)² ] | 27022.93 | Linear | 44.32 | dB |  |  |  |
|  | Received Noise (at output of antenna) | Received Noise Temp TIN | 30.00 | K | 14.77 | dBK |  |  |  |
|  | RF Stage Noise and Gain | RF Stage Noise Temp TRF | 50.00 | K | 16.99 | dBK | Million SR per K lower than 50 | 100 | 2 |
|  |  | RF Stage Gain | 500.00 | Linear | 26.99 | dB | Million SR per Unit of Gain | 0.001 | 0.5 |
|  | Mixer Stage Noise and Gain | Mixer Stage Noise Temp TM | 200.00 | K | 23.01 | dBK | Million SR per K lower than 250 | 0.02 | 1 |
|  |  | Mixer Stage Gain | 0.50 | Linear | -3.01 | dB | Million SR per Unit of Gain | 1 | 0.5 |
|  | IF Stage Noise and Gain | IF Stage Noise Temp TIF | 400.00 | K | 26.02 | dBK | Million SR per K lower than 500 | 0.01 | 1 |
|  |  | IF Stage Gain | 10.00 | Linear | 10.00 | dB | Million SR per Unit of Gain | 0.01 | 0.1 |
|  | Receiver System Gain and Noise Temperature | Receiver System Noise Temp TS | 82.00 | K | 19.14 | dBK |  |  |  |
|  |  | Receiver System Gain | 2500 | Linear | 33.97940009 | dB |  |  |  |
| Transmission Path |  |  |  |
|  | Satellite-Earth Station Distance | R | 40000.00 | km |  |  |  |  |  |
|  | Clear Air Atmospheric Loss | LA | 0.06 | Linear | -12.00 | dB |  |  |  |
|  | Rain Loss | LR | 0.01 | Linear | -20.00 | dB |  |  |  |
|  | Other Losses | LO | 0.15 | Linear | -8.24 | dB |  |  |  |
|  | Free Space Path Loss | LP [ = 1 / (4πR / λ)² ] | 3.56208E-21 | Linear | -204.4829647 | dB |  |  |  |
| Carrier Power Results |  |  |  |
|  | Effective Transmitted Power at Edge of Beam (or center point for point-to-point transmission) |  | 2.511886432 | W | 4.00 | dBW |  |  |  |
|  | Transmitter Antenna Gain |  | 27000 | Linear | 44.31 | dB |  |  |  |
|  | Receiver Antenna Gain |  | 27022.93 | Linear | 44.32 | dB |  |  |  |
|  | Free Space Path Loss |  | 3.56208E-21 | Linear | -204.48 | dB |  |  |  |
|  | All Other Losses |  | 9.46436E-05 | Linear | -40.24 | dB |  |  |  |
|  | Earth Station Received Carrier Power |  | 6.17861E-16 | Linear | -152.09 | dB |  |  |  |
| Noise Power Results |  |  |  |
|  | Boltzmann's Constant |  | 1.3804E-23 | J/K | -228.6 | dBW/K/Hz |  |  |  |
|  | Receiver System Noise Temperature |  | 2500.00 | K | 33.97940009 | dBK |  |  |  |
|  | Noise Bandwidth |  | 22.00 | MHz | 13.42422681 | dBHz |  |  |  |
|  | Receiver Noise Power |  | 6.17861E-16 | W | -181.1963731 | dBW |  |  |  |
| C/N Ratio |  |  |  |
|  | C/N Ratio at Receiving Antenna Output (or at Receiver IF Stage Output) | 969.86 | Linear | 29.10528322 | dB | Total Cost of Uplink-Downlink Components | 17.93 |

Sample of the Excel sheet you will use

This Excel sheet has three types of cells: 1) un-shaded cells are blank or have description text [do not modify these],  2) red-shaded cells are cells that take inputs [feel free to modify these as you wish, just remember that losses should be input as values smaller than 1 or negative values in dB], and 3) blue-shaded cells are cells that produce outputs [do not modify these]. Some of the red-shaded cells will sometimes change when you modify other input cells such as the cells that relate the reflector antenna efficiency, diameter, (3dB, and gain. Changing the gain of an antenna, for example, will result in modifying the diameter and (3dB cells so this will allow you to put the efficiency, the required gain, and the sheet will give you the required diameter.

You will have to put suitable values for all the parameters according the given specifications in the Satellite System Specifications part of this document.

Note: Remember that for the uplink, the parameters you will use for the transmitter part of the Excel sheet come from the Earth station parameters while the parameters you use for the receiver part of the sheet come from the satellite parameters. The opposite is true for the downlink. Also, note that you will have to enable Macros in MS Excel to be able to use the Excel sheet (Click on Tools ( Click on Macro ( Click on Security ( Choose “Medium”  ( Restart MS Excel ( Open the file, you will be informed that it contains macros and asked if you want to permit them or not ( Choose “Enable Macros”)

4.	Matlab Code

A Matlab function called “lookangles.m” is also provided, This will help you determine the look angles to the satellite from any point on earth, the distance to the satellite, and one more important quantity, which is the clear air atmospheric attenuation, which depends on the length of the path that the satellite signal travels through the atmosphere (this is certainly a function of the elevation angle). Put this file in the “work” directory of Matlab, and type “help lookangles” to get help on how to give it parameters and how to get results from it. This function will give you the length of the path from earth stations to the satellites in addition to the length of the path that the electromagnetic waves will travel through the atmosphere assuming the thickness of the atmosphere is 100 km (so all values you get for this parameter are always greater than or equal to 100 km and will depend on the elevation angle. This path length will result in atmospheric losses. We will assume that atmospheric loss has a value of 0.04 dB/km of path through the atmosphere.

5.	Report

An electronic report (MS Document) giving a brief introduction, your work and method of obtaining your design, tables from the two Excel sheets containing results of your final design that you are satisfied with, bill of materials (a complete list of components used in the design showing the cost of each component and total cost).

Also, your report must include a professionally generated (using MS Visio or any other professional program that allows generating block diagrams) showing a detailed block diagram of the uplink earth station, the GEO satellite, and the downlink earth station with all details on each component including antennas, RF stages, Mixers, IF stages, … (details of each component such as operating frequency, bandwidth, noise temperature, antenna diameters, and cost in million SRs must be shown on the figure). Also, show on your figure the look angles of the antennas of the two earth stations.  A brief conclusion about the project is also required. In addition to the MS Word document, please submit the two Excel sheets called “Uplink” and “Downlink”. Think of the report you will write as a report that you will submit to Wajih Telecom Inc. to convince the COE (named Wajih Abu-Al-Saud) that your design is the best design possible meeting all requirements at the lowest cost. So, include any additional information that you feel is suitable.