THE XLAT (transLATe) INSTRUCTION

The syntax of the XLAT instruction is:

XLAT

or

XLAT   TranslationTableName

where TranslationTable is an unsigned byte array of maximum size 256.

- The instruction requires BX to be initialized to have the offset of the translation table:

MOV  BX , OFFSET   TranslationTableName

- The contents of the byte that is AL bytes from the start of the translation table pointed to by DS:BX is copied into AL, i.e., the effect of XLAT is equivalent to the invalid statement:

MOV  AL  ,  [BX + AL]

- Example: Suppose a byte variable VAR1 has a value in the range 0 to 15. Display this value as a hexadecimal digit.

.DATA

HEXDIGIT   DB  ‘0123456789ABCDEF’

VAR1  DB  ?

.   .   .

MOV  AX , @DATA

MOV DS , AX

.   .   .

MOV  AL , VAR1

MOV  BX , OFFSET  HEXDIGIT

XLAT

MOV  DL , AL

MOV AH , 02H

INT  21H

.   .   .

If the value in VAR1 is, say, 12 then ‘C’ is copied to AL by the XLAT instruction. If AL contained a value not in the range 0 to 15, XLAT would translate it to some garbage value.

Note: We could have achieved what the above code is doing without using XLAT by:

.   .   .

MOV  AH , 02H

MOV  DL , VAR1

CMP  DL , 9

JBE  DIGIT

ADD  DL , 37H		; convert value to character in {‘A’ , ‘B’ , ‘C’ , ‘D’ , ‘E’ , ‘F’}

JMP  DISPLAY

DIGIT:	ADD  DL , 30H		; convert value to ASCII digit

DISPLAY:	INT  21H

.   .   .

- Example: Read an ASCII uppercase letter and then obtain the EBCDIC code for that letter

The EBCDIC hexadecimal codes for the uppercase letters are:

| ‘A’ | ‘B’ | ‘C’ | ‘D’ | ‘E’ | ‘F’ | ‘G’ | ‘H’ | ‘I’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C1H | C2H | C3H | C4H | C5H | C6H | C7H | C8H | C9H |

| ‘J’ | ‘K’ | ‘L’ | ‘M’ | ‘N’ | ‘O’ | ‘P’ | ‘Q’ | ‘R’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| D1H | D2H | D3H | D4H | D5H | D6H | D7H | D8H | D9H |

| ‘S’ | ‘T’ | ‘U’ | ‘V’ | ‘W’ | ‘X’ | ‘Y’ | ‘Z’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| E2H | E3H | E4H | E5H | E6H | E7H | E8H | E9H |

.DATA

EBCDIC  DB  0C1H , 0C2H , 0C3H , 0C4H , 0C5H , 0C6H , 0C7H , 0C8H , 0C9H

DB  0D1H , 0D2H , 0D3H , 0D4H , 0D5H , 0D6H , 0D7H , 0D8H , 0D9H

DB  0E2H , 0E3H , 0E4H , 0E5H , 0E6H , 0E7H , 0E8H

.   .   .

MOV  AX , @DATA

MOV DS , AX

LEA  BX , EBCDIC

MOV AH , 01H

INT  21H

SUB  AL , ‘A’		; put the offset in AL

XLAT

.   .   .

If the letter ‘K’ is, say, read then 0D2H is copied to AL by the XLAT instruction. If AL contained a value not in the range ‘A’ to ‘Z’, XLAT would translate it to some garbage value.

- The ASCII characters are arranged as follows:

| Number of characters | ASCII code ranges | Comment | Character type |
| --- | --- | --- | --- |
|  | Decimal | Hexadecimal |  |  |
| 32 | 0 – 31 | 00H – 1FH |  | NON-PRINTABLE |
| 16 | 32 – 47 | 20H – 2FH |  |  |
| 10 | 48 – 57 | 30H – 39H | ASCII digits |  |
| 7 | 58 – 64 | 3AH – 40H |  |  |
| 26 | 65 – 90 | 41H – 5AH | Uppercase letters | PRINTABLE |
| 6 | 91 – 96 | 5BH – 60H |  |  |
| 26 | 97 – 122 | 61H – 7AH | Lowercase letters |  |
| 5 | 123 – 127 | 7BH – 7FH |  |  |
| 128 | 128 – 255 | 80H - FFH |  | NON-PRINTABLE |

- Example: Character filtering

One use of XLAT is to filter out unwanted characters from a stream of text. Suppose we want to input a string of 20 characters from the keyboard but echo only those with ASCII values from 32 to 127 (i.e., only printable ASCII characters). We can set up a translation table, place a zero in each table position corresponding to a non-printable character, and place a one in each position corresponding to a printable character:

.DATA

VALIDCHARS  DB  32  DUP(0)		; invalid characters: 0 – 31

DB  96  DUP(1)		; valid characters: 32 – 127

DB  128  DUP(0)		; invalid characters: 128 – 255

.   .   .

MOV  AX ,  @DATA

MOV  DS ,  AX

.   .   .

MOV  BX ,  OFFSET  VALIDCHARS

MOV  CX , 20

GETCHAR:	MOV  AH , 08H			; input character, no echo

INT  21H

MOV  DL ,  AL			; save character in DL

XLAT

CMP  AL , 0

JE  GETCHAR			; reject non-printable character

MOV  AH ,  02H

INT  21H

LOOP  GETCHAR

- Example: Cryptography (Character encoding)

The XLAT instruction provides a simple way to encrypt and decrypt data. The following program encrypts text read into a buffer, such that all digits and alphabetic letters have been rearranged. The program then decrypts the encrypted text. The program uses the following translations:

ENCRYPTION			     DECRYPTION

4 5 9 0 8 2 1 3 6 7		3 6 5 7 0 1 8 9 4 2		keys

­ ­ ­ ­ ­ ­ ­ ­ ­ ­		­ ­ ­ ­ ­ ­ ­ ­ ­ ­

0 1 2 3 4 5 6 7 8 9		0 1 2 3 4 5 6 7 8 9		positions

__________________________________________________________________________

XQPOGHZBCADEIJUVFMNKLRSTWY		JHIKLQEFMNTURSDCBVWXOPYAZG	keys

­					      ­

ABCDEFGHIJKLMNOPQRSTUVWXYZ		ABCDEFGHIJKLMNOPQRSTUVWXYZ	positions

__________________________________________________________________________

xqpoghzbcadeijuvfmnklrstwy		jhiklqefmntursdcbvwxopyazg	keys

­					      ­

abcdefghijklmnopqrstuvwxyz		abcdefghijklmnopqrstuvwxyz	positions

.MODEL SMALL

.DATA

PROMPT  DB  'ENTER SOME TEXT TO BE ENCRYPTED (LENGTH <= 80):', 0DH, 0AH

LENGTH_PROMPT  EQU  $ - PROMPT

CRLF  DB  0DH , 0AH

LENGTH_CRLF  EQU  $ - CRLF

BUFFER  DB  81 , 82 DUP(?)

CODE_KEY     DB  48 DUP(0)                      			; no translation

DB  '4590821367'                   			; 0-9

DB  7  DUP(0)                     				; no translation

DB  'XQPOGHZBCADEIJUVFMNKLRSTWY'   	; A-Z

DB  6  DUP(0)                      			; no translation

DB  'xqpoghzbcadeijuvfmnklrstwy'   			; a-z

DB  133  DUP(0)                    			; no translation

DECODE_KEY   DB  48 DUP(0)                      			; no translation

DB  '3657018942'                   			; 0-9

DB  7  DUP(0)                      			; no translation

DB  'JHIKLQEFMNTURSDCBVWXOPYAZG'   	; A-Z

DB  6  DUP(0)                      			; no translation

DB  'jhiklqefmntursdcbvwxopyazg'   		; a-z

DB  133  DUP(0)                    			; no translation

.STACK  400H

.CODE

MAIN  PROC

MOV AX , @DATA

MOV DS , AX

MOV CX , LENGTH_PROMPT				; Display the prompt

LEA DX , PROMPT					;

CALL DISPLAY_STRING				;

LEA DX , BUFFER					; Read the message

CALL READ_STRING					;

LEA BX , CODE_KEY					; Encrypt the message

LEA DI , BUFFER[2]					;

MOV CH , 00H						;

MOV CL , BUFFER[1]					;

L1: 	MOV DL , [DI]						;

MOV AL , DL						;

XLAT							;

CMP AL , 0						;

JE L2							;

MOV [DI] , AL						;

JMP L3							;

L2: 	MOV [DI] , DL						;

L3: 	INC DI							;

LOOP L1

MOV CX , LENGTH_CRLF				; Move cursor to next line

LEA DX , CRLF						;

CALL DISPLAY_STRING				;

MOV CH , 00H						; Display the encrypted message

MOV CL , BUFFER[1]					;

LEA DX , BUFFER[2]					;

CALL DISPLAY_STRING				;

MOV CX , LENGTH_CRLF				; Move cursor to next line

LEA DX , CRLF						;

CALL DISPLAY_STRING				;

LEA BX , DECODE_KEY				; Display the decrypted message

LEA DI , BUFFER[2]					;

MOV CH , 00H						;

MOV CL , BUFFER[1]					;

L4: 	MOV DL , [DI]						;

MOV AL , DL						;

XLAT							;

CMP AL , 0						;

JE L5							;

MOV DL , AL						;

L5: 	MOV AH , 02H						;

INT 21H						;

INC DI							;

LOOP L4						;

MOV AX , 4C00H					; Return to DOS

INT 21H						;

MAIN  ENDP

DISPLAY_STRING  PROC

PUSH AX

PUSH BX

MOV AH , 40H

MOV BX , 01H

INT 21H

POP BX

POP AX

RET

DISPLAY_STRING  ENDP

READ_STRING  PROC

PUSH AX

MOV AH , 0AH

INT 21H

POP AX

RET

READ_STRING  ENDP

END MAIN