ARITHMETIC INSTRUCTIONS

Pentium provides arithmetic instructions for: Addition (ADD, ADC), incrementation (INC), subtraction (SUB, SBB), decrementation (DEC), comparison (CMP ), negation (NEG), multiplication (MUL, IMUL), and division (DIV, IDIV).

Each arithmetic instruction modifies one or more processor status flags.

Zero Flag (ZF): Tests the result of a flag modifying instruction whether zero or not. The Zero Flag is set if the result is zero; otherwise it is cleared.

The following conditional jump instructions may be used to react to the value of the zero flag: JZ, JE, JNZ, JNE

Carry Flag (CF): Tests for unsigned overflow. The carry flag is set if there is unsigned overflow; otherwise it is cleared.

The following conditional jump instructions may be used to react to the value of the carry flag: JC, JNC

Overflow Flag (OF): Tests for signed overflow. The overflow flag is set if there is signed overflow; otherwise it is cleared.

The following conditional jump instructions may be used to react to the value of the overflow flag: JO, JNO

Sign Flag (SF): This flag is useful only when dealing with signed numbers. The flag is set if the result is negative; otherwise it is cleared.

The following conditional jump instructions may be used to react to the value of the sign flag: JS (Jump if SF=1), JNS (Jump if no sign, i.e., SF=0)

Note: The processor does not know whether a given bit pattern represents a signed or unsigned number. It is up to the program logic to interpret a given bit pattern correctly, by using appropriate conditional jump instruction.

Auxiliary Flag (AF): The Auxiliary flag indicates whether an operation has produced a result that has generated a carry out of, or a borrow into, the low-order four bits of 8-, 16-, or 32-bit operands. The Auxiliary flag is set if there is such a carry or borrow; otherwise it is cleared.

Example:

# MOV AL, 43		; 00101011B

ADD AL, 94		; 01011110B

1			Carry out of 4 low order bits

00101011B

01011110B

10001001B

Thus the Auxiliary flag is set.

Note: There is no conditional jump instruction to test the value of the Auxiliary flag.

Parity Flag (PF): Only the low-order 8 bits of an 8-, 16-, or 32-bit operand are considered to set or clear the Parity flag. The parity flag is set if the low-order 8-bits contain an even number of 1 bits; otherwise it is cleared.

The following conditional jump instructions may be used to react to the value of the parity flag: JP, JPE (Jump if Parity Even, i.e., if PF=1), JNP, JPO (Jump if Parity Odd, i.e., if PF=0).

# ADD - Arithmetic Addition

Syntax:  		ADD     destination,	source

Effect:		destination ( destination + source

Modifies flags: AF CF OF PF SF ZF

Examples:

ADD  EBP, EAX

ADD  BYTE PTR [DI], 3

ADD  BX, [EAX + 2*ECX]

# ADC - Add With Carry

Syntax:	  	ADC     destination, source

Effect:		destination ( destination + source + CF

Modifies flags: 	AF CF OF SF PF ZF

ADC is used to add numbers that are wider than 16-bits in 8086 – 80286 processors, or wider than 32-bits in the 80386-80686 processors.

Example: Suppose we want to perform the following 32-bit addition in an 8086 – 80286 processor:

DX, CX ( DX, CX + BX, AX

Then the addition can be performed as:

ADD	CX, AX

ADC	DX, BX

Example: Suppose we want to perform the following 64-bit addition in 80386 – 80686 processor:

EDX, ECX ( EDX, ECX + EBX, EAX

The addition can be performed as:

ADD 	ECX, EAX

ADC 	EDX, EBX

# INC - Increment

Syntax:  		INC     destination

Effect:		destination ( destination + 1

Modifies flags: AF OF PF SF ZF

This instruction is often used to increment indexes and therefore does not affect the carry flag.

Thus the following instructions will not set the carry flag:

MOV AL, 255

INC AL	; value in AL is now 0

# SUB - Subtract

Syntax:  		SUB     destination, source

Effect:		destination ( destination - source

Modifies flags: AF CF OF PF SF ZF

# SBB - Subtract with Borrow/Carry

Syntax:  		SBB     destination, source

Effect:		destination ( destination – source - CF

Modifies flags: 	AF CF OF PF SF ZF

The most common use for this instruction is for subtractions that are wider than 16-bits in 8086 – 80286 microprocessors, or wider than 32-bits in 80386 – 80586 microprocessors. Wide subtractions require that borrows propagate through the subtraction.

Example: Perform the following 32-bit subtraction in an 8086 processor:

DX, CX ( DX, CX – BX, AX

The subtraction can be performed as:

SUB	CX,  AX

SBB	DX,   BX

# DEC - Decrement

Syntax:  		DEC     destination

Effect:		destination ( destination - 1

Modifies flags: 	AF OF PF SF ZF

This instruction is often used to decrement indexes and therefore does not affect the carry flag.

# NEG - Two's Complement Negation

Syntax:  		NEG     destination

Effect:		destination ( 0 - destination

Modifies flags: AF CF OF PF SF ZF

This instruction is meaningful only with signed operands. The carry flag is always set, except when the destination is 0, in which case it is cleared.

Example:

; compute the absolute value of EAX

CMP EAX, 0

JGE  DONE

NEG	EAX

DONE:

Note: The instructions:

MOV  AL,  -128		; minimum 8-bit signed value

NEG   AL

will set the Overflow flag; but will not modify AL

Similarly, the instructions:

MOV  AX,  -32768	; minimum 16-bit signed value

NEG   AX

will set the Overflow flag; but will not modify AX

# CMP - Compare

Syntax:  		CMP     destination,  source

Modifies flags: AF CF OF PF SF ZF

Effect: Subtracts source from destination and updates the flags but does

not save result.  Flags can subsequently be checked for conditions.

If the destination is a 16-bit or 32-bit operand and source is a 8-bit immediate value, source is sign-extended to match the size of destination.

MULTIPLICATION INSTRUCTIONS (MUL AND IMUL)

Signed and unsigned multiplication lead to different results. Example, consider: 10000000B  *  11111111B. Interpreted as unsigned numbers, the product is:  128  *  255  =  32640  =  0111 1111 1000 0000B. Interpreted as signed numbers, the product is: -128  *  -1  =  128  =  0000 0000 1000 0000B.

Because signed and unsigned multiplication lead to different results, there are two multiplication instructions: MUL for unsigned multiplication and IMUL for signed multiplication:

|  | Instruction syntax | Effect |
| --- | --- | --- |
| 8-bit multiplication | MUL Source8 | AX ( AL * Source8 |
|  | IMUL Source8 |  |
| 16-bit multiplication | MUL Source16 | DX:AX ( AX * Source16 |
|  | IMUL Source16 |  |
| 32-bit multiplication | MUL Source32 | EDX:EAX ( EAX * Source32 |
|  | IMUL Source32 |  |

Where: (i) Source8 is either an 8-bit register or an 8-bit memory operand.

(ii) Source16 is either a 16-bit general-purpose register or a 16-bit memory operand.

(iii) Source32 is either a 32-bit general-purpose register or a 32-bit memory operand.

Two- and three-operand forms of IMUL

| Instruction Syntax | Effect |
| --- | --- |
| IMUL register1, register2 | register1 ( register1 * register2 |
| IMUL register, memory | register ( register * memory |
| IMUL register, immediate | register ( register * immediate |
| IMUL register1, register2, immediate | register1 ( register2 * immediate |
| IMUL register, memory, immediate | register ( memory * immediate |

In these forms of IMUL, the register and memory operands must all be of the same size. The registers are general-purpose registers. The immediate operand is treated as signed, if it sign-extended to the size of the destination operand, if its size is smaller.

Examples:

IMUL  ECX		; EDX:EAX ( EAX * ECX

IMUL  BL,  CH,  7	; BL ( CH * 7

Note:

- For multiplication of positive numbers, MUL and IMUL give the same results.

- For IMUL, if the result of an 8-bit multiplication is 8-bits, it is sign-extended into the AH register. If the result of a 16-bit multiplication is 16-bits, it is sign-extended into the DX register. Similarly, if the result of a 32-bit multiplication is 32-bit, it is sign-extended into the EDX register.

Both MUL and IMUL leave all status flags undefined, except the Carry flag and the Overflow flag.

Multiplication overflow

- Effect of MUL on the Carry Flag (CF) and the Overflow Flag (OF)

Both the Carry Flag and the Overflow Flag are cleared if the upper half of the result (AH for 8-bit MUL,  DX for 16-bit MUL, and EDX for 32-bit MUL) is zero; otherwise they are set.

- Effect of IMUL on the Carry Flag (CF) and the Overflow Flag (OF)

Both the Carry Flag and the Overflow Flag are cleared if the upper half of the result (AH for 8-bit IMUL, DX for 16-bit IMUL, and EDX for 32-bit IMUL) is the sign-extension of the lower half (AL for 8-bit IMUL, and DX for 16-bit IMUL); otherwise they are set.

For two- or three-operand IMUL, the CF and OF are cleared if the multiplication result is within the range, of signed numbers, of the destination operand; otherwise they are set

Thus, for both MUL and one-operand IMUL, if CF and OF are set it means that the product is too big to fit in the lower half of the destination (AL for 8-bit multiplication, AX for 16-bit multiplication, and EAX for 32-bit multiplication).

Note: Unlike an overflow condition resulting from ADD, SUB, NEG, SHL, or SAL, (which indicate an error in computation) an overflow condition resulting from MUL or IMUL may or may not indicate an error in computation. The interpretation of an error condition or otherwise depends on the application program being developed. For example, in the 16-bit decimal input algorithms developed latter in this chapter, a multiplication overflow indicates an error, because in those algorithms, the number input must fit in 16-bits.

Detection of Multiplication overflow in a program

Both signed and unsigned multiplication overflow can be detected by constructs of the form:

.   .   .

Multiplication instruction

JC  MULTIPLICATION_OVERFLOW

.   .   .

JMP  DONE

MULTIPLICATION_OVERFLOW:

.   .   .

DONE:

or	.   .   .

Multiplication instruction

JO  MULTIPLICATION_OVERFLOW

.   .   .

JMP  DONE

MULTIPLICATION_OVERFLOW:

.   .   .

DONE:

Example:

.   .   .

MOV  AX , 50

MUL  BX

JC  MULTIPLICATION_OVERFLOW

.   .   .

JMP  DONE

MULTIPLICATION_OVERFLOW:

.   .   .

DONE:

Example: In each of the program fragments below, determine whether multiplication overflow will occur or not. Find also the result in the destination operand(s):

- MOV  AL , 05H

MOV  BL , 10H

MUL  BL		; AX :=  AL * BL = 0050H ,  CF := 0 , OF := 0 , there is no overflow

- .DATA

VAR1  DW  2000H

VAR2  DW  0010H

.   .   .

MOV  AX ,  VAR1

MUL  VAR2	; DX:AX := AX * VAR2 = 0002 0000H , CF := 1 , OF := 1 , there is overflow

- MOV  AL , 1

MOV  BL , -1

IMUL  BL	; AX := -1 = 11111111 11111111B , CF := 0 , OF := 0 , there is no overflow

; the 8-bit result 11111111B is sign-extended into the AH register.

- MOV  AX , 10

MOV  CX , -48

IMUL  CX	; DX:AX := -480 = FFFF FE20H , CF := 0 , OF := 0 , there is no overflow

; the 16-bit result FE20H is sign-extended into the DX register.

Example: Assuming that W and Y are word variables holding signed values, translate W := 5 * W  - 12 * Y into an 8086 program fragment. The fragment must test for signed overflow.

MOV  AX ,  5

IMUL  W		; AX :=  5 * W

JO  OVERFLOW

MOV  W ,  AX		; W :=  5 * W

MOV  AX ,  12

IMUL  Y		; AX :=  12 * Y

JO  OVERFLOW

SUB  W ,  AX		; W := 5 * W - 12 * Y

JO  OVERFLOW

.   .   .

JMP  DONE

OVERFLOW:

.   .   .

DONE:

Example: Perform an unsigned multiplication on a byte variable VAR1 and a word variable VAR2, and store the result in a double-word variable VAR3 :

.DATA

VAR1  DB  20H

VAR2  DW  1234H

VAR3  DD  ?

.   .   .

MOV  AX ,  VAR2

MOV  BH ,  0

MOV  BL ,  VAR1

MUL  BX

MOV  WORD  PTR  VAR3 ,  AX

MOV  WORD  PTR  VAR3 + 2 , DX

.   .   .

Example: Let N be a word variable holding an unsigned value. Assuming no multiplication overflow, write a program fragment to leave the factorial of N in the AX register.

MOV  AX ,  1

MOV  CX ,  N

JCXZ  EXIT

TOP:	MUL  CX

LOOP  TOP

EXIT:

DIVISION INSTRUCTIONS (DIV AND IDIV)

DIV is used for unsigned division, and IDIV for signed division.

|  | Instruction syntax | Effect |
| --- | --- | --- |
| 8-bit division | DIV Divisor8 | AL Divisor8 AX - Divisor8 * AL AH |
|  | IDIV Divisor8 |  |
| 16-bit division | DIV Divisor16 | AX Divisor16 DX:AX - Divisor16 * AX DX |
|  | IDIV Divisor16 |  |
| 32-bit division | DIV Divisor32 | EAX Divisor32 EDX:EAX - Divisor32 * EAX EDX |
|  | IDIV Divisor32 |  |

Where: (i) Divisor8 is either an 8-bit register or an 8-bit memory operand.

(ii) Divisor16 is either a 16-bit general-purpose register or a 16-bit memory operand.

(iii) Divisor32 is either a 32-bit general-purpose register or a 32-bit memory operand.

Note:

- If both dividend and divisor are positive, DIV and IDIV give the same result.

(ii) For a signed division, the remainder, if not zero, has the same sign as the dividend.

- The division instructions do not set flags to any useful values. They may destroy previously set values of CF, OF, SF and ZF flags.

Initialisation of the AH register before an 8-bit division

- For a DIV instruction, the AH register must be initialised to 0 if the actual dividend is a byte; however if the actual dividend is a word then no initialisation is required.

Example:	MOV  AL ,  BYTE_VAR

MOV  AH ,  0			; AH must be initialised to 0

MOV  BL ,  5

DIV  BL

Example:	MOV  AX ,  20			; no initialisation of AH required

MOV  CL ,  4

DIV  CL

Example: Read an ASCII digit, convert it to a numeric value, and then divide it by 3:

MOV  AH ,  01H

INT  21H

SUB  AL ,  30H

MOV  AH ,  0			; initialise AH to 0

MOV  BL ,  3

DIV  BL

Note: The instruction MOVZX (Move with Zero Extension) may also be used to initialise AH to zero:

MOVZX AX,  BYTE_VAR

MOV  BL,  5

DIV  BL

- For IDIV instruction, the sign-bit of AL must be extended throughout the AH register. This is done by the instruction:

CBW			; Convert Byte to Word

Example: 	MOV  AL ,  VAR1

CBW

MOV  BL ,  -7

IDIV  BL

Note: If CBW instruction is not used to initialise AH before an 8-bit, signed division, the result of the division may be wrong. Consider:

MOV  AX ,  -48

MOV  BL , 5

IDIV  BL

48d = 30H = 00110000B

2's complement

-48d	   = 11010000B

Thus AX will contain 0000000011010000B , which is +208 and not -48. However, if the division is performed as:

MOV  AX ,  -48

CBW

MOV  BL ,  5

IDIV  BL

Then the instruction CBW extends the sign bit of AL into AH. Hence, AX will contain 1111111111010000B i.e., FFD0H which is the 16-bit representation of -48.

The instruction MOVSX (Move with Sign Extension) may also be used to initialise AH:

MOVSX   AX,  -48

MOV  BL,  5

IDIV  BL

Initialisation of the DX  register before a 16-bit division

- For a 16-bit DIV instruction, the DX register must be initialised to 0.

Example:	.DATA

DIVIDEND  DW  8003H

DIVISOR  DW  100H

.   .   .

MOV  DX ,  0

MOV  AX ,  DIVIDEND

DIV  DIVISOR

.   .   .

- For a 16-bit IDIV instruction, the sign-bit of AX must be extended throughout the DX register. This is done by the instruction:

CWD			; Convert Word to Double-word

Example:	MOV  AX ,  -12			; AX :=  FFF4H

CWD				; DX:AX :=  FFFF FFF4H

MOV  BX ,  7

IDIV  BX			; AX := -1 = FFFFH , DX := -5 = FFFBH

Initialisation of the EDX  register before a 32-bit division

- For a 32-bit DIV instruction, the EDX register must be initialised to 0.

Example:	.DATA

DIVIDEND  DWORD  8003FFBCH

DIVISOR  DWORD  10000000H

.   .   .

MOV  EDX ,  0

MOV  EAX ,  DIVIDEND

DIV  DIVISOR

.   .   .

- For a 32-bit IDIV instruction, the sign-bit of EAX must be extended throughout the EDX register. This is done by the instruction:

CDQ			; Convert Double-Word to Quad-word

Example:	MOV  EAX ,  8FBA2FECh

CDQ

MOV  EBX ,  2FFFFFFFh

IDIV  EBX

Division overflow

If the quotient of either an 8-bit or a 16-bit division is too big to fit in an8-bit or a 16-bit register, respectively, then division overflow occurs. The CPU then automatically invokes software interrupt 00H and the program terminates or the system hangs.

- Unsigned division overflow

Unsigned division overflow will only occur if the divisor is below or equal to the high-order register in the dividend (AH for 8-bit division, DX for 16-bit division, and EDX for 32-bit division).

Example: The sequence:	MOV  AX ,  0200H

MOV  BL ,  02H

DIV  BL

Causes division overflow, because BL ( AH. Note that the quotient in this case is 100H i.e., 256 which is above 255, the maximum 8-bit unsigned value.

Note: If AH is initialised to 0 before an unsigned division, overflow can only occur if the divisor has the value zero.

To avoid an 8-bit, unsigned, division-overflow in a program, a sequence like the one below can be used:

CMP  Divisor8  ,  AH

JBE  DIV_OVERFLOW

DIV  Divisor8

.   .   .

JMP  DONE

DIV_OVERFLOW:

.   .   .

DONE:

To avoid a 16-bit, unsigned, division-overflow in a program, a sequence like the one below can be used:

CMP  Divisor16  ,  DX

JBE  DIV_OVERFLOW

DIV  Divisor16

.   .   .

JMP  DONE

DIV_OVERFLOW:

.   .   .

DONE:

- Signed division overflow

For an 8-bit signed division in which the AH register is initialised by the instruction CBW, overflow can only occur if either the divisor has the value zero or if the divisor has the value -1 and the dividend in AL is –128 (i.e., 80H, the minimum 8-bit signed value). For a 16-bit signed division in which the DX register is initialised by the instruction CWD, overflow can only occur if either the divisor has the value zero or if the divisor has the value -1 and the dividend in AX is –32768 (i.e., 8000H, the minimum 16-bit signed value). For a 32-bit signed division in which the EDX register is initialised by the instruction CDQ, overflow can only occur if either the divisor has the value zero or if the divisor has the value –1 and the dividend in EAX is –2147483648 (i.e., 80000000H, the minimum 32-bit signed value).

To avoid an 8-bit, signed, division-overflow in a program, a sequence like the one below can be used:

MOV  AL ,  Dividend

CBW

CMP  Divisor8 , 0

JE  IDIV_OVERFLOW

CMP  Divisor8 , -1

JNE   L1

CMP  AL ,  -128

JNE  L1

JMP  IDIV_OVERFLOW

L1:	IDIV  Divisor8

.   .   .

JMP  DONE

IDIV_OVERFLOW:

.   .   .

DONE:

To avoid a 16-bit, signed, division-overflow in a program, a sequence like the one below can be used:

MOV  AX ,  Dividend

CWD

CMP  Divisor16 , 0

JE  IDIV_OVERFLOW

CMP  Divisor16 , -1

JNE   L1

CMP  AX ,  -32768

JNE  L1

JMP  IDIV_OVERFLOW

L1:	IDIV  Divisor16

.   .   .

JMP  DONE

IDIV_OVERFLOW:

.   .   .

DONE:

DECIMAL I/O ROUTINES

- Unsigned Decimal Output (Algorithm#1)

Write a procedure to display the unsigned contents of AX in decimal.

Assuming that num is the unsigned number to be displayed in decimal, the pseudo-code algorithm is:

count  :=  0 ;

do

{

quotient  :=  num / 10 ;

remainder  :=  num % 10 ;

PUSH the remainder in the stack ;

num :=  quotient ;

count  :=  count  +  1 ;

}while( quotient  (  0 ) ;

for (count times )do

{

POP remainder from the stack ;

Convert remainder to ASCII ;

Display: remainder ;

} ;

STOP ;

This pseudo-code algorithm can be refined to the following pseudo-code algorithm:

count  :=  0 ;

do

{

clear DX to zero ;

divide AX by 10 ;

PUSH the remainder DX in the stack ;

count  :=  count  +  1 ;

}while( AX  (  0 ) ;

for (count times )do

{

POP remainder DX from the stack ;

DL  :=  DL  +  30H ;					Note, in this case DH is always zero

Display: DL ;

}

STOP ;

The required procedure is then:

WRITE_UNSIGNED_DECIMAL16  PROC uses AX  BX  CX  DX

; Displays the contents of AX as an unsigned decimal value.

MOV  CX , 0			; counter

MOV  BX , 10			; divisor

@1:	MOV  DX , 0			; initialise the high-order register of the dividend DX:AX

DIV  BX			; AX := quotient ,   DX := remainder

PUSH  DX			; save the remainder

INC  CX

CMP  AX , 0			; compare the quotient with zero

JA  @1

; Display

MOV  AH , 02H

@2:	POP  DX			; pop a remainder

ADD  DL , 30H			; convert to ASCII

INT  21H

LOOP  @2

RET

WRITE_UNSIGNED_DECIMAL16  ENDP

Note:

- The above procedure will display the unsigned contents of AX in binary if the divisor is 2.

- The XLAT instruction can be used in conjunction with the above procedure to display an unsigned number in any base in the range 2 to 16. This is done in procedure WRITE_UNSIGNED on the next page.

- Unsigned Output.

WRITE_UNSIGNED  PROC uses AX  BX  CX  DX  DS

; Displays the unsigned contents of AX using the base in SI. The base must be in the range 2 to 16.

MOV  DX ,  CS

MOV  DS ,  DX

MOV  CX , 0

CMP  SI , 2

JB   INVALID_BASE

CMP  SI , 16

JA   INVALID_BASE

@1:	MOV  DX , 0

DIV  SI

PUSH  DX

INC  CX

CMP  AX , 0

JA  @1

LEA  BX , HEXDIGITS

@2:	POP  AX

XLAT

MOV  DL , AL

MOV  AH , 02H

INT  21H

LOOP  @2

CMP  SI , 2

JE  BINARY

CMP  SI , 8

JE  OCTAL

CMP  SI , 10

JE  DECIMAL

CMP  SI , 16

JE  HEXADECIMAL

JMP  EXIT

INVALID_BASE:	MOV  AH ,  09H

LEA DX ,  ERROR_MSG

INT 21H

JMP EXIT1

BINARY:	MOV  DL , 'B'

JMP  EXIT2

OCTAL:	MOV  DL , 'o'

JMP  EXIT2

DECIMAL:	MOV  DL , 'd'

JMP  EXIT2

HEXADECIMAL:	MOV  DL , 'H'

EXIT2:	MOV  AH , 02H

INT  21H

EXIT1:

RET

HEXDIGITS  DB  '0123456789ABCDEF'

ERROR_MSG  DB  0DH, 0AH, 'ERROR - INVALID BASE', '$'

WRITE_UNSIGNED ENDP

- Signed Decimal Output.

Write a procedure to output the signed contents of AX.

The pseudo-code algorithm is:

if( AX  (  0 )then

{

if( AX =  -32678 )then

{

display: "-32678" ;

STOP ;

}

else

{

display: '-'  ;

NEG  AX  ;

}

endif  ;

}

endif  ;

count  :=  0 ;

do

{

clear DX to zero ;

divide AX by 10 ;

PUSH the remainder DX in the stack ;

count  :=  count  +  1 ;

}while( AX  (  0 ) ;

for (count times )do

{

POP remainder DX from the stack ;

DL  :=  DL  +  30H ;					Note, in this case DH is always zero

Display: DL ;

}

STOP ;

Note: In this algorithm, the case of AX having the value -32678 is special in that we cannot perform the operation NEG AX without causing unsigned overflow.

The required procedure is:

WRITE_SIGNED_DECIMAL16  PROC uses AX  BX  CX  DX

; Displays the contents of AX as a signed decimal value.

CMP  AX , 0

JGE  @2

CMP  AX , -32768		; minimum 16-bit unsigned value

JNE  @1

PUSH  DS

MOV  DX  ,  CS

MOV  DS  ,   DX

MOV  AH , 09H

LEA  DX , MINVALUE

INT  21H

POP  DS

JMP  EXIT1

@1:	PUSH  AX

MOV  AH , 02H

MOV  DL , '-'

INT  21H

POP  AX

NEG  AX

@2:	MOV  CX , 0			; counter

MOV  BX , 10			; divisor

@3:	CWD				; sign-extend AX into DX

IDIV  BX

PUSH  DX			; save the remainder

INC  CX

CMP  AX , 0

JG  @3

; Display

MOV  AH , 02H

@4:	POP  DX			; pop a remainder

ADD  DL , 30H			; convert to ASCII

INT  21H

LOOP  @4

EXIT1:

RET

MINVALUE DB '-32768', '$'

WRITE_SIGNED_DECIMAL16  ENDP

- Unsigned Decimal Input

Write a procedure to read an unsigned 16-bit decimal number in the BX register. The procedure should set the Carry Flag if there is overflow or if no value is entered. For an invalid input the procedure should beep and give the user the chance of entering another value.

A number such as 53248 is read as a sequence of ASCII digits '5', '3', '2', '4', '8'. Each ASCII digit in the sequence must then be converted to a numeric value, multiplied by an appropriate factor 10i  ( i  ( {0, 1, 2, 3, 4}), and finally summed up:

'5'                        '3'	             '2'	          '4'		      '8'

-30H	                    -30H		      -30H		   -30H	                -30H

( 5     *  10000) 	  +       ( 3  *  1000)  +    ( 2  *  100)   +    ( 4  *  10)    +               8

Assuming valid input, the pseudo-code algorithm to do the reading is:

sum  :=  0  ;

multiplier  :=  10000 ;

for( 5 times )do			; a 16-bit decimal value has a maximum of 5 digits

{

Read: ch  ;

ch  :=  ch  -  30H			; convert to numeric value

sum  :=  sum  +  ch  *  multiplier  ;

multiplier  :=  multiplier /  10 ;

};

STOP ;

The disadvantage with this algorithm is that 5 digits must be input for each number read. So, for example, the number 6 must be input as 00006. However, using Horner's factorisation, an expression of the form:

( 5   *  10000)   +   ( 3  *  1000)  +   ( 2  *  100)   +   ( 4  *  10)    +     8

can be factorised to:

10 * ( 10 * ( 10 * ( 5 * 10  +  3)  +  2 )  +  4 )  +  8

Assuming no invalid input, the pseudo-code algorithm to read an unsigned decimal number using this factorised form is:

count  :=  0 ;

sum  :=  0 ;

do

{

Read: ch ;

if( ch  =  0DH)then

break ;

endif ;

ch  :=  ch  -  30H  ;

sum  :=  10  *  sum  ;

sum  :=  sum  +  ch  ;

count  :=  count  +  1  ;

}while( count  (  5 ) ;

STOP ;

Refining the previous algorithm to incorporate input validity checking we have:

count  :=  0 ;

sum  :=  0 ;

do

{

Read: ch ;

if( ch  =  0DH)then

goto  exit ;

endif ;

if( ch  (  '0'  and  ch  (  '9' )then

{

count  :=  count  +  1  ;

ch  :=  ch  -  30H  ;

sum  :=  10  *  sum  ;

if( UnsignedMultiplicationOverflow )then

goto  errorLabel ;

endif  ;

sum  :=  sum  +  ch  ;

if( UnsignedAdditionOverflow )then

goto  errorLabel  ;

endif  ;

}

else

{

Beep  ;

Move the cursor back ;

}

endif  ;

}while( count  (  5 ) ;

exit:		if( count  =  0 )then

Display: “ERROR – NO VALUE OR NO VALID VALUE ENTERED”

STC				; set Carry flag  (No input)

else

CLC				; clear Carry flag

endif

goto  done ;

errorLabel:	Display: “ERROR - UNSIGNED OVERFLOW”

STC  ;

done:

STOP ;

The previous algorithm is translated into the following procedure:

READ_UNSIGNED_DECIMAL16  PROC uses AX  CX  DX

comment @

Reads an unsigned decimal number in the range 0 - 65535 in BX. The procedure rejects invalid input by beeping and backspacing the cursor. If there is unsigned overflow or if no value or no valid value is entered before the enter key is pressed, an appropriate error message is displayed and the Carry flag is set.

@

MOV  BX , 0

MOV  CX , 0

L1:  MOV  AH , 01H

INT  21H

CMP  AL , 0DH

JE  END_DO_WHILE

CMP  AL , '0'

JB  INVALID

CMP  AL , '9'

JA  INVALID

INC  CX

SUB  AL , 30H

MOV  AH , 0

PUSH  AX

MOV  AX , 10

MUL  BX

POP  BX

JC  OVERFLOW

ADD  BX , AX

JC  OVERFLOW

JMP  NEXT

INVALID: MOV  AH , 02H		; beep

MOV  DL , 07H			;

INT  21H			;

MOV  DL , 08H			; backspace

INT  21H			;

NEXT: CMP  CX , 5

JB  L1

END_DO_WHILE:

CMP  CX , 0

JE  L2

CLC

JMP  DONE

L2:  PUSH  DS

MOV  AX , CS

MOV  DS , AX

MOV  AH , 09H

LEA  DX , NO_VALUE_MSG

INT  21H

POP  DS

STC

JMP  DONE

OVERFLOW:

PUSH  DS

MOV  AX , CS

MOV  DS , AX

MOV  AH , 09H

LEA  DX , OVERFLOW_MSG

INT  21H

POP  DS

STC

DONE: RET

OVERFLOW_MSG  DB  0DH, 0AH, 'ERROR - UNSIGNED OVERFLOW','$'

NO_VALUE_MSG  DB  0DH, 0AH, 'ERROR - NO VALUE OR NO VALID VALUE ENTERED','$'

READ_UNSIGNED_DECIMAL16  ENDP

- Signed Decimal Input

Write a procedure to read a signed 16-bit decimal number in the BX register. The procedure should set the Carry Flag if there is overflow or if no value is entered. For an invalid input the procedure should beep and give the user the chance of entering another value.

Assuming:

- the signed number to be read is preceded by a +ve or -ve sign,

- no invalid input,

- the minimum 16-bit, signed value, i.e., -32768, is not read,

the pseudo-code algorithm is:

count  :=  0 ;

sum  :=  0 ;

negative  :=  0 ;

Read: ch ;

if( ch   =  '-' )then

negative  :=  1 ;

endif ;

do

{

Read: ch ;

if( ch  =  0DH)then

break ;

endif ;

ch  :=  ch  -  30H  ;

sum  :=  10  *  sum  ;

sum  :=  sum  +  ch  ;

count  :=  count  +  1  ;

}while( count  (  5 ) ;

if( negative  =  1)then

sum  =  -sum ;

endif ;

STOP ;

The above algorithm cannot be used to read the value -32768; because the line:

sum  :=  sum  +  ch ;

in the algorithm, will translate to:

sum  :=  32760  +  8

This addition causes signed addition overflow, because the maximum 16-bit, signed value is 32767. To take care of this special case, the algorithm is modified as shown in the next page:

count  :=  0 ;

sum1 :=  0 ;

sum2  :=  0 ;

negative  :=  0 ;

Read: ch ;

if( ch   =  '-' )then

negative  :=  1 ;

endif ;

do

{

Read: ch ;

if( ch  =  0DH)then

break ;

endif ;

ch  :=  ch  -  30H  ;

sum1  :=  10  *  sum2  ;

if( (sum1  =  32760)  and  (ch  =  8)  and  (negative  =  1))then

{

sum2  :=  (-32760)  +  (-8) ;

goto  done ;

}

endif ;

sum2  :=  sum1  +  ch  ;

count  :=  count  +  1  ;

}while( count  (  5 ) ;

if( negative  =  1)then

sum2  =  -sum2 ;

endif ;

done:

STOP ;

Refining the previous algorithm to incorporate input validity checking and to take care of the fact that a positive value may be entered without being preceded by a positive sign we have:

count  :=  0 ;

sum1  :=  0 ;

sum2  :=  0 ;

negative  :=  0 ;			assume the value to be read is not negative

Read: ch ;

if( ch  =  '-' )then

{

negative  :=  1 ;

Read: ch  ;

}

else if( ch  =  '+' )then

Read:  ch ;

endif  ;

while( ch  (  0DH)do

{

if( ch  (  '0'  and  ch  (  '9' )then

{

count  :=  count  +  1  ;

ch  :=  ch  -  30H  ;

sum1  :=  10  *  sum2  ;

if( SignedMultiplicationOverflow )then

goto  errorLabel ;

endif  ;

if( (sum1  =  32760)  and  (ch  =  8)  and  (negative  = 1) )then

{ sum2  =  -sum1  +  -ch ;

CLC ;

goto  done ;

}  ;

sum2  :=  sum1  +  ch  ;

if( SignedAdditionOverflow )then

goto  errorLabel  ;

endif  ;

}

else

{

Beep  ;

Move the cursor back ;

}

endif  ;

if( count  =  5)then

goto  exit ;

endif ;

Read: ch ;

}

endwhile ;

exit:		if( count  =  0 )then

Display: “ERROR – NO VALUE OR NO VALID VALUE ENTERED”

STC				; set Carry flag  (No input)

else

if( negative  =  1)then

sum2  =  -sum2 ;

endif ;

CLC				; clear Carry flag

endif

goto  done ;

errorLabel:	Display: “ERROR - SIGNED OVERFLOW”

STC  ;

done:	STOP ;

The previous algorithm is translated into the following procedure:

READ_SIGNED_DECIMAL16  PROC uses AX  CX  DX  SI

comment @

Reads a signed decimal number in the range -32768 to +32757 in BX. The procedure rejects invalid input by beeping and backspacing the cursor. If there is signed overflow or if no value or no valid value is entered before the enter key is pressed, an appropriate error message is displayed and the Carry flag is set.

@

MOV  BX , 0

MOV  SI , 0

MOV  CL , 0

MOV  AH , 01H

INT  21H

CMP  AL , '-'

JE  MINUS

CMP  AL , '+'

JE  PLUS

JMP  L1

MINUS:

MOV  CL , 1

PLUS:

MOV  AH , 01H

INT  21H

L1:	CMP  AL , 0DH

JE  EXIT

CMP  AL , '0'

JB  INVALID

CMP  AL , '9'

JA  INVALID

INC  SI

SUB  AL , 30H

MOV  AH , 0

PUSH  AX

MOV  AX , 10

IMUL  BX

POP  BX

JO  OVERFLOW

CMP  AX , 32760

JE  L2

JMP  L3

L2:  CMP  BL , 8

JNE  L3

CMP  CL , 0

JE  L3

NEG  AX

NEG  BX

ADD  BX , AX

CLC

JMP  DONE

L3:	ADD  BX , AX

JO  OVERFLOW

JMP  NEXT

INVALID: MOV  AH , 02H			; beep

MOV  DL , 07H			;

INT  21H			;

MOV  DL , 08H			; backspace

INT  21H			;

NEXT: CMP  SI , 5

JE  EXIT

MOV  AH , 01H

INT  21H

JMP  L1

EXIT:

CMP  SI , 0

JE NO_VALUE_ENTERED

JA  L4

STC

JMP  DONE

L4:	CMP  CL , 1

JE  L5

CLC

JMP  DONE

L5:	NEG  BX

CLC

JMP  DONE

OVERFLOW:

PUSH DS

MOV  DX , CS

MOV  DS , DX

MOV  AH , 09H

LEA  DX , OVERFLOW_MSG

INT  21H

POP  DS

STC

JMP DONE

NO_VALUE_ENTERED:

PUSH DS

MOV  DX , CS

MOV  DS , DX

MOV  AH , 09H

LEA  DX , NO_VALUE_MSG

INT  21H

POP  DS

STC

DONE:

RET

OVERFLOW_MSG  DB  0DH, 0AH, 'ERROR - SIGNED OVERFLOW','$'

NO_VALUE_MSG  DB  0DH, 0AH, 'ERROR - NO VALUE OR NO VALID VALUE ENTERED','$'

READ_SIGNED_DECIMAL16  ENDP