King Fahd University of Petroleum & Minerals

# CIVIL ENGINEERING DEPARTMENT

## CE 415

First Major Exam

October, 2004

First Semester 2004-2005 (041)

Student Name: _______________________________

Student I.D.: _______________

Grade: ____________

# Instructor:  Dr. Ahmad S. Al-Gahtani

Question (1):

The flooring system shown below supports a 70 psf service live load and 25 psf service dead load.  The beams are 10"×18" in the short direction and 12"×20" in the long direction.  The slab thickness is 5".  For this system:

1-	Check the limitation of the Direct Design Method.

2-	Check the minimum slab thickness for deflection control of panel (1).

3-	Verify ( value for the edge beam in short direction [Beam (A)].

4-	Estimate the torsional rigidity of the edge beam in the short direction (Bt =    ?).  [Beam (A)].

(’s for the beams are shown and fc( = 4000 psi, fy = 40000 psi.

Question (2):

For the two-way flooring system, shown in the figure, all beams are 16"×28" and the slab thickness is 6".  The floor supports 120 psf service live load and 60 psf service dead load.  For the interior frame A determine:

1-	The moment at critical sections (positive & negative).

2-	Distribute the max. negative moment to column strip and middle strip.

3-	Distribute the column strip to beam and slab components.

4-	Tabulate your solution. (fc( = 4000 psi, fy = 60,000 psi)

Question (3):

(a)	For the drop panel shown, check its conformity with the code requirements.

(b)	For the flat plate shown, compute the torsional constant C in both direction.