Lecture No. 16

Subject:  Force and Couple Systems

Objectives of Lecture:

- To explain how a force acting at a point on a body may be replaced by an equivalent system, consisting of the force at another point on the body and a couple moment applied at any point on the body

- To explain how to determine resultants of a force and couple system

  - Equivalent System

Fat a point A = [Fat a point O and

Couple Moment, Mat any point]

Note:

Mat any point, because the couple moment is a free vector and its effect is same at any point on the body.

Case-I: When point O is on the line of action of F acting at point A (Fig.16.1)

### Fig.16.1

The above is in agreement of the “Principle of Transmissibility of a Force”

Case-II: When point O is not on the line of action of F acting at point A (Fig.16.2)

# Fig. 16.2

  - Resultants of a Force and Couple System

FR and MRO (Fig.16.3)

# Fig. 16.3

FR =F1 +F2 			     (acting at point O)

MRO = M1 + M2 +MC  (may act at any point)

In general,

i) In vector form

FR = ΣF

MRO = ΣMO + ΣMC

ii) In scalar form

FR = [ FRx + FRy]0.5

Where

FRx = ΣFx, FRy = ΣFy

MRO = ΣMO + ΣMC

Examples of FR and MR

Numerical Examples

- Try the solved examples from Book

(Examples 4 –14 to 4 –15, page 164 to 165)

- Unsolved Examples

4-99

Replace the force at A by an equivalent resultant force and a couple moment at P (Fig.4-99)

Fig. 4-99

4-105

Replace the force and couple system by an equivalent force and couple moment acting at point P (Fig. 4-105).

Fig. 4-105

4-109

Replace the force and couple moment by an equivalent resultant force and specify its coordinate point of application (0, y) on the y-axis (Fig.4-109)

# Fig. 4-109

4-113

Replace the two forces by an equivalent resultant force and couple moment at point O. Set F = 15-lb (Fig. 4-113).

# Fig. 4-113